Documentation of THE SAPRC-22 Mechanism

Report to California Air Resources Board Contract No. 21AQP011

William P. L. Carter

September 9, 2023

College of Engineering Center for Environmental Research and Technology (CE-CERT)

University of California, Riverside, California 92521

Summary

This document describes an updated version of the SAPRC gas-phase mechanisms, designated SAPRC-22. This employs a similar base mechanism and lumping approach for organic compounds as used in SAPRC-16 and 18, but uses the more computationally efficient method to represent reactions of peroxy radicals that requires many fewer species and reactions, resulting in a mechanism closer in size to the widely-used SAPRC-07 mechanism. As with previous SAPRC mechanisms, the reactions of almost all of the organics were derived using the SAPRC mechanism generation system (MechGen), which has been recently been updated and documented. SAPRC-22 incorporates some potentially significant updates to the organic chemistry, which the underlying chemistry incorporated in MechGen now being documented in a separate paper that is being submitted for publication. As with previous SAPRC versions, SAPRC-22 was evaluated by comparing its predictions of O3 formation and NO oxidation rates against a large body of chamber experiments, and its performance was comparable to that of previous versions, despite less compound-by-compound adjustment of uncertain mechanism parameters. It is concluded that SAPRC-22 is an appropriate replacement to SAPRC-07, with more updated chemistry, more tracking of toxic species, and comparable size and computer demands.

This report describes the general features of SAPRC-22 and how it was developed using the mechanism generation system. All the reactions and species in the base mechanism are documented and the generated mechanisms are summarized in the body of this report, and an electronic supplement contains complete mechanism listings and other large tables, and also files useful for mechanism implementation and duplicating the calculations discussed in this report. Additional information and the files needed to implement the mechanism are available at https://intra.cert.ucr.edu/~carter/SAPRC/22.

Contents

1.	Introduction	1

2.	Mechanism Description	3

2.1.	Mechanism Size and Comparison with Recent SAPRC Mechanisms	3

2.2.	Mechanism Listings	4

2.3.	Base Mechanism and Rate Constant Changes	8

2.4.	Use of the SAPRC Mechanism Generation System	8

2.4.1.	Mechanism Generation Process	10

2.4.2.	Peroxy Radical Representation Methods	14

2.4.3.	Generated Mechanisms for Lumped Model Species	20

2.5.	Emissions Assignments	22

3.	Test Calculations	23

3.1.	Ambient Model Scenarios and Calculations	23

3.1.1.	Scenario Inputs	23

3.1.2.	Mechanism Comparison Results	25

3.2.	Standard Conditions used for Mechanism Preparation and Analysis	25

3.3.	Evaluation Against Chamber Data	31

3.4.	Mechanism Implementation Test Calculation	33

4.	Discussion	33

5.	Supplementary Information Available	35

6.	Acknowledgements	37

7.	References	37

8.	Mechanism Listing tables	41

List of Tables

Table 1.	Summary of mechanism sizes and related information for various versions of lumped SAPRC mechanisms for airshed models	4

Table 2.	List of reactive organic compounds that are represented explicitly in various versions of lumped SAPRC mechanisms for airshed models.	5

Table 3.	List of lumped model species used in various representative SAPRC mechanisms.	6

Table 4.	Reactions in the base mechanism whose rate constants changed by 10% or more.	9

Table 5.	Summary of types of reactions supported by the SAPRC mechanism generation system.	11

Table 6.	Illustration of reaction lumping using the reaction of n-butane with OH as an example	16

Table 7.	Illustration of reaction lumping using portions of the reactions of 1,3-butadiene with OH radicals as an example.	17

Table 8.	Summary of inputs for the box model simulations of multi-day, urban pollution scenarios used in this work.	24

Table 9.	Concentrations of species and parameters used to define the standard sets of environmental conditions used in this work .	29

Table 10.	Relative amounts that peroxy radicals undergo their various possible bimolecular reactions in the four sets of environmental conditions used in this work.	31

Table 11.	Supplementary information needed for mechanism documentation and implementation, and links to other relevant data and software that is available online.	36

Table A-1.	List of model species in the SAPRC-22 mechanisms.	42

Table A-2.	List of reactions and documentation notes in the standard SAPRC-22 mechanisms.	50

List of Figures

Figure 1.	Comparison of yields of isoprene products whose predicted yields are highly dependent on absolute NO levels derived revised SAPRC-07 approach with varying EffNO levels against those calculated using the hybrid approach used for the standard mechanism with varying NO levels.	20

Figure 2.	Plots of model simulations of selected species in the 2nd and 3rd day of the multi-day ambient simulations using various versions of SAPRC-22 developed in this work.	26

Figure 3.	Plots of model simulations of organic product species that appeared to be most sensitive to differences in SAPRC-22 lumping approaches on the 2nd and 3rd day of the multi-day ambient simulations using various versions of SAPRC-22..	27

Figure 4.	Comparisons of predictions of using SAPRC-07 through SAPRC-22 for selected species in the 2nd and 3rd day of the multi-day ambient simulations.	28

Figure 5.	Plots of fractions of the various types of bimolecular reactions of peroxy radicals against time for the scenarios used to derive standard conditions, showing the time periods where concentrations were averaged to yield the standard concentrations given on Table 9.	30

Figure 6.	Comparisons of average biases in the simulations of rates of NO oxidation and maximum O3 concentrations in the evaluations of versions of SAPRC-22 and earlier SAPRC mechanisms against NOx - air chamber experiments with all the compounds and mixtures used for SAPRC mechanism evaluations..	32

Figure 7.	Concentration-time plots of selected species in the test simulation provided to verify correct implementation of SAPRC-18 in airshed model software.	33

List of Supplementary Tables

Table B-1.	List of model species in the standard SAPRC-22 mechanism

Table B-2.	List of reactions and kinetic parameters in the standard SAPRC-22 mechanism

Table B-3.	Absorption cross sections and quantum yields for the photolysis reactions

Table B-4.	List of SAPRC detailed model species and assignments to SAPRC-22 model species

Table B-5.	Mixtures or compounds used to derive mechanisms of the lumped organic model species.

Table B-6.	Composition of the California 2018 anthropogenic emissions mixture used to derive mixtures to derive mechanisms of lumped model species representing emitted organics

Table B-7.	Composition of the California 2018 biogenic emissions mixture used to derive mixtures to derive mechanisms of lumped model species representing emitted organics

Table B-8.	Input conditions for implementation test calculation using SAPRC box model software. These were used as inputs for the test calculations shown on Table B-9.

Table B-9.	Output concentrations of test calculations using the standard SAPRC-22 mechanism

# Introduction

The SAPRC series of mechanism are designed for use in airshed models to predict the effects of reactions of emitted volatile organic compounds (VOCs) in the presence of NOx to form O3 and other secondary pollutants, including toxic organic products and precursors to particle formation. The most widely used of these has been the SAPRC-07 (Carter et al, 2010a,b; Hutzell et al, 2010), which was implemented in a number of airshed models, though it has been subsequently updated as discussed above. The versions for airshed models are similar in objective and approach (though somewhat larger in size in some cases) to the RADM/RACM (Stockwell et al, 1990, 1997, 2006, Goliff et al, 2013) or Carbon Bond (Gery et al, 1988, Yarwood et al, 2005, 2010, Sarwar et al, 2008) series of mechanisms that are also widely used in airshed models, which use a limited number of model species to represent the reactions of the many emitted organic compounds and their reaction products, and uses the steady state assumptions and other approximations to reduce the number of model species needed to represent reactions of intermediate radicals. More detailed versions of SAPRC mechanisms represent the major emitted organics explicitly, but use the same lumped model species to represent reactions of their oxidized products. These detailed versions are used for calculation of MIR and other ozone reactivity scales for organic compounds (Carter, 1994, 2010a-c), and for evaluating the mechanisms using environmental chamber data, but are generally not used in other modeling applications.

The widely-used SAPRC-07 mechanism was updated in 2011 to SAPRC-11 to improve its ability to simulate results of environmental chamber experiments with aromatics (Carter and Heo, 2012, 2013), and then it underwent a complete update in 2016-2020 to the SAPRC-16 through SAPRC-18 mechanisms (Carter, 2015, Venecek et al, 2018, Carter, 2020a). The update of SAPRC-07 to SAPRC-11 was an incremental update that focused mainly on aromatics, while the update to SAPRC-16 was a major update to all portions of the mechanism, using a larger number of model species to better represent precursors to secondary organic aerosol (SOA) formation, and to using a more accurate method to represent peroxy radical reactions, which required use of a much larger number of model species to represent reactions of peroxy radicals than the previous mechanisms. This more accurate peroxy radical representation was considered necessary in order for the model to represent effects of unimolecular, "auto-oxidation" reactions of peroxy radicals, which were not previously recognized to be important, and which was not readily compatible with the way previous versions of SAPRC represented effects of peroxy radical reactions, which relied on the assumption that reactions with NO and (to a lesser extent) other bimolecular reactions were their major fate.

Unfortunately, the modeling community has been hesitant to incorporate SAPRC-16 or 18 because of their large size, which may not be necessary for most regulatory models. Although the more accurate peroxy radical representation method is better suited to mechanisms where there are competitions between unimolecular and bimolecular peroxy reactions, the use of the large number of model species and reactions it requires may not be necessary for the purposes of many if not most modeling applications. This may not be necessary for models used primarily for ozone predictions, or predictions of most of the known toxic gas-phase species of current interest. This complexity and increased accuracy in representing auto-oxidation reaction may be necessary for accurate SOA modeling, but only if the SOA module in the model incorporates the complete gas-phase chemistry. Current regulatory models use separate SOA modules that take only limited input from the gas-phase mechanism, so they do not benefit with the greater complexity and accuracy of SAPRC-16 and later versions.

Another problem with the latest versions of the SAPRC mechanisms is that the SAPRC mechanism generation system, MechGen (Carter, 2023a,b), which is used to derive mechanisms for almost all organic compounds the recent SAPRC mechanisms, has been has been continuously evolving as it is being developed. Because of this, both SAPRC-16 and 18 became out-of-date shortly after they were developed. In addition, MechGen have not been comprehensively documented or discussed in the peer-reviewed literature, which means that the mechanisms that depend on it are also inadequately documented. The reliance of SAPRC mechanisms on MechGen follows the approach outlined by Kaduwela et al (2015) for mechanism development, involving use of detailed mechanisms and mechanism generation system to serve as the bridge between fundamental science and mechanisms for airshed models. However, MechGen needs to be more stable and better documented if it is to serve as the scientific basis for chemical mechanisms used in modeling.

Because of these considerations, it was decided in early 2022 to pause the continued development of updates for of MechGen until all its existing components can be documented for publication and peer review, and therefore provide a stable basis and citable reference for updated versions of the SAPRC mechanism and other scientific applications. This documentation effort took place during second half of 2022 and a draft manuscript and supplementary section containing details has been prepared and is now under internal review prior to submission to publication in early 2023 (Carter, 2023c). This documentation process required re-examining all the many components, and some revisions to MechGen were found to be necessary, which rendered portions of SAPRC-18 out of date. Most recently, in mid-2023 it was found necessary to completely update the methods to estimate rate constant for peroxy radical isomerization reactions, with the results indicating that such isomerizations are even more widespread than estimated when SAPRC-18 was developed. This required further updates to MechGen and its documentation. However, now this documentation effort is now sufficiently complete to serve as the basis for more stable and documented updated SAPRC mechanisms.

This report presents and describes the newly-developed SAPRC-22 mechanism, which is an update to SAPRC-18, and which was derived from the newly updated and documented version of MechGen (Carter, 2023a-c). This can be thought of as an incremental update to SAPRC-18, with several additional explicit species added. Several versions were examined, all being based on the same detailed mechanisms and having similar levels of chemical detail in terms of lumping organic compounds as SAPRC-18, but differing in the method used to represent peroxy radical reactions. The most detailed "full" version employs a more detailed and accurate method for representing peroxy radical reactions similar to that incorporated in SAPRC-18, now requires far too many intermediate species to be practical for regulatory modeling. The most condensed version examined used the "chemical operator" approach to represent peroxy radical reactions, which is comparable to that used in SAPRC-07 and 11. This requires far fewer species and reactions to represent the reactions of peroxy radicals in the models, and should satisfy the need for an updated version of SAPRC without excessive requirements for computer resources. Unfortunately, because of the peroxy isomerization reactions, it is strictly only valid for an assumed "effective NO" concentration, what must be specified when the mechanism is derived. The version that was adopted for SAPRC-22 was a modification of the most condensed version where a single intermediate was added to the representation of VOC reactions to account for the effects of absolute NO levels on predictions of product yields. This was found to give predictions that are sufficiently close to the full version, to be suitable for regulatory modeling, while not requiring significantly more computer resources than SAPRC-07.

This report gives a description of the new mechanism and how it was derived using the mechanism generation system, describes box model simulations used to develop and evaluate the mechanism, and other information needed to implement the mechanism in airshed models. It includes an electronic supplement consisting of an Excel file containing the large tables, complete mechanism listings, and input and output data to implementation test simulations, and also text files for use in implementing the mechanism using SAPRC and other modeling software systems.

It should be emphasized that, as with previous versions, SAPRC-22 is designed primarily for predictions of gas-phase species. Halogen chemistry was included in SAPRC-07 but has not yet been incorporated into SAPRC-16 through 22 because this was beyond the scope the more recent SAPRC updates. SOA prediction is also beyond the scope of this project, even though SAPRC-22 includes most of the lumped model species added to SAPRC-16 and 18 to improve representation of SOA precursors. Additional work is needed before gas-phase mechanisms such as SAPRC can be directly used to reliably predict formation of condensable species based on detailed chemistry, which may require far more chemical detail than is practical for regulatory models. In the meantime, continued use of separate SOA modules linked to the output of the gas-phase mechanism is still required for SOA predictions.

# Mechanism Description

## Mechanism Size and Comparison with Recent SAPRC Mechanisms

Table 1 gives a summary of the numbers of species and reactions recent SAPRC mechanisms, including the two versions of SAPRC-22 developed in this work. The number of model species used for emitted and product species, and the compounds represented explicitly, varies with the version of the mechanism, tending to increase as the mechanism is updated through SAPRC-18 to take into account increased chemical knowledge and the desire to track more toxic species in airshed model calculations. Another factor in affecting the sizes of these mechanisms in models is the method used to represent the effects of peroxy radical reactions, which are also indicated on the table and discussed further below. Note that the two versions of SAPRC-22 shown on the table differ only how peroxy radical reactions are represented, with both versions using the same model species for stable compounds. The different methods used to represent peroxy radical reactions are discussed later in Section 2.4.2.

The numbers of model species used to represent emitted and oxidized product organic compounds also affects the size of the mechanism, and increased from SAPRC-99 through SAPRC-18 and then declined somewhat for SAPRC-22. The individual emitted and product compounds represented explicitly in the recent and current versions of SAPRC are listed in Table 2, and the model species used for the other compounds are listed in Table 3. The numbers of explicit and lumped model species has increased with each version through SAPRC-18 in order to more accurately represent the mechanisms of the wide range of organic compounds that react in the atmosphere. The numbers of explicitly represented emitted compounds increased for the "toxics" version of SAPRC-07 at the request of the EPA so more compounds of regulatory interest can be tracked, and it was increased further for SAPRC-22 for the same reason at the request of the CARB modelers. SAPRC-18 also uses the approach of representing individual emitted compounds that are particularly important in emissions explicitly. In addition to allowing these important compounds to be tracked and be more accurately represented in model simulations, it also allows the (usually) higher molecular weight compounds that would otherwise be lumped with them to be represented with model species that better represents their mechanisms. Another factor in affecting the sizes of these mechanisms in models is the method used to represent the effects of peroxy radical reactions, which are also indicated on the table and discussed further below. These characteristics are discussed further below.

The numbers of model species used to represent emitted and oxidized product organic compounds also affects the size of the mechanism, and increased from SAPRC-99 through SAPRC-18 and then stayed about the same for SAPRC-22. The individual emitted and product compounds represented explicitly in the recent and current versions of SAPRC are listed in Table 2, and the model species used for the other compounds are listed in Table 3. The numbers of explicit and lumped model species has increased with each version through SAPRC-18, in order to more accurately represent the mechanisms of the wide range of organic compounds that react in the atmosphere. The numbers of explicitly represented emitted compounds increased for the "toxics" version of SAPRC-07 at the request of the EPA so more compounds of regulatory interest can be tracked, and it was increased further for

Table 1.	Summary of mechanism sizes and related information for various versions of lumped SAPRC mechanisms for airshed models

| Mechanism Version [a] | SAPRC-99 | SAPRC-07 (in CMAQ) | SAPRC-18 | SAPRC-22 (full) | SAPRC-22 (reduced) | SAPRC-22 (standard) |
| --- | --- | --- | --- | --- | --- | --- |
| Model Species | 82 | 126 | 516 | 1143 | 210 | 260 |
| Inorgancs | 22 | 23 | 22 | 19 | 19 | 19 |
| Explicit organics |  |  |  |  |  |  |
| Primarily emitted | 3 | 13 | 21 | 30 | 30 | 30 |
| Primarily products | 9 | 10 | 24 | 16 | 16 | 16 |
| Lumped organics |  |  |  |  |  |  |
| Primarily emitted | 10 | 13 | 32 | 23 | 23 | 23 |
| Primarily products | 26 | 26 | 42 | 40 | 40 | 40 |
| Intermediates [b] | 12 | 41 | 375 | 1015 | 82 | 132 |
| Reactions | 211 | 569 [b] | 1772 | 5750 | 647 | 747 |
| Peroxy method [c] | SAPRC-99 | SAPRC-07 | SAPRC-16 | SAPRC-16 | SAPRC-07 (revised) | Hybrid |

[a]	Information for versions prior to SAPRC-22 are applicable to versions available online at the SAPRC mechanism web site (Carter, 2019b).

[b]	Includes inorganic intermediates such as O3P and O1D, peroxy radical operators, explicit peroxy radicals, and other intermediates where use of the steady state approximation is recommended.

[c]	Method used to represent peroxy reactions. See text.

SAPRC-22 for the same reason at the request of the CARB modelers. SAPRC-18 also uses the approach of representing individual emitted compounds that are particularly important in emissions explicitly. In addition to allowing these important compounds to be tracked and be more accurately represented in model simulations, it also allows the (usually) higher molecular weight compounds that would otherwise be lumped with them to be represented with model species that better represents their mechanisms.

## Mechanism Listings

Table A-1 and Table A-2 give listings of the model species and reactions in the SAPRC-22 mechanism. These are given at the end of this report because of their size. Footnotes to Table A-1 describe the model species and what they represent, and footnotes to Table A-2 document the rate constants used the base mechanism and other aspects of the reaction as applicable. The derivations of rate constants and mechanisms for the MechGen-derived reactions are described elsewhere (Carter, 2023c), so are not discussed here. Because of their size, these tables are also abbreviated in some respects, with not all of the peroxy operators shown on Table A-1 and not all of the products are shown on Table A-2 for the MechGen-derived reactions. Complete listings of the model species and products of all reactions are given in Table B-1 and Table B-2 in the electronic supplement (see Section 5). Complete mechanism listings can also be obtained from files implementing the mechanism,, which are available at https://intra.engr.ucr.edu/~carter/SAPRC/22/.

Table 2.	List of reactive organic compounds that are represented explicitly in various versions of lumped SAPRC mechanisms for airshed models.

| Compound (primarily emitted) | Explicit in [a] |  | Compound (primarily product) | Explicit in [a] |
| --- | --- | --- | --- | --- |
|  | 99 | 07T | 18 | 22 |  |  | 99 | 07T | 18 | 22 |
| Explicit in all versions |  | Explicit in all versions |
| Methane | X | X | X | X |  | Formaldehyde | X | X | X | X |
| Ethylene | X | X | X | X |  | Methanol | X | X | X | X |
| Isoprene | X | X | X | X |  | Formic Acid | X | X | X | X |
|  |  |  |  |  |  | Glyoxal | X | X | X | X |
| Added for "Toxics" version of SAPRC-07 |  | Acetaldehyde | X | X | X | X |
| Propene |  | X | X | X |  | Peroxyacetyl nitrate | X | X | X | X |
| 1,3-Butadiene |  | X | X | X |  | Acetone | X | X | X | X |
| (-Pinene |  | X | X | X |  |  |  |  |  |  |
| Acetylene |  | X | X | X |  |  |  |  |  |  |
| Benzene |  | X | X | X |  | Explicit in most versions |
| Toluene |  | X | X | X |  | Methyl Hydroperoxide | X |  | X | X |
| m-Xylene |  | X | X | X |  | Acetic acid | X | X | X |  |
| o-Xylene |  | X | X | X |  |  |  |  |  |  |
| p-Xylene |  | X | X | X |  |  |  |  |  |  |
| 1,2,4-Trimethyl Benzene |  | X | X | X |  | Added for SAPRC-07T |
|  |  |  |  |  |  | Ethanol |  | X | X | X |
| Added for SAPRC-16/18 |  | Glycolaldehyde |  | X | X | X |
| Ethyl Benzene |  |  | X | X |  |  |  |  |  |  |
| Ethane |  |  | X | X |  |  |  |  |  |  |
| Propane |  |  | X | X |  | Added for SAPRC-16/18 but not kept for 22 |
| n-Butane |  |  | X | X |  | Glycolaldehyde's PAN |  |  | X |  |
| (-Pinene |  |  | X | X |  | Peroxy acetic acid |  |  | X |  |
| d-Limonene |  |  | X |  |  | Ethyl hydroperoxide |  |  | X |  |
| 1,2,3-Trimethyl Benzene |  |  | X | X |  | Peroxy propionyl nitrate |  |  | X |  |
| 1,2,4-Trimethyl Benzene |  | X | X | X |  |  |  |  |  |  |
| 1,3,5-Trimethyl Benzene |  |  | X | X |  |  |  |  |  |  |
| Added for SAPRC-22 |  | Added for SAPRC-16/18 and kept for 22 |
| Methyl t-Butyl Ether |  |  |  | X |  | Propionaldehyde |  |  | X | X |
| Vinyl chloride |  |  |  | X |  | Acrolein |  |  | X | X |
| Acrylonitrile |  |  |  | X |  | Methyl ethyl ketone | [b] | [b] | X | X |
| Perchloroethylene |  |  |  | X |  | Methacrolein | [b] | [b] | X | X |
| p-dichlorobenzene |  |  |  | X |  | Methyl Vinyl Ketone | [b] | [b] | X | X |
| Methylene chloride |  |  |  | X |  | 2-Butene-1,4-dial |  |  | X | X |
| Ethylene dibromide |  |  |  | X |  | Maleic anhydride |  |  | X | X |
| Ethylene dichloride |  |  |  | X |  | Phenol |  |  | X | X |
| Ethylene oxide |  |  |  | X |  |  |  |  |  |  |

[a]	"X" indicates that the compound is explicit in the SAPRC-99, SAPRC-07T, SAPRC-18 or SAPRC-22 mechanisms. Blank indicates it is represented using a lumped model species that is also used for other similar compounds.

[b]	Methyl ethyl ketone (MEK), methacrolein (METHACRO or MACR) or methyl vinyl ketone (MVK) model species are used to represent chemically similar compounds that are lumped with them.

Table 3.	List of lumped model species used in various representative SAPRC mechanisms.

| Lumped Model Species | Description |
| --- | --- |
| SAPRC-99 | SAPRC-07T | SAPRC-18 | SAPRC-22 |  |
| Alkanes and other saturated compounds that react only with OH |
| ALK1 | ALK1 | ALK3 | ALK1 | Used for saturated compounds that react only OH radicals. Assigned based on the OH rate constant, alkane status (for SAPRC-18) and molecule size (for SAPRC-22). Primarily used for alkanes, alcohols, and ethers. (The approach used for SAPRC-22 is based on that for SAPRC-07, except ALK6 is used for those with 12 or more carbons + oxygens. |
| ALK2 | ALK2 | ALK4 | ALK2 |  |
| ALK3 | ALK3 | ALK5 | ALK3 |  |
| ALK4 | ALK4 | OTH1 | ALK4 |  |
| ALK5 | ALK5 | OTH2 | ALK5 |  |
|  |  | OTH3 | ALK6 |  |
|  |  | OTH4 |  |  |
| Alkenes and other non-photoreactive, non-aromatic compounds with C=C bonds |
| OLE1 | OLE1 | OLE1 | OLE1 | Alkenes |
| OLE2 | OLE2 | OLE2 | OLE2 | (kOH and/or number of substituents around the double bond used to determine model species) |
|  |  | OLE3 | OLE3 |  |
|  |  | OLE4 | OLE4 |  |
|  |  | OLEC | [a] | Cycloalkenes |
|  |  | OLED | [a] | Dialkenes |
| TERP | TERP | TERP | TERP | Terpenes |
|  | SESQ | SESQ | SESQ | Sesquiterpenes |
|  |  | OLEP | OLEP | Non-photoreactive oxygenated alkenes |
| Acetylenes |
|  |  | ACYLS | [b] | C3+ Acetylenes |
| Aromatics and furans |
|  |  | BENX | BENX | Aromatic hydrocarbons |
| ARO1 | ARO1 | ARO1 | ARO1 | (kOH used to determine model species) |
| ARO2 | ARO2 | ARO2 | ARO2 |  |
|  |  | NAPS | NAPS | Naphthalenes |
|  |  | STYRS | STYRS | Styrenes |
|  |  | FURNS | FURNS | Furans |
| Reduced nitrogen compounds |
|  |  | AMINS | AMINS | Amines |
|  |  |  | TAMNS | Amines bonded to a tertiary carbon (inhibiting) |
|  |  | IMINE | IMINE | Imines |
|  |  | NAMIN | NAMIN | Nitramines |
| Aldehydes |
| RCHO | RCHO | RCHO | RCHO | Saturated aldehydes |
|  |  | RTCHO | [c] |  |
| ISO-PROD | IPRD | OLEA1 | OLEA1 | Unsaturated aldehydes |
|  |  | OLEA2 | OLEA2 |  |
| MGLY | MGLY | MGLY | MGLY | alpha-carbonyl aldehydes |
| BALD | BALD | BALD | BALD | Aromatic aldehydes |
| DCB1 | AFG1 | AFG1 | AFG1 | Photoreactive aromatic ring opening products |
| DCB2 | AFG2 | AFG2A | AFG2A |  |
|  |  | AFG2B | AFG2B |  |
| Ketones |
| MEK | MEK | KET2 | KET2 | Saturated ketones |
| PROD2 | PROD2 | LVKS | LVKS | Unsaturated ketones |
| BACL | BACL | BACL | BACL | alpha-diketones |
| DCB3 | AFG3 | AFG3 | AFG3 | Various non-photoreactive aromatic ring opening products |
| Organic acids |
| RCO-OH | RCOOH | RCOOH | OACID | Organic acids |
| RCO-OOH | RCO3H |  | PACID | Organic peroxy acids |
| Aromatic oxygenates and nitrates |
| CRES | CRES | CRES | CRES | Phenols and catechols |
|  |  | XYNL | XYNL |  |
|  |  | CATL | CATL |  |
| NPHE | NPHE | NPHE | NPHE | Nitrophenols |
|  |  | NAPPRD | NAPPRD | Unspecified products from naphthalenes |
| Organic nitrates |
| RNO3 | RNO3 | R1NO3 | R1NO3 | Saturated organic nitrates (kOH used to determine model species) |
|  |  | R2NO3 | R2NO3 |  |
|  |  | RCNO3 | RCNO3 | Carbonyl nitrates |
|  |  | RHNO3 | RHNO3 | Hydroxy nitrates |
|  |  | RANO3 | RANO3 | Organic nitrates formed primarily from aromatics |
|  |  | RPNO3 | RPNO3 | Organic nitrates with hydroperoxy groups |
|  |  | RDNO3 | RDNO3 | Organic dinitrates |
| PAN Analogues |
|  | PAN2 | PAN2 | PAN2 | Saturated PAN analogues |
|  | MA-PAN | MAPAN | APANS | Unsaturated PAN analogues |
|  | PBZN | PBZN | PBZN | Aromatic PAN analogues |
|  |  | PAN2N | [d] | PAN analogues with additional nitrate groups |
| Organic hydroperoxides |
| ROOH | ROOH | ROOH | ROOH | Hydroperoxides |
|  | R6OOH |  |  |  |
|  |  | RUOOH | RUOOH | Unsaturated organic hydroperoxides |
|  | RAOOH | RAOOH | RAOOH | Cyclic hydroperoxide with peroxy groups from aromatics |
|  |  | HPALD | HPCRB | Organic hydroperoxides with carbonyl groups |
|  |  | CROOH |  |  |
| Unreactive model species |
| NROG | NROG | NROG | NROG | Volatile unreactive |
|  |  | RNNO3 | RNNO3 | Non-volatile organic nitratrs |
|  |  | OTHN | OTHN | Other non-volatile products |

[a]	It was determined that there are insufficient amounts of emitted alkenes of this type to justify using separate model species for them. They are lumped with OLE2 or OLE4 depending on the number of substituents about the double bond(s).

[b]	There are insufficient amounts of higher acetylenes emitted to justify using separate model species for them. Because they react primarily with OH, they are represented by ALKx, depending on their OH rate constants.

[c]	RTCHO was used for C10+ aldehydes formed from primarily from terpenes primarily to aid SOA predictions. Lumping these with RCHO is sufficient for gas-phase predictions

[d]	The amount of such compounds predicted to be formed (primarily from NO3 + alkene reactions) was determined to be insufficient to justify having separate PAN and RCO3 model species for them.

## Base Mechanism and Rate Constant Changes

The base mechanism consists of the reactions of the inorganic species and the C1 organics that were derived manually based on a review of the literature and available evaluations. This portion of the mechanism as used in SAPRC-11 was essentially the same in SAPRC-07 but underwent a major update for SAPRC-16, with very little further changes for SAPRC-18 or SAPRC-22. Table 4 summarizes the reactions in the base mechanism where the rate constant changed by more than 10% relative to SAPRC-07 or where reactions were added or removed. Also shown are the reactions with larger changes in rate constants for explicitly represented organics and in photolysis rates for lumped photoreactive model species. Not shown are changes in rate constants or mechanisms for lumped species that were derived using MechGen, which reflect changes in estimation methods between the times that SAPRC-07 (Carter, 2000) and SAPRC-22 (Carter, 2023c) were developed. The portions of the mechanism derived using the mechanism generation system are discussed in the following section.

Although a majority of rate constants in the base or explicit mechanisms were not changed significantly, Table 4 shows that there were a number with relative changes greater than 10%, and several where the change was greater than a factor of 2. The largest changes were generally for photolysis reactions, particularly for some types of bifunctional species that are represented separately in SAPRC-22, but lumped with monofunctional compounds in SAPRC-07, are now assumed to photolyze much more rapidly (Carter, 2023c) and are represented by separate model species. There was also a large increase in the generic peroxy + HO2 rate constant that will affect NOx levels where these reactions become important. On the other hand, the large decreases in dicarbonyl + NO3 rate constants will have small effects on model predictions because these reactions are generally unimportant (except perhaps at nighttime), and the changes regarding phenoxy and phenyl peroxy radicals do not significantly impact predictions of the effects and products of reactions forming these radicals.

In general, the effects of the changes in rate constants and mechanism would depend significantly on the environmental conditions being simulated. The effects of these changes on several box model simulations are presented in Section Error! Reference source not found., but a comprehensive study of the effects of the changes under a variety of conditions will require 3D regional model calculations, which is beyond the scope of this report.

## Use of the SAPRC Mechanism Generation System

The SAPRC mechanism generation system (also called MechGen) is a computer program with various algorithms, tools, and assignments that can be used to derive fully explicit reaction schemes for organic compounds and intermediates in the atmosphere, and tools and assignments for using the explicit reactions to derive condensed SAPRC mechanisms. Previous versions were described in the documentation for the SAPRC-99 mechanism (Carter, 2000), with updates for SAPRC-07 (Carter, 2010a,b), SAPRC-16 (Carter, 2016), SAPRC-18 (Carter, 2020a) and this work. Complete documentation of the current capabilities of the software and the current basis of the chemical mechanistic assignments and estimates of the system is in preparation and will be available elsewhere (Carter, 2023b,c). In addition, information about the various estimates and assignments used when generating mechanisms can be obtained using the web based interface offered by MechGen (Carter, 2023a,b) The major types of reactions currently supported by the mechanism generation system are summarized on Table 5.

Although MechGen could be used to generate all the reactions of a selected compound and its oxidation products leading either to unreactive or nonvolatile compounds or CO or CO2, for SAPRC mechanism development it is used primarily to generate reactions leading to first generation products, with the subsequent reactions of the non-radical organic oxidation products not automatically being generated. Reactions of these product compounds are treated by separately, either by generating reactions

Table 4.	Reactions in the base mechanism whose rate constants changed by 10% or more.

| Reaction | Rate constant [a] |
| --- | --- |
|  | SAPRC-07 | SAPRC-22 | Change [b] |
| Base inorganic and C1 mechanism |
| HO2 + NO | [c] | 4.33e-14 |  |
| HO2 + NO + H2O | [c] | 2.35e-31 |  |
| N2O5 + H2O | 2.50e-22 | [d] |  |
| N2O5 + H2O + H2O | 1.80e-39 | [d] |  |
| MEO2 + HO2 = MEOOH + O2 | 4.72e-12 | 5.21e-12 | 10% |
| MEO2 + HO2 = HCHO + O2 + H2O | 4.69e-13 | 0 |  |
| HO2 + NO2 = HNO4 | 1.14e-12 | 7.50e-13 | -41% |
| HNO4 = HO2 + NO2 | 8.55e-2 | 6.20e-2 | -32% |
| OH + NO3 | 5.98e-12 | 4.86e-12 | -21% |
| HO2 + HO2 | 2.90e-12 | 2.54e-12 | -13% |
| HO2 + HO2 + H2O | 6.53e-30 | 5.71e-30 | -13% |
| HO2 + NO3 | 4.00e-12 | 3.50e-12 | -13% |
| O1D + M = O3P + M | 3.29e-11 | 3.69e-11 | 11% |
| HCHO + HV = H2 + CO | 5.20e-5 | 5.81e-5 | 11% |
| Organic radicals in base mechanism |
| BZO + NO2 = NPHE | 3.80e-11 | 2.08e-12 | fac 18.3 lower |
| BZO = other products (unimolecular) | 1.00e-3 | [e] |  |
| BZO + O3 = BZO2 | [c] | 2.86e-13 |  |
| BZO2 + NO, HO2, NO3, RO2, RCO3 | [f] | [g] |  |
| Generic RO2 + HO2 | 7.79e-12 | 1.49e-11 | fac 1.9 higher |
| Generic RCO3 + HO2 | 1.39e-11 | 2.20e-11 | 45% |
| TBUO = ACET + MEO2 | 9.87e+2 | 1.43e+3 | 36% |
| PAN analogues in base mechanism |
| MECO3 + NO2 = PAN | 9.46e-12 | 8.69e-12 | -8% |
| PAN = NO2 + MECO3 | 4.64e-4 | 3.82e-4 | -19% |
| R2CO3 + NO2 = PAN2 | 1.22e-11 | 7.70e-12 | -45% |
| PAN2 = NO2 + R2CO3 | 4.01e-4 | 3.39e-4 | -17% |
| BZCO3 + NO2 = PBZN | 1.37e-11 | 1.11e-11 | -21% |
| PBZN = BZCO3 + NO2 | 3.12e-4 | 3.18e-4 | 2% |
| Photolysis changes for explicitly represented organics |
| Methyl vinyl ketone + hv | 1.25e-6 | 5.32e-6 | fac 4.3 higher |
| Glyoxal + hv = HCHO + CO | 5.30e-5 | 2.76e-5 | fac 1.9 lower |
| PBZN + hv | 1.02e-6 | 1.91e-6 | fac 1.9 higher |
| Acrolein + hv | 2.95e-6 | 3.89e-6 | 28% |
| Acetaldehyde + hv | 6.93e-6 | 7.74e-6 | 11% |
| Photolysis changes for lumped organics |
| Nitrophenols + hv = HONO | 1.81e-5 | 1.81e-5 | 0% |
| Nitrophenols + hv = Other products | 1.81e-4 |  |  |
| Aromatic fragmentation product #1 + hv | 6.45e-3 | 1.42e-3 | fac 4.5 lower |
| Dinitrates + hv | 3.92e-6 | 1.17e-5 | fac 3.0 higher |
| Hydroperoxy carbonyls + hv | 2.34e-5 | 6.59e-5 | fac 2.8 higher |
| Carbonyl nitrates + hv | 2.34e-5 | 5.05e-5 | fac 2.2 higher |
| Lumped higher PANs + hv | 1.02e-6 | 1.91e-6 | fac 1.9 higher |
| Rate constant changes for explicitly represented VOCs |
| Methyl glyoxal + NO3 | 2.43e-15 | 5.00e-16 | fac 4.9 lower |
| Glyoxal + NO3 | 9.63e-16 | 4.00e-16 | fac 2.4 lower |
| p-Xylene + OH | 1.43e-11 | 1.21e-11 | -17% |
| a-Pinene + O3 | 8.44e-17 | 9.59e-17 | 13% |
| Methyl ethyl ketone + OH | 1.18e-12 | 1.05e-12 | -12% |

[a]	Rate constant units are in cm3 molec-1 s-1 or sec-1 units. Thermal rate constants are for 298K. Photolysis rate constants are for direct overhead sunlight (see Table 8 for the calculation method, and Table B-2 for a listing of all photolysis rate constants in SAPRC-22).

[b]	Factor increase or decrease if change is more than a factor of 2, or (SAPRC-22 - SAPRC-07) / Average, if the change is less than that.

[c]	These reactions were not considered when SAPRC-07 was developed.

[d]	Not included in the SAPRC-22 gas-phase mechanism since this is now considered to be a heterogeneous reaction.

[e]	The pseudo-unimolecular loss of phenoxy radicals was added to SAPRC-07 to avoid problems when both NO2 and HO2 are low. It is not needed for SAPRC-22 because of the addition of the phenoxy + O3 reaction, which was omitted from previous versions.

[f]	The phenyl peroxy radical is represented using chemical operators in SAPRC-07. This method could not be used in SAPRC-22 because of the inclusion of phenyl peroxy + O3 reaction means it cannot be treated like other peroxy radicals.

[g]	The same rate constants are used as used for other C2+ peroxy radicals.

for selected product compounds, or by representing them using lumped model species derived from generated reactions of representative compound, as discussed below.

### Mechanism Generation Process

The operations of the SAPRC mechanism generation system are described in more detail elsewhere (Carter, 2023b), but relevant features will be summarized here. For each initial reaction of the subject VOC or intermediate radical formed, the system first determines whether there any existing rate constant or mechanism assignments for the reactions, and uses them if available to generate the reaction. If no such assignments have been made (as is usually the case), the system generates the various possible reactions and uses various SARs or estimation methods to estimate the rate constants or branching ratios involved. In some cases there are many possible pathways, some of which may be negligible. The system does not generate reactions it determines to be negligible based on criteria discussed in the following paragraph. In the case of peroxy or acyl peroxy radicals, the system first determines whether it undergoes unimolecular reactions, with the subsequent processing depending on the magnitude of the total estimated unimolecular rate constant (kUni). Unimolecular reactions are treated as the only fate of the peroxy radical if kUni greater ~450 sec-1, are not generated if kUni is less than 2.25 x 10-3 sec-1, while both unimolecular and bimolecular of peroxy radicals are generated if kUni is between these levels

Table 5.	Summary of types of reactions supported by the SAPRC mechanism generation system.

| Reactant(s) | Type of reactions [a] |
| --- | --- |
| VOC + OH | H-atom abstraction |
|  | Addition to double bonds |
|  | Addition to aromatic rings. |
| VOC + O3 | Addition to double bonds followed by Criegee biradical formation. |
|  | Excited adduct addition to amines, followed by decomposition of adduct forming OH |
| VOC + NO3 | H-atom abstraction |
|  | Addition to double bonds |
| VOC + O3P | Addition to double bonds |
| VOC + h( | Breaking the weakest bond in saturated aldehydes, hydroperoxides, (-dicarbonyls, PAN compounds, and monofunctional organic nitrates |
|  | Breaking the weakest bonds in saturated ketones |
|  | Radical formation from (-unsaturated and (-carbonyl aldehydes |
|  | Radical formation or decompositions of other unsaturated carbonyls. |
|  | More rapid photolysis of carbonyl nitrates and dinitrates |
|  | Very rapid photolysis of carbonyl hydroperoxides |
| VOC Uni. | Thermal decompositions of peroxynitrates |
| Carbon-centered Radicals | Unimolecular decompositions of radicals with (-nitro, (-nitrato or (-peroxy groups |
|  | Reaction with O2 with H-abstraction from (-OH groups |
|  | Addition of O2 to radicals with allylic resonance |
|  | Reactions of O2 with aromatic - OH adducts |
|  | Addition of O2 to other alkyl radicals |
| Peroxy of Acyl peroxy Radicals | Reactions with NO forming the corresponding alkoxy radical or organic nitrate |
|  | Cyclization of aromatic OH-O2 adducts |
|  | Unimolecular H-shift reactions forming hydroperoxides |
|  | Reactions with NO2 forming the corresponding peroxynitrate or PAN |
|  | Reaction with HO2 forming the corresponding hydroperoxide or other products |
|  | Reaction with NO3 forming NO2 and the corresponding alkoxy radical |
|  | Reaction with other peroxy radicals forming the corresponding alkoxy radical, carbonyl compound, or alcohol, depending on whether the radical has an alpha hydrogen. |
| Alkoxy Radicals | (-H abstraction by O2 forming the corresponding carbonyl compound (-scission decompositions |
|  | H-shift isomerizations |
|  | Ester rearrangement |
| Crigiee intermediates | Decompositions, stabilization, or rearrangements of excited intermediates |
|  | Decompositions of stabilized intermediates or reactions with H2O |

[a]	See Carter (2023c) for a complete description of the types of reactions that may be generated and assignments and estimates made for them.

These peroxy kUni limits were assigned after examining various unimolecular vs bimolecular branching ratios that may occur with atmospheric NO and HO2 levels.

Each generated reaction forms one or several species. If the species is a stable organic compound (i.e., is not a radical or a rapidly reacting species such as an excited intermediate), or is a radical that is directly represented by a lumped model species in the base mechanism (as is the case for all acyl peroxy radicals in the current SAPRC lumped mechanisms), then it is categorized as a product of the reaction of the starting VOC and it is not reacted further. Otherwise, it is added to the list of intermediates to be reacted, with the process ending when all those formed have been reacted. The result of this process yields a series of explicit reactions of the VOC and the intermediates with the reactions of the type listed on Table 5. Thousands of such reactions can be generated for larger VOCs, forming hundreds of stable products; and this does not count the reactions of the many reactive stable products.

The system uses a "de minimis yield" parameter, which is set at 0.5% for SAPRC mechanisms, to determine which minor reactions can be ignored when mechanisms are generated. In the version used for SAPRC-18 and previous mechanisms, this yield test was applied independently at each reaction step, even if the reactant at the step is an intermediate formed in relatively low (but over 0.5%) yield from another intermediate also formed in a relatively low yield. This can result in many products being formed in extremely low yields that would be negligible by any reasonable criterion. To address this, for SAPRC-22 the yield test is modified so the system will ignore reaction pathways if the relative yield of the pathway multiplied by an estimated upper limit yield of the reactant is less than the de minimis yield parameter. Because the relative importance of intermediates in mechanisms depend on the relative levels of NOx, O3, OH, HO2, and other radicals that are present in the reaction system, it is necessary to define a set of environmental conditions where the concentrations of these species are specified, and thus the relative yields of all the reaction pathways, relative to the amount of starting compound reacting, can be determined. MechGen has algorithms that can derive these yields given a set of environmental conditions, provided that no reactive intermediate in the generated mechanism have reactions that ultimately re-forms itself. Because the mechanism may be used in simulations representing a variety of conditions, mechanism are generated based on estimated yields derived for three different representative environmental conditions, with the de minimis yield test being applied to the reactant yield in the environment where its yield is the highest for the particular series of competitive reactions being generated. The three environmental conditions used for mechanism generation are described in Section 3.2, and represent high NOx and low NOx daytime conditions and moderate NOx nighttime conditions.  Note that when reaction pathways are neglected due to low yields, the yields of competing pathways are increased accordingly, to maintain mass balance during the mechanism generation process.

This modified yield test procedure resulted in a more efficient mechanism generation process, with far fewer very minor pathways and very low yield intermediates and products, while having no significant effect on the major pathways and products that are predicted.

Despite the improved procedure used to eliminate negligible processes, the generated mechanisms are still much larger than necessary or appropriate for use in airshed model calculations, and need to be reduced further before MechGen output are integrated into SAPRC. In view of this, MechGen applies the following "post processing" procedures to prepare the generated mechanism for implementation into SAPRC:

Reactive intermediates that only undergo rapid unimolecular reactions (kUni > 1 min-1) or that only react with O2 are replaced by the products that they ultimately form. This is equivalent to assuming they are in steady state, which should be a good approximation for these intermediates. Branching ratios are based on ratios of rate constants at 298 K and (where applicable) atmospheric O2 levels. Effects of temperatures or varying O2 levels on these branching ratios are not considered. This eliminates essentially all types of carbon-centered and alkoxy radicals (other than phenoxy), and all types of reactive excited intermediates from the mechanism, as well as peroxy radicals that undergo isomerizations at kUni > 450 sec 1. The only remaining intermediates in the mechanisms in the mechanisms generated for SAPRC-22 are peroxy radicals that undergo bimolecular and in some cases also unimolecular reactions at competitive rates.

Reactions that occur in parallel (have the same reactants but different products) are combined into single reactions with non-integer product yield coefficients that reflect ratios of rate constants of the competing processes. Temperature dependence in the rate constant ratios (if any) are not considered, though the temperature dependence of the total rate constant is retained. This greatly reduces the number of reactions in the mechanism. It can also reduce the number of species formed in the mechanism because products formed in reactions occurring less than 0.5% of the time are removed.

Each individual organic product compound predicted to be formed in the generated mechanism is assigned a lumped model species to represent it in the processed mechanism. The SAPRC-22 lumped model species are assigned as indicated in Table A-1 and its footnotes. MechGen uses various "lumping rules", which assign compounds to model species based primarily on groups or combinations of groups in the molecule, and in some cases the OH rate constant or estimated vapor pressure, to control this process. Acyl peroxy radicals (RC(O)OO· or RCO3) are also lumped as shown on Table A-1, and for that reason MechGen does not need to generate reactions for such radicals when mechanisms are generated. This greatly reduces the number of product species in the mechanism, but only slightly reduces the numbers of remaining intermediates, which all represent various peroxy radicals.

Finally, the numbers of model species used to represent the peroxy radicals are reduced using various approaches. As indicated above and discussed in more detail below, different SAPRC mechanism use different approaches in this regard, and this is a major factor affecting differences in mechanism sizes (e.g., see Table 1). Because different peroxy representation methods were investigated and used when developing SAPRC-22, MechGen provides several options in this regard, as discussed in more detail in the following section.

MechGen will also derive mechanisms for lumped model species based on mechanisms generated for individual compounds they represent. This process is discussed below in Section 0.

Once MechGen has completed processing the reactions of all organic compounds and mixtures, the reactions of the organics in the mechanism is output to a file that is imported into a master spreadsheet that also has the base mechanism and other information needed to compile the mechanism. Macros in this spreadsheet then produce text files used by various modeling systems to implement the mechanism in models.

### Peroxy Radical Representation Methods

Many types of intermediate radicals, such as carbon-centered or alkoxy radicals, react primarily with O2 or via unimolecular reactions such that the products ultimately formed do not depend on the presence of reactants whose concentrations vary, and thus can be replaced by the product(s) they form to a good chemical approximation. However, this is not the case for peroxy radicals, which are critical intermediates that are (in most cases) primarily consumed by bimolecular reactions with NO, HO2, and to a lesser extent NO3 and other peroxy radicals, so the products they ultimately formed depend on the variable concentrations of these species. It is now realized that many peroxy radicals also undergo unimolecular "auto oxidation" isomerization reactions, but the ultimate products they form still depend on NO and other reactants unless the isomerizations are sufficiently fast that he bimolecular reactions can be neglected, which is sometimes but not always the case. This is why a more accurate peroxy representation was adopted for SAPRC-16, and utilized in SAPRC-18, resulting in much larger mechanism compared to other versions of SAPRC. Explicitly representing each of these intermediates requires large numbers of model species and reactions, so mechanisms for airshed models have to use various approaches to reduce the numbers of reactions and intermediates required.

Mechanisms designed primarily for ozone predictions can take advantage of the fact that reactions with NO is the major bimolecular loss process for peroxy radicals under conditions where O3 formation occurs, so ignoring or only approximately representing the competing reactions have only small effects on ozone predictions. SAPRC-99 (Carter, 2000) and earlier versions of SAPRC, and also versions of Carbon Bond, made the assumption that the major loss process for peroxy radicals was reaction with NO, so peroxy radicals generated in the mechanisms can be replaced by the products they ultimately form, plus the chemical "operators" that represent the amounts of NO converted to NO2 (designated "RO2-R." in SAPRC-99) or are consumed in conjunction with nitrate formation (designated "RO2-N," in SAPRC-99). This resulted in no additional model species being added to represent any radical intermediates, other than those (such as methyl peroxy and lumped acyl peroxy radicals) represented explicitly, and thus represents the maximum degree of condensation in this respect.

While this "SAPRC-99" approach is sufficient for modeling ozone formation, much of the atmosphere represented by regional models have relatively low NOx levels, and reactions with HO2 and (to a much lesser extent) other peroxy radicals become important or dominate. In addition, reactions with NO3 radicals become important fates for peroxy radicals at nighttime. The hydroperoxides formed from peroxy + HO2 reactions have generally lower vapor pressures than the products from the alkoxy radicals formed in the NO reactions, and thus can make greater contributions to SOA formation, whose predictions are increasingly important in models. In order to take the changes in product yields, and particularly the increased hydroperoxide yields, that occur under lower NOx conditions, the SAPRC-07 mechanism extended this chemical operator approach to include "x" operators to represent the formation of products from alkoxy radicals formed peroxy + NO and NO3 reactions, "z" operators to represent the formations of organic nitrates in the NO reactions, and "y" operators to represent the formation of hydroperoxides (Carter, 2010a,b), and other products formed in peroxy + HO2 reactions. This has the significant advantage of not require separate model species for the peroxy radicals themselves, though it does require including a series model species and reactions for the operators used for each product (lumped or explicit) that might be formed. This approach is also used in SAPRC-11 (Carter and Heo, 2012, 2013) and a modified version of it is extended to SAPRC-22 as discussed below. The operators used for representing peroxy reactions in standard SAPRC-22, which are analogous to those used in SAPRC-07 and 11, are included in the model species listings in Table B-1 and summarized in footnotes to Table A-1.

The SAPRC-07 operator method required incorporating the assumptions that all peroxy radicals are consumed by bimolecular reactions and making the additional approximations that (1) the rate constants for these bimolecular reactions are approximately the same for all peroxy radicals, and (2) that relative yields of products formed in NO vs. other reactions for peroxy radicals formed from other peroxy radicals in multi-step mechanisms can be estimated in the same way as from those formed directly. The first approximation ignores the fact that rate constants reactions between organic peroxy radicals can very by orders of magnitude, but these are very minor processes compared to other peroxy radical reactions (e.g., see Table 10 in Section 3.2 below), so the net effect of this approximation is relatively minor under most conditions. The second approximation neglects the fact that reactions the formation of peroxy radicals from the reactions of other peroxy radicals is reduced when the parent peroxy radical reacts to form other products. In addition, it is now realized that many peroxy radicals are also consumed by "auto oxidation" isomerization reactions, so the assumption that all are peroxy radicals are consumed by bimolecular reactions is incorrect. This would not be a problem if the major isomerization reactions are either so fast that the peroxy radical can be replaced by the products they form (as with carbon centered and alkoxy radicals), or are so slow they can be neglected, as is the case for most peroxy radicals formed from saturated hydrocarbons. However, the SAPRC-07 methods cannot handle cases where the reactions are competitive, at least not without modifications or additional approximations.

For these reasons, a more explicit approach to representing peroxy radicals was adopted for the SAPRC-16 and retained for SAPRC-18. This approach represents explicitly all the peroxy radicals predicted in the generated mechanisms at relative yields greater than 5%, though peroxy radicals formed in the same reactions and that do not undergo isomerizations are lumped together, since they generally react in parallel with the approximately the same rate constants for the major processes. The lower yield peroxy radicals are then represented using a modification of the more approximate SAPRC-07 operator approach, with an "effective NO" concentration assigned to estimate fractions of peroxy radicals that react via unimolecular vs. bimolecular reactions for the purpose of deriving product yields in the overall reactions. This is referred to as the "revised SAPRC-07 method" in the subsequent discussion, with "EffNO" being used as abbreviation for the effective NO parameter.

Assuming a constant NO concentration when deriving product yields for the revised SAPRC-07 representation is an approximation because the actual NO concentration can vary, so it is important that the choice in EffNO be appropriate for the environment being modeled. However, using this approach for low yield radicals in the SAPRC-16 representation is necessary to avoid having very large numbers of very low yield model species mechanisms for compounds with very large generated mechanisms. Although an EffNO parameters still has to be specified, its exact values is not as important for mechanisms derived using the SAPRC-16 peroxy lumping method, since its choice affects only low yield products.

Table 6 provides an example of the application of the peroxy lumping methods used in the simple case of the reaction of OH radicals with n-butane. The table shows only reactions of peroxy radicals with NO and HO2, but the reactions with NO3 and other peroxy radicals are treated similarly (and not directly used to derive the SAPRC-07 representations). The names and structures of the species used are given at the top, columns on the right give the explicit reactions (in terms of the species names) and their relative yields where applicable, and the column on the left give the merged and combined reactions as processed for the condensed mechanism. The top portion shows how the reactions are combined using the SAPRC-16 or 18 method, with those incorporated into the mechanism shown in the cells with double lines. Note that in this case the SAPRC-16 method uses two peroxy radical model species, one ("RO2-12") representing the two radicals formed in the initial reactions of OH with n-butane which can be combined because they do not isomerize), and the other ("RO2-3") representing the peroxy radical formed following the isomerization of RO2-2 (1-butyl peroxy). The bottom box shows how these are all combined to form a single reaction for the SAPRC-07 representation. Note that the "SumRO2"

Table 6.	Illustration of reaction lumping using the reaction of n-butane with OH as an example

| Name | Structure |  | Name | Structure |  | Name | Structure |
| --- | --- | --- | --- | --- | --- | --- | --- |
| NC4 | CH3CH2CH2CH3 |  | R3. | HOCH2CH2CH2CH2. |  | R1NO3-2 | CH3CH2CH2CH2ONO2 |
| R1. | CH3CH2CH(·)CH3 |  | RO2-3 | HOCH2CH2CH2CH2OO. |  | MEK | CH3CH2C(O)CH3 |
| RO2-1 | CH3CH2CH(OO·)CH3 |  | RO-3 | .OCH2CH2CH2CH2OH |  | RCHO-1 | CH3CH2CH2CHO |
| RO-1 | CH3CH2CH(O·)CH3 |  | R4. | HOCH2CH2CH2CH(.)OH |  | RCHO-2 | HC(O)CH2CH2CH2OH |
| R2. | CH3CH2CH2CH2· |  | C2. | CH3CH2· |  | ROOH-1 | CH3CH2CH(CH3)OOH |
| RO2-2 | CH3CH2CH2CH2OO· |  | ETO2 | CH3CH2OO· |  | ROOH-2 | CH3CH2CH2CH2OOH |
| RO-2 | CH3CH2CH2CH2O· |  | R1NO3-1 | CH3CH2CH(CH3)ONO2 |  | MECHO | CH3CHO |

| Ratio | Explicit reactions * | Processed for lumping (* Not shown: RO2 + NO3, RO2 and RCO3) |
| --- | --- | --- |
| 87% | NC4 + OH -> H2O + R1. | NC4 + OH -> 0.87 RO2-1 + 0.13 RO2-2 + SumRO2 |
|  | R1. + O2 -> RO2-1 |  |
| 13% | NC4 + OH -> H2O + R2. |  |
|  | R2. + O2 -> RO2-2 |  |
| 93% | RO2-1 + NO -> RO-1 + NO2 | RO2-1 + NO -> 0.93 {RO-1 + NO2} + 0.07 R1NO3-1 |
| 7% | RO2-1 + NO -> R1NO3-1 | RO-1 ->-> 0.59 {MEK + HO2} + 0.41 {MECHO + ETO2} |
| 59% | RO-1 + O2 -> MEK + HO2 |  |
| 41% | RO-1 -> MECHO + C2. | RO2-1 + NO -> 0.93*0.59 {MEK + HO2} + 0.93*0.41 {MECHO + ETO2} + 0.93 NO2 + 0.07 R1NO3-1 |
|  | C2. + O2 -> ETO2 |  |
|  | RO2-1 + HO2 -> ROOH-1 + O2 | RO2-1 + HO2 -> ROOH-1 |
| 93% | RO2-2 + NO -> RO-2 + NO2 |  |
| 7% | RO2-2 + NO -> R1NO3-2 | RO2-2 + NO -> 0.93 {RO-2 + NO2} + 0.07 R1NO3-2 |
| 83% | RO-2 ->R3. | RO-2 ->-> 0.83 {RO2-3 + SumRO2} + 0.17 {RCHO-1 + HO2} |
| 17% | RO-2 + O2 -> RCHO-1 + HO2 | RO2-2 + NO -> 0.93*0.83 {RO2-3 + SumRO2} + 0.93*0.17 {RCHO-1 + HO2} + 0.93 NO2 + 0.07 R1NO3-2 |
|  | R3. + O2 -> RO2-3 |  |
|  | RO2-2 + HO2 -> ROOH-2 + O2 | RO2-2 + HO2 -> ROOH-2 |
|  |  | Reactions used for the SAPRC-16 peroxy method are highlighted below |
|  | Merge the two peroxy radicals formed in the same reaction: RO2-12 = 0.87 RO2-1 + 0.13 RO2-2 | NC4 + OH -> RO2-12 + SumRO2 |
|  |  | RO2-12 + NO -> 0.87*0.93*0.59 {MEK + HO2} + 0.87*0.93*0.41 {MECHO + ETO2} + 0.87*0.93 NO2 + 0.87*0.07 R1NO3-1 + 0.13*0.93*0.83 {RO2-3 + SumRO2} + 0.13*0.93*0.17 {RCHO-1 + HO2} + 0.13*0.93 NO2 + 0.13*0.07 R1NO3-2 |
|  |  | RO2-12 + HO2 -> 0.87 ROOH-1 + 0.13 ROOH-2 |
| 93% | RO2-3 + NO -> RO-3 + NO2 | RO2-3 + NO -> 0.93 RO-3 + 0.07 RHNO3 |
| 7% | RO2-3 + NO -> RHNO3 | RO-3 ->-> RCHO-2 + HO2 |
|  | RO-3 -> R4. |  |
|  | R4 + O2 -> RCHO-2 + HO2 | RO2-3 + NO -> 0.93 {RCHO-2 + HO2} + 0.07 RHNO3 |
|  | RO2-3 + HO2 -> ROOH-3 + O2 | RO2-3 + HO2 -> ROOH-3 |
|  | Reactions used for the SAPRC-07 peroxy method are shown to the right. (RO2C and RO2XC represent effects on NO and NO2. See Table A-1 for the operator list for SAPRC-22) | NC4 + OH -> 0.87*0.93*0.59 {xMEK + xHO2} + 0.87*0.93*0.41 {xMECHO + xETO2} + 0.87*0.93 RO2C + 0.87*0.07 {zR1NO3-1 + RO2XC} + 0.13*0.93*0.83*0.93 {xRCHO-2 + xHO2 + RO2C} + 0.13*0.93*0.83*0.07 {zRHNO3 + RO2XC} + 0.13*0.93*0.17 {xRCHO-1 + xHO2} +0.13*0.93 RO2C + 0.13*0.07 {zR1NO3-2 + RO2XC} + 0.87 yROOH-1 + 0.13 yROOH-2 + {1 + 0.13*0.93*0.83} SumRO2 |

Table 7.	Illustration of reaction lumping using portions of the reactions of 1,3-butadiene with OH radicals as an example.

| Name | Structure |  | Name | Structure |  | Name | Structure |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BUT13 | CH2=CH-CH=CH2 |  | RO2-1 | HOCH2CH=CH-CH2OO· |  | R3. | HOCH2CH=CH-CH(·)OH |
| R1. | .CH2CH=CH-CH2OH ↔ CH2=CH-CH2(·)OH |  | R2. | HOCH(·)CH=CH-CH2OOH |  | HPCRB | HC(O)CH=CH-CH2OOH |
|  |  |  | RO-1 | HOCH2CH=CH-CH2O· |  | OLEA1 | HOCH2CH=CH-CHO |

| Ratio | Example explicit reactions | Example reactions processed for lumping |
| --- | --- | --- |
| 95% | BUT13 + OH -> R1. | BUT13 + OH = 0.95*0.33 RO2-1 + other products |
| 5% | BUT13 + OH -> other products |  |
| 62% | R1. + O2 -> other products |  |
| 33% | R1. + O2 -> RO2-1 |  |
|  | RO2-1 -> R2. (k = kUni1) | RO2-1 -> 0.92 {HPCRB + HO2} + other products |
| 92% | R2. + O2 -> HPCRB + HO2 |  |
| 8% | R2. + O2 -> other products |  |
| 95% | RO2-1 + NO -> RO-1 + NO2 | RO2-1 + NO -> 0.95 {RO-1b + NO2} + 0.05 RHNO3 (k = kNO) |
| 5% | RO2-1 + NO -> RHNO3-2 | RO-1 ->-> OLEA1 + HO2 |
|  | RO-1 -> R3. | RO2-1 + NO -> 0.95 {OLEA1 + HO2 + NO2} + other products |
|  | R3. + O2 -> OLEA1 + HO2 |  |
| Combine RO2-1 reactions, assuming fraction unimolecular = fUNI1 = kUni1/(kUni1 + kNO*[NOeff]) (This is an example of the "revised SAPRC-07" method used in this work.) |
| BUT13 + OH -> | 0.95*0.33*Funi1*0.92 {HPCRB + HO2} + 0.95*0.33*(1-Funi1)*0.95 {xOLEA1 + xHO2 + RO2C} + other products |

species is added as a product to any reaction forming a peroxy radical in both representations, so that rates of peroxy + total peroxy reactions can be calculated in the model. Table 6 shows how all the product yield coefficients in the lumped representations are calculated from the relative rates of the various competing reactions in the explicit mechanism.

An illustration of how an assigned "effective NO" concentration is used to derive the SAPRC-07-type representation of peroxy radical reactions in a case where both unimolecular and bimolecular peroxy reactions need to be represented, as is the case for portions of the isoprene + OH mechanism, is shown on Table 7. 1,3-Butadiene is used as the example because it has a somewhat simpler mechanism. This peroxy lumping method is referred to as the "revised SAPRC-07" approach in the subsequent discussion.

The "Full" version of SAPRC-22 employs essentially the same peroxy lumping approach as SAPRC-16 and 18, except that it does not lump together peroxy radicals that react in parallel, since that did not result in a significant reduction of numbers of model species. These mechanisms explicitly represent all peroxy radicals that are formed in yields of 5% or higher under standard conditions (see Section 0 for a discussion of how generated mechanisms are processed and yields are derived, and Section 3.1 for a discussion of standard conditions). Peroxy radicals formed in yields lower than 5% are represented using revised SAPRC-07 operator method discussed above. Note that this gives a mechanism that is much larger than SAPRC-18 (see Table 1), because of the revised estimation methods for unimolecular reactions of peroxy radicals results in a much larger number of non-negligible that need to be represented explicitly than was the case when SAPRC-18 was developed. This gives too large a mechanism to be appropriate for airshed modeling, but can serve as a standard in box model calculations when assessing predictions using more reduced approaches.

An important parameter in the SAPRC-16/18 peroxy lumping method used to derive the full version of SAPRC-22 is the 5% cutoff, indicating the maximum yield of peroxy radicals to be represented explicitly, as opposed to using the revised SAPRC-07 method with an assigned EffNO. Using a higher value for this cutoff would decrease the number of peroxy radicals that have to be represented explicitly, with the limit being a 100% cutoff, which is equivalent to using the revised SAPRC-07 method for all reactions, requiring no peroxy intermediates other than the SAPRC-07 operators.

The "Reduced" version of SAPRC-22 employs the revised SAPRC-07 approach for all reactions, which is equivalent to using the SAPRC-16 method with a 100% cutoff. This mechanism is comparable in size to the widely-used SAPRC-07 mechanism (see Table 1), making it suitable for use in 3D models, at least in terms of its size. However, the size advantage relative to the full version is offset by the mechanism being much more sensitive to the choice of the EffNO parameter, at least for predictions of product yields that are affected by competitions between unimolecular and bimolecular reactions of peroxy radicals. A high effective NO value would represent the higher NOx urban conditions where O3 formation is most sensitive to VOCs, such as those used to derive the MIR scale (Carter, 1994), whereas a low value represents regional or remote conditions where O3 is affected primarily by NOx availability and reactions of organics are less important in affecting O3 predictions. In view of this, and the fact that the SAPRC-22 mechanism is expected to be used primarily for modeling regions affected by urban emissions, it was decided to use an EffNO value of 0.5 ppb when deriving the reduced version of SAPRC-22. This is approximately representative of "equal benefit incremental reactivity" (EBIR) scenarios used in reactivity scale calculations (e.g., Carter, 1994), with the total pollutant levels reduced to be more representative of current pollution levels. EBIR scenarios represent intermediate NOx conditions where O3 is equally sensitive to relative changes in VOC and NOx emissions, and is one of the scenarios used in this work to compare different mechanisms and is described in Section 3.1, below. However, this may not be appropriate for all applications where SAPRC-22 may be employed, such as modeling reactions in plumes or near other NOx sources.

Test calculations discussed later in this report indicate that the full and reduced versions of SAPRC-22 give very close predictions of O3 and most other species in ambient simulations, except for certain organic products predicted from isoprene whose yields are highly dependent on NOx levels. Products from other compounds, are also affected, but differences in predictions in simulations of complex ambient mixtures are not as noticeable because of their relatively lower contributions to total emissions, The full and reduced versions also give very similar results when evaluating results of chamber experiments, except for experiments with 1,3-budadiene, isoprene and terpenes.  Therefore, use of the condensed version may be satisfactory is the main interest is predictions of ozone and atmospheric lifetimes, but is not as satisfactory if predictions of oxidized products and SOA precursors is a priority.

In order to obtain better balance between mechanism size and accuracy in product predictions, we developed a new "hybrid" peroxy lumping approach that provides a means to derive yields that depend on NO levels with a minimum number of additional reactions and model species, without having to use an assumed EffNO parameter. Rather than having a single, lumped overall reaction for each VOC reaction that represents the distribution of products formed ultimately with an assumed effective NO level, a single intermediate model species is added for each initial VOC reaction that has both a unimolecular and NO reaction, so together they can predict how yields vary with absolute NO levels without having to represent all the intermediate peroxy radicals explicitly. If reactions of any VOC model species with an atmospheric oxidant, ox (e.g., OH, O3, etc) is given by

VOC + ox ( Σi yi(EffNO) Prodi	k(VOC+ox),

but if the product or operator yields, yi depend on an as assumed EffNO, this dependence can be removed by using the following representation:

VOC + ox ( VOC_ox + Σi y0i Prodi	k(VOC+ox)

VOC_ox ( Σi yU Prodi	kUni(VOC,ox)

VOC_ox + NO ( NO + Σi yN Prodi	k(RO2+NO)

Here, "VOC_ox" is a new intermediate species added to the mechanism, and the y0's, yU's, yN's, and kUni values are derived using the revised SAPRC-07 approach as follows:

ylowNOi = Yield of Prodi derived using an EffNO low enough so yields are insensitive to EffNO

yhighNOi = Yield of Prodi derived using an EffNO high enough so yields are insensitive to EffNO

ymidNOi = Yield of Prodi using an EffNO in the range where product yields are sensitive NO

y0i = min( yhighNO,i, ylowNO,I )

yUi = ylowNOi - y0i

yNi = yhighNOi - y0i

kUnii = k(RO2+NO) x ( yhighNOi - ymidNOi) / ( ymidNOi - ylowNO)

kUni(VOC,ox) = Avg (for 3 highest |yhighNOi-ylowNOi|) kUnii

and the ylowNO, yhighNO, and ymidNO values are derived using the revised SAPRC-07 method used for the reduced versions, but for high, low, and middle EffNO levels. The low and high values were chosen so that the product yields predicted are applicable for either low or high NOx conditions, but are not sensitive to the specific values used, which were arbitrarily chosen to be 0.1 ppt and 1 ppm, respectively. The ymidNOi's were derived using an EffNO of 5 ppb, which was chosen to represent the range of NO levels where the yields are the most dependent on the EffNO values chosen. If yhighNO = ylowNO for all products, then the additional species and reactions are not added, and the reaction is represented using the same modified SAPRC-07 approach as in the condensed version. If there is no product where |yhighNO-ylowNO|>0.015, then the intermediate and the additional reactions are not added, and the modified SAPRC-07 approach is used, employing the ymidNO values as the yields. This is to avoid adding the additional model species and reactions where there is only minor a difference between high and low NO yields.

Isoprene is an example of a compound where yields of several major products in its reaction with OH are affected by absolute NO levels because of peroxy intermediates that have non-negligible unimolecular reactions. Figure 1 shows the NO dependences of the yields of two representative types of isoprene products, unsaturated aldehydes other than methacrolein formed following peroxy + NO reactions and unsaturated hydroperoxy carbonyls formed after competing unimolecular reactions of the same radicals, calculated using the revised SAPRC-07 approach as a function of the EffNO parameter. The lines on the figure show the yields derived using the hybrid approach discussed above, which fit the yields derived from varying EffNO reasonably well. The fit is not perfect because in general there are several unimolecular reactions with different rate constants that may affect overall yields, while the hybrid approach uses only one "best fit" rate constant. However, the fit is reasonably good, and this isoprene + OH case is probably reasonably representative.

The "Standard" version of SAPRC-22 employs this hybrid peroxy lumping approach, and is included in the summary of versions of SAPRC-22 given on Table 1. It was derived with ylowNO and yhighNO values of 0.1 ppt and 1 ppm, respectively, where yields are insensitive to the EffNO value used, and the ymidNO values using 5 ppb, where the yields are highly sensitive to EffNO, as shown on Figure 1. It is considered a good compromise between the somewhat more accurate but very large "full" version

Figure 1.	Comparison of yields of isoprene products whose predicted yields are highly dependent on absolute NO levels derived revised SAPRC-07 approach with varying EffNO levels against those calculated using the hybrid approach used for the standard mechanism with varying NO levels.

and the less accurate "reduced" version, and is thus recommended for use in most general airshed model applications because it does not require using a constant EffNO parameter. As discussed below, it does not give exactly the same predictions as the full version in all cases because of the approximate treatments in the revised SAPRC-07 approach of bimolecular reactions of peroxy radicals with NO3 and other peroxy radicals. However, the differences are relatively small in most cases.

### Generated Mechanisms for Lumped Model Species

Mechanisms used for most lumped model species are derived from mechanisms of the representative individual compounds the model species are designed to represent. MechGen does this by averaging or combining mechanisms of the compounds in the representative mixtures, as discussed below. The exact procedure depended on the peroxy lumping approach employed.

In the case of the reduced mechanism, where each initial reaction of individual VOCs is a single reaction given a list of product species and yields, the mechanisms of the corresponding reaction of the mixture is derived by weighted averages of the products of each initial reaction that the compounds undergo, with the rate constants for the initial reactions of the lumped species being the weighted average of the rate constants for corresponding reactions of the constituents. Note that all lumped model species must have the same types of reactions as the compounds they represent, so there are no cases where some species lumped together have a certain type of initial reaction (e.g., with O3 or NO3), while others do not. There are also no cases where species lumped together have significantly different atmospheric photolysis rates, since this is one of the criteria used to determine how to lump photoreactive species.

In the case of the full or standard mechanisms, the initial reactions of the VOCs in the initially derived explicit mechanisms are also merged using weighted averages of the product yields and rate constants, but since the explicit mechanisms are used as the starting point the products also include intermediate species. The representations of the subsequent reactions of the intermediate species formed from the components of the mixture are then derived using the same procedure as used when deriving the lumped mechanisms for individual compounds.

Four mixtures representing ambient conditions were used to determine which compounds to take as representative of the various lumped model species, depending on the primary sources of the compounds in the model simulation in terms of emissions or formation. The mixtures used when developing lumped mechanisms for SAPRC-22 are indicated in the model species listing on Table A-1 and the specific compound used for each lumped species are given in Table B-5 in the electronic supplement. These were as follows:

The "EmitMix" mixture was used to represent anthropogenic VOC emissions and consisted of annual statewide 2018 California VOC emissions from all sources, excluding wildfires and biogenics. This was provided by CARB staff (Chenxia Cai, private communication, November 2022) in terms speciation categories used by the CARB, and was used to derive speciation in terms of individual compounds using the assignments in the Carter (2015, 2023d) speciation database. Approximately 90% of the mass of this mixture could be identified as chemical compounds where MechGen could assign lumped model species. This was used to derive mixtures to use to derive mechanisms for model species representing primarily anthropogenic emissions, such as ALKn, OLEn, AROn, AMINS, etc. Note that compounds that are represented explicitly, such as, for example, propene, toluene, and the di- and trimethyl benzene isomers (see Table 2 for a complete list), are excluded from these mixtures. The composition of this mixture as used in this work is given in Table B-6 in the electronic supplement.

The "BioMix" mixture was used to represent biogenic emissions, and consisted of the statewide 2018 biogenic emissions in California, and was also provided by the CARB staff (Chenxia Cai, private communication, November 2022). It was used to derive the mixture of terpenes to derive the mechanism of the TERP model species that represents terpenes that are not represented explicitly. Note that ( and ( pinenes are excluded from this TERP mixture because they are represented explicitly (Table 2). The composition of this mixture as used in this work is given in Table B-7 in the electronic supplement.

The "Products" mixture consisted of the mixture of organic oxidation products that resulted from reacting a mixture consisting of reacting equal parts (by mass) of the anthropogenic (EmitMix) and biogenic (BioMix) mixtures under standard reaction conditions. Standard reaction conditions represented approximately EBIR conditions where O3 is equally sensitive to relative changes in VOC and O3, which is one of the four environmental conditions derived in this work as discussed in Section 3.2 for the purpose of mechanism processing and sensitivity analysis. If these background reactant concentrations and photolysis frequencies are assumed to be constant, and if a reaction time is specified (6 hours is used in this work), then the distribution of products formed when the VOC reacts under these conditions can be determined. (This is an approximation because the subsequent reactions of the non-radical products are not taken into account.) The relative concentrations in this "Products" mixture is derived by multiplying the compositions of the 50:50 anthropogenic + biogenic mixtures times the yields of a all of all the products formed when they react under standard conditions, with products formed from different compounds being summed up. This was used to derive mixtures for model species that primarily represent oxidation products, such as RCHO, KET2, CRES, etc. This calculation is done within MechGen. Note that oxidation products represented explicitly, such as acetaldehyde, glyoxal, 2-butene-1,4-dial (see Table 2 for a complete list) are excluded from these mixtures.

The "Products2" mixture consists of oxidation products that result from reacting the "Products" mixture under the standard set of conditions as discussed above. It is used to derive the mixture of catechols that result from the reactions of the phenolic compounds in the atmosphere. Although some phenolic compounds are emitted directly, most are formed as products in the reactions of aromatic hydrocarbons, so their relative levels in the "Products" mixture would be more representative to their relative atmospheric levels, and thus to relative amounts of different catechols formed in their reactions.

In some cases, there were large numbers of individual compounds represented by a given model species in the mixture representing their emissions or formation, but with only a few compounds making significant contributions. In those cases, only the compounds whose total mole fractions summed up to 90% of the total, or only the top 15 compounds (which ever was less), were used in to derive mechanisms for any lumped species. Table B-5 in the Supplementary Materials give the mixtures used to derive mechanisms of all the mixture-dependent model species used for SAPRC-22. Note that these mixtures are the same for both the standard and full version of SAPRC-22.

Although it was necessary to assume anthropogenic and biogenic mixture compositions in order to derive mechanisms for lumped model species, it should be recognized that the resulting mechanisms are not very sensitive to the exact composition of these mixtures. This is in part because the most important compound in emissions are represented explicitly, and the relatively large numbers of model species used for product compounds means that the compounds being lumped together are very chemically similar, giving similar mechanisms being derived even if the mixture of compounds used to derive their mechanisms change. Therefore, even though the anthropogenic and biogenic mixtures used to derive lumped mechanisms are based on California data, use of different mixtures will probably not result in mechanisms that give significantly different predictions, so this mechanism should be equally usable for non-California scenarios.

## Emissions Assignments

An important but often overlooked part of developing new atmospheric mechanisms is providing assignments of model species to the many hundreds of categories of compounds and mixtures used in emissions speciation profiles. Assignments of SAPRC-22 model species to all the individual compounds in the SAPRC detailed model species database are given in Table B-4 in the electronic supplement. This includes the major compounds identified in emissions, including those for which ozone reactivity scales have been calculated (Carter, 1994, 2010c).

Previously, we developed a speciation assignment database for assigning model species used in various mechanisms to speciation categories used in various emissions databases, including the Speciate database maintained by the EPA, and emissions categories used by the CARB (Carter, 2015). In addition to various SAPRC mechanisms, it includes model species assignments for Carbon Bond IV, RADM2, RACM2, and other mechanisms. This database has two parts: the assignments of actual compounds to categories used in the various databases (which includes mixtures as well as individual compounds), which is mechanism independent, then the assignments of model species to the individual compounds for the different mechanisms. The second part was updated as part of this work to include assignments of SAPRC-22. This revised speciation database is now available online at the Speciation Database website (Carter, 2023d).

When providing the anthropogenic and biogenic emissions data used to derive lumped mechanisms as discussed in Section 0 or for box model simulations described in Section 3.1, the CARB staff also provided a list of new speciation categories added to the California emissions database. Although there was insufficient time and resources available in this project to update the assignments of the new categories to chemical compounds, or to add new compounds to the speciation database, the new categories and compounds were found not to be important in the anthropogenic or biogenic emissions data that were used in this work, so the lack of assignments for them should not to be important in affecting the mixture assignments discussed in Section 0 or for box model simulations described in Section 3.1. Assignments for these new categories can be made later if required.

# Test Calculations

Several atmospheric box model scenarios were simulated in order to compare predictions of the three versions of SAPRC-22 with different peroxy lumping approaches with each other and also with SAPRC07. These simulations were also used to derive oxidant concentrations to define standard conditions for determining which routes can be neglected when generating mechanisms and for estimating relative product yields (see Section 3.2). The derivations of the test scenarios and the results of the test and evaluation calculations are discussed in this section.

## Ambient Model Scenarios and Calculations

### Scenario Inputs

The conditions and inputs of the box model scenarios used to compare different mechanisms under simulated but simplified ambient conditions, and to derive sets of standard conditions for mechanism derivation and analysis, are summarized on Table 8. These were based on averages of inputs to the 39 simplified urban scenarios used to derive the MIR and other reactivity scales (Carter, 1994), except they involved four simulated days rather than one, and had lower pollutant levels in order to better represent current ozone pollution levels in the United States. (The reactivity scenarios were based on ambient data and emissions in the '80's, and reflect higher pollutant levels than currently is the case.) No pollutants were present initially except for background CO and methane, both VOC and NOx emissions occurred at constant fluxes during the day and none at nighttime. The mixing height started at 100 meters in the morning and increased to 540 meters each day, during which the air mass was being diluted with clean air from aloft. The mixing height declined back to 100 meters at night, but this did not affect the simulation because there was no mixing or dilution during the period. The photolysis rates were calculated as a function of solar zenith angle using the same actinic fluxes used for the reactivity scale calculations (Carter, 1994, 2010a), with the zenith angles calculated from the time of day using the latitude and declination of Los Angeles and daylight savings time. The simulated results for days 2-3 owere used for the mechanism comparisons, and those for days 2 and 4 were used to derive the standard conditions. The first simulated day was used to establish background levels, since the initial and background conditions were essentially clean air.

Four different scenarios were employed, each with the same inputs except for the amounts of NOx emissions. The daily VOC emissions fluxes were set at ¼ the average used in the reactivity calculations (Carter, 1994), which gave maximum ozone levels more representative or current O3 pollution conditions than the average of the Carter (1994) reactivity scenarios, where the maximum O3 was 180-230 ppb, depending on NOx inputs. The reduced VOC inputs gave maximum ozone levels of ~140 ppb in the maximum O3 scenario, so they still represent highly polluted conditions. NOx inputs were adjusted to derive approximate MIR, MOIR, EBIR, and lower NOx conditions, representing high NOx conditions where O3 is most sensitive to VOC emissions (MIR), lower NOx conditions that achieve peak O3 levels, still lower NOx where O3 is equally sensitive to relative changes in VOC and NOx conditions (EBIR), and even lower NOx conditions where NOx is about 10% that yielding maximum O3. These conditions were determined by varying O3 to determine the highest day 2-4 O3 levels (to establish the MOIR scenario), with the NOx for the MIR and EBIR scenarios being based on ratios of MIR/MOIR and EBIR/MOIR NOx inputs (1.53 and 0.65, respectively) derived for the Carter (1994) reactivity scenarios. The low NOx scenario had NOx inputs at 10% of the MOIR level, which is arbitrary but reasonably representative of low NOx conditions.

Table 8.	Summary of inputs for the box model simulations of multi-day, urban pollution scenarios used in this work.

| Input types | Input values and description |
| --- | --- |
| Simulation times Start time End Time | Total of 4 days and 15 hours, data for the 2nd-4th day used. 6:00 AM solar daylight (8:00 AM solar) 9:00 PM solar daylight (8:00 PM solar) |
| Photolysis rate calculation | Calculated using the same actinic fluxes as a function of solar zenith angle as used for the incremental reactivity calculations of Carter (1994). These were calculated by Jeffries (unpublished results, ~1992). The zenith angle as a function of solar time was calculated for a latitude of 31.1 degrees north and 23.5 degrees west, appropriate for Los Angeles, CA. |
| Mixing heights | Reacting air mass is diluted by clean air as height raises, total volume reduced as it declines. Same schedule each day. Constant at 100 meters at the start of the simulation until 6:00 AM, then raises linearly to 250 meters at 9 PM, and declines back to 100 meters by 6AM the next day. (No emissions input while the height is declining.) |
| Initial concentrations | 2 ppm CO and 2 ppm methane. No other pollutants |
| Water concentration | 2 x 104 ppm, or ~50% RH. |
| Temperature | Constant at 300 K. |
| Aloft pollutants | None. Reactants diluted by clean air when the mixing height goes up. |
| VOC and NOx emissions schedule | VOC and NOx are emitted at constant fluxes beginning at 8:00 AM and ending at 6:15 PM local time. No emissions at other times. |
| VOC emissions flux | VOC emissions flux for all scenarios is 3.85 micromoles C/meter2/day. This is ¼ the average daily VOC emissions flux used in the reactivity scenarios of Carter (1994). Adjusted downward to better represent current U.S. pollution levels. |
| NOx emissions fluxes | NOx emissions varied by scenario, as follows: |
|  | Scenario MIR MOIR EBIR Low NOx | NOx emissions flux (micromoles/meter2/day) 0.87 (1.53 x MOIR value) 0.67 (adjusted to yield maximum ozone) 0.37 (0.65 x MOIR value) 0.06 (approximately 1/10 MOIR value) |
| VOC Speciation | Equal mass fractions of the 2018 California anthropogenic and the 2018 biogenic mixtures, as given in Table B-6 and Table B-7 in the electronic supplement. These tables also give the model species assignments for these compounds. |
| NOx Speciation | 75% NO and 25% NO2 by moles. No HONO co-emissions. |

### Mechanism Comparison Results

Figure 2 and Figure 3 show results of model simulations of representative species for the 2nd and 3rd say of these four scenarios using the three versions of SAPRC-22 developed in this work. The results for O3, NOx, OH, and other inorganics were essentially indistinguishable among the versions, and were also similar for most of the major organic species, with the data on Figure 2 being representative. However, there are larger differences between versions for some types of organic species, with Figure 3 showing the species where the largest differences are seen. As shown on Figure 1, above, the lumped unsaturated aldehydes (other than acrolein and methacrolein, which are represented explicitly and where predictions are essentially the same for the two versions) (OLEA1) and the lumped hydroperoxy carbonyls (HPCRB), formed primarily from isoprene, show the greatest differences between the full and reduced versions among the higher yield products. These differences are differences are significantly reduced when the standard version, which accounts for effects of absolute NO on product yields, is used. Use of the standard version also reduces differences in predictions of the lumped very low volatility products (OTHN). However, for some other species, particularly lumped unsaturated hydroperoxides (RUOOH), and to a lesser extent peroxy acids (PACID) and unsaturated PAN analogues (APANS), the difference between the full and other versions are greater, and additional reactions added to the standard version do not reduce these differences. In these cases, the differences can be attributed to effects of approximations incorporated in the SAPRC-07 peroxy lumping method regarding treatments of peroxy + NOx and peroxy + peroxy reactions. The full version of the mechanism would be required for more accurate predictions for these relatively minor species, but for most model applications this is not sufficient to justify use of the much larger mechanism that gives very close predictions for most species of interest.

Figure 4 compares predictions of the standard SAPRC-22 mechanism of representative species in these same scenarios with predictions of previous versions of the SAPRC mechanism, starting with SAPRC-07. It can be seen that the different versions give very similar O3 predictions, with the greatest differences being in the higher NOx, approximate MIR scenario, where O3 tends to be most sensitive to mechanisms used for reactions of VOCs. Predictions for OH are also very similar, with the greatest difference in this case being the very low NOx scenario, where SAPRC-22 and -18 gave higher OH predictions than the earlier mechanisms. The differences are greater for other species, where in most cases, where predictions of SAPRC-22 are generally closer to those for SAPRC-18, which is to be expected since SAPRC-22 was developed from SAPRC-18. Some of the differences between SAPRC-22 and SAPRC-18 can be attributed to recent updates in the mechanism generation system used during their development.

## Standard Conditions used for Mechanism Preparation and Analysis

The results of SAPRC-22 simulations of selected times in selected scenarios were used to define the standard conditions used to determine which reactions can be neglected during mechanism generation (Section 2.4.1), and to derive compositions of mixtures representing lumped organic products (Section 2.4.3. Since the derivation of SAPRC-22 depends on some these standard conditions, the initial calculations used a previous version of the mechanism, whose predictions of species concentrations defining the standard conditions were essentially the same as the final version delivered for this project. The standard conditions and their derivations are discussed in the following section.

The four sets of standard conditions used in this work are summarized on Table 9. The concentrations of the reactive species defining the conditions were derived by averaging the data for selected scenarios for selected time periods. These periods are shown Figure 5, which shows plots of fractions that peroxy radical reactions with various species as a function of time for the EBIR and low NOx scenarios. (The results for the MIR and MOIR scenarios are similar to those for EBIR, except that

Figure 2.	Plots of model simulations of selected species in the 2nd and 3rd day of the multi-day ambient simulations using various versions of SAPRC-22 developed in this work.

Figure 3.	Plots of model simulations of organic product species that appeared to be most sensitive to differences in SAPRC-22 lumping approaches on the 2nd and 3rd day of the multi-day ambient simulations using various versions of SAPRC-22..

Figure 4.	Comparisons of predictions of using SAPRC-07 through SAPRC-22 for selected species in the 2nd and 3rd day of the multi-day ambient simulations.

Table 9.	Concentrations of species and parameters used to define the standard sets of environmental conditions used in this work .

| Species or parameter | Input or species concentration (cm3 molec-1 s-1) |
| --- | --- |
|  | High NOx (MIR) | Standard (EBIR) | Low NOx | Nighttime (EBIR) |
| Use [a] | MG | PY, S | MG | MG |
| OH | 7.51e+6 | 1.11e+7 | 3.69e+6 | 2.86e+5 |
| O3 | 1.78e+12 | 2.26e+12 | 9.20e+11 | 2.90e+12 |
| O3P | 5.50e+4 | 2.84e+4 | 8.85e+3 | ~0 |
| NO | 9.58e+10 | 1.59e+10 | 4.12e+9 | 7.43e+5 |
| NO2 | 3.15e+11 | 8.63e+10 | 1.32e+10 | 4.88e+10 |
| NO3 | 8.54e+6 | 9.92e+6 | 1.25e+6 | 2.25e+9 |
| HO2 | ~0 | 6.00e+8 | 7.17e+8 | 1.27e+8 |
| Total RO2's | ~0 | 4.59e+8 | 6.69e+8 | 2.35e+8 |
| Total RCO3's | ~0 | 7.30e+7 | 7.27e+7 | 1.04e+8 |
| Reaction time [b] | 6 hours |
| T, RH | 300K and 50% RH |
| Photolysis rates | Calculated for direct overhead sunlight [c] |

[a]	Usage codes: MG: used for mechanism generation to determine reactions that can be neglected; PY: used to derive product yields for deriving mechanisms of lumped model species; S: used for comparisons of product yields with different lumping methods.

[b]	This is only used when deriving product yields for lumped model species mechanisms to determine how much product can be formed when the starting compounds have insufficient time to react completely.

[c]	Actinic fluxes are the same as those used for the box model calculations except they are assumed to be constant at a solar zenith angle of zero.

the fractions reacting with NO are close to unity during more of the daytime periods, and the fractions for the other reaction pathways are lower.  Note that a set of standard conditions representing maximum O3 (MOIR) conditions was not needed for mechanism generation because MOIR conditions are intermediate between the MIR and EBIR conditions that are already used for this purpose, and because the EBIR conditions was judged to be more appropriate for applications using a single set of conditions, since it represents intermediate NOx levels.

The standard conditions are used to determine relative amounts of the starting compounds are consumed by OH, O3, other oxidants, or photolysis, and to determine relative rates of competing reactions of the peroxy radicals, including unimolecular reactions when applicable. The former are determined by assigned concentrations of OH, O3, NO3, O3P and the actinic fluxes, while the latter are determined by concentrations of NO, HO2, NO3, and total peroxy and acyl peroxy radical levels. The relative amounts of peroxy radical reactions for the various conditions are shown on Table 10. It can be seen that essentially all peroxy radicals react with NO under high NOx or MIR conditions, while all but 7% react this way under the standard (EBIR or medium NOx) conditions, and over ¾'s react this way under low NOx conditions. However, as expected since NO is rapidly titrated by O3 at nighttime, reaction with NO is a minor loss process for nighttime conditions, where more than half of the consumption is due

Note: The mechanism used for this figure was derived using a slightly earlier version of MechGen, but the results should be essentially the same.

Figure 5.	Plots of fractions of the various types of bimolecular reactions of peroxy radicals against time for the scenarios used to derive standard conditions, showing the time periods where concentrations were averaged to yield the standard concentrations given on Table 9.

Table 10.	Relative amounts that peroxy radicals undergo their various possible bimolecular reactions in the four sets of environmental conditions used in this work.

| Reaction | Fraction peroxy radical reacts with the indicated reactant |
| --- | --- |
|  | High NOx (MIR) | Standard (EBIR) | Low NOx | Nighttime (EBIR) |
| NO | 100% | 93% | 76% | 0.08% |
| HO2 | ~0 | 6% | 22% | 22% |
| NO3 | 0.002% | 0.01% | 0.01% | 59% |
| Total RCO3's | ~0 | 0.8% | 2% | 19% |
| Total RO2's | ~0 | 0.005% | 0.02% | 0.04% |

to reaction with NO3. These ratios are shown as a function of time Figure 5, which shows the time periods over which the data were averaged to obtain the values in Table 9 and Table 10.

## Evaluation Against Chamber Data

The capability of the SAPRC-22 mechanism to predict effects of individual compounds on O3 formation, NO oxidation, and (in many cases) OH radical levels was evaluated against the essentially the same large database of environmental chamber experiments and using the same modeling procedures as used for previous versions of SAPRC, including SAPRC-07 (Carter, 2010a,b), SAPRC-11 (Carter and Heo, 2012, 2013) and SAPRC-18 (Carter, 2020a). A complete discussion of these results is beyond the scope of this report, so only a brief summary will be given here. Except as indicated below, the model performance of SAPRC-22 in simulating these data was very similar to that for SAPRC-18, was comparable to that for SAPRC-11, and was about the same for ambient mixtures or compounds important in emissions. This is probably as good as can be reasonably be expected considering uncertainties in chamber data and characterization, as well as uncertainties in the chemistry. However, for certain types of compounds, such as some esters and individual alkylbenzenes, SAPRC-18 and 22 did not perform quite as well as SAPRC-11. This is because there was less compound-by-compound adjustment of uncertain aspects of the mechanisms when developing SAPRC-18 than was the case for SAPRC-07 and 11. A greater priority was given in SAPRC-18 and 22 to developing and evaluating general estimation methods applicable to wide ranges of compounds that may have been studied previously, as opposed to minimizing biases for each one of the many individual compounds studied. Consequently, the environmental chamber data were used less for mechanism adjustment, and more for evaluating the performance of our overall estimation methods, than is the case with previous versions.

Figure 6 compares model biases for various of SAPRC-22 and also SAPRC-18 and SAPRC-11 for the various types of experiments used for mechanism evaluation. Most of the points are experiments with single compounds, but several are for various surrogates representing ambient mixtures. Figure 6a shows that the both the full and standard versions give essentially the same results in simulating the chamber data, and Figure 6b shows that the reduced version gives very close results for most compounds, except for 1,3-butadiene, isoprene, sabinene, and methacrolein, where competitions between peroxy isomerizations and bimolecular reactions are apparently more important. Figure 6c and d show that the distribution of biases for SAPRC-18 and 11 are similar to those for SAPRC-22, there are much greater differences among different types of experiments. Some experiments are simulated better using the earlier mechanisms, while some are simulated better using SAPRC-18 or 22. For example, about 60% of the types of experiments are simulated somewhat better using SAPRC-11 than SAPRC-22.

Note that, unlike the case for SAPRC-07 and 11, there was no adjustment of uncertain mechanism parameters to fit the experimental chamber data during the process of updating the mechanism to SAPRC-18 or 22. However, some of the estimation methods used by MechGen when generating mechanisms, such estimations of nitrate yields in reactions of peroxy radicals with NO and of radical forming processes in reactions of Criegee intermediates were derived based on fits to chamber data as discussed by Carter (2023c). No adjustments were made for individual compounds, however, which is why the chamber run fit statistics are not quite as good for SAPRC-18 and 22 as for previous versions, such as SAPRC-11, where much more compound-by-compound adjustment were carried out. However, compound-by-compound adjustment of sensitive uncertain parameters may be appropriate for mechanisms used to calculate ozone reactivity scales, but updating the mechanism for this purpose is beyond the scope of the present project.

| a) | b) |
| --- | --- |
| c) | d) |

Average bias is ( [model] - [experimental] ) / average ( [model], [experimental] )

Figure 6.	Comparisons of average biases in the simulations of rates of NO oxidation and maximum O3 concentrations in the evaluations of versions of SAPRC-22 and earlier SAPRC mechanisms against NOx - air chamber experiments with all the compounds and mixtures used for SAPRC mechanism evaluations..

## Mechanism Implementation Test Calculation

The electronic supplement to this document contains inputs and outputs of a test simulation for the purpose of verifying model implementation. These simulations employ 0.1 ppm NOx, 1ppmC of an anthropogenic mixture from emissions inventories, and 0.25 ppmC of a biogenic mixture, with nonzero inputs for all emitted model species in the mechanism. The photolysis rate constants are held constant at specified values appropriate for direct overhead sunlight, but they were all set to zero after 480 minutes to simulate dark chemistry. The input conditions used for the SAPRC box modeling software (Carter, 2020b) are given in Table B-8 in the electronic supplement. The simulation gave nonzero values for all reactive model species in the mechanism. The simulations were carried out for both the standard and full version of SAPRC-22, and the results in the Table B-8 and Table 11, respectively in the electronic supplement, where they can be compared with results calculated using other solvers with the same inputs. Representative results are shown in Figure 7.

Figure 7.	Concentration-time plots of selected species in the test simulation provided to verify correct implementation of SAPRC-18 in airshed model software.

# Discussion

The SAPRC-22 mechanism is the latest version of the SAPRC series of gas-phase atmospheric mechanisms for airshed models, and incorporates our current understanding of atmospheric reactions of organic compounds. The objective is to provide airshed modelers with an up-to-date mechanism with more of the chemical detail needed for more reliable ozone, toxics and eventually SOA modeling, but not so large that it is impractical for use in 3D airshed models. A unique feature of the current SAPRC mechanisms is their close link to the automated mechanism generation system, MechGen, that predicts detailed atmospheric reactions of emitted and oxidized organic compounds, using known kinetic and mechanistic data where available, and up-to-date estimates and structure-activity (SAR) estimation methods when not. This is consistent with the systematic mechanism development approach outlined by Kaduwela et al (2015), involving first developing detailed mechanisms based on available data, mechanism generation tools, and structure-reactivity and other estimation methods, evaluating the mechanism for consistency with available data, then utilizing various methods to reduce or condense the detailed mechanism for specific airshed model applications.

The SAPRC-16 mechanism (Carter, 2016, Venecek et al, 2017) represented the first complete update of the SAPRC mechanisms since the widely-used SAPRC-07 mechanism was developed (Carter, 2010a,b). Unfortunately, the scientific basis of the MechGen system used to derive most of its organic reactions was not completely documented at the time, and the system was continually changing as it was being updated to incorporate new data and estimation methods. This resulted in SAPRC-16, and its successor SAPRC-18, becoming out of date shortly after they were released. Because the scientific and regulatory community requires a stable as well as a documented mechanism, it was decided to freeze the continued development of MechGen while it is being documented for peer-reviewed publication, and update the SAPRC mechanism only after it is completed. This documentation has now been prepared and will be soon submitted for publication, and this now-documented version of MechGen has been used to develop the SAPRC-22 mechanisms discussed in this report. Although this is not the first version of SAPRC to use a mechanism generation system, it is the first where the system is comprehensively documented. Although MechGen or its successors may continue to be developed into the future and serve as the basis for new SAPRC or SAPRC-like mechanisms, the version used to derive SAPRC-22 will continue to be available to provide information and background for this mechanism, and to duplicate predictions used in its development.

However, inadequate documentation and stability was not the only problem with the SAPRC-16 and 18. In order to better account for auto-oxidation reactions of peroxy radicals and better support predictions of SOA precursors that may be influenced by such reactions, these mechanisms utilize a more accurate and detailed representation of peroxy radical reactions than employed in previous versions, requiring the use of many more model species and reactions to represent reactive intermediates. This has increased the computer resource and time requirements to use these mechanisms in 3D airshed models, which has inhibited the use of these updated mechanisms for regulatory modeling. Because the CARB has been relying on SAPRC-07 mechanisms for their regulatory modeling but needs to have a more up-to-date version, they contracted the author to develop an updated version of SAPRC that is more comparable in size to SAPRC-07, though with additional model species to better track selected toxics.

To address this need, the newly developed SAPRC-22 utilizes a somewhat modified version of the more approximate method that earlier versions used to represent peroxy reactions, though modified to account for auto-oxidation reactions by adding an extra intermediate when representing reactions where auto-oxidation is a factor. To assess the effects of this approximation on model predictions, a "full" version of SAPRC-22 was developed that was the same as the standard version except that it employed more accurate peroxy representation methods similar to that employed in SAPRC-16 and 18, and its were predictions were compared with those of the standard mechanisms. The results indicated that the approximations did affect predicted yields of some types of organic products, but O3, OH radicals and other oxidants were not significantly affected, and the products whose predictions were most affected were formed in relatively low yields, and expected to be sensitive to uncertain details in the complex mechanisms.

Therefore, the standard version of SAPRC-22 should be a good replacement to SAPRC-07 because of the updated chemistry that now includes auto-oxidation reactions, greater chemical detail for some toxic species and SOA precursors, and its comparable size and computer resource demands. It may not have as accurate a representation of peroxy chemistry as does SAPRC-16 or 18, but it is better than that used in SAPRC-07 because it can at least approximately incorporate their unimolecular reactions, and gives very close predictions of O3 and the major toxic species of current interest as the version of SAPRC-22 with the more accurate peroxy representation.

One reason for the added size and complexity of the SAPRC-16 and 18 mechanisms is the desire to have the gas-phase mechanism provide better support for SOA predictions, where chemical detail is much more important. However, it now appears likely that accurately predicting precursors to SOA formation based on actual chemistry will require far larger mechanisms that is currently used in most modeling applications. Previous work with the GeckoA mechanism generation system has indicated that multi-generation reactions, which are poorly represented in current lumped mechanisms, are important sources of SOA precursors (Aumont et al, 2005, 2012, 2013). This means that even the full version of SAPRC-22 would probably not give any more reliable predictions of SOA precursors than other lumped mechanisms, even if the uncertainty in our ability to estimate the underlying chemistry of formation of SOA precursors were not significant (which it is). Because no lumped mechanisms are considered sufficient for SOA predictions, current models use separate SOA modules to predict SOA formation using empirically derived parameters with relatively little input from the gas-phase mechanism. Although less accurate, it has the advantage of requiring less chemical detail in the gas-phase mechanism. This will have to continue to be the case until either computers become more powerful or until we develop other methods to make SOA predictions based on considerations of detailed chemistry.

Although SAPRC-07 included a module for chlorine chemistry, including halogen chemistry was beyond the scope of this project, so it is not part of SAPRC-22. It would be relatively straightforward to add and update the inorganic portion of the SAPRC-07 chlorine module to this mechanism, and also the reactions of Cl· with many of the VOCs. MechGen can already predict reactions of alkanes and other saturated VOCs where the major reaction is Cl atoms abstracting a hydrogen and forming the same types of radicals that are formed in their OH reactions, albeit with somewhat different branching ratios, which MechGen can estimate. However, adding chlorine to double bonds forms Cl-substituted radicals that require additional thermochemical estimates to MechGen to process. This is another area that could be addressed in future versions of MechGen and the mechanism, should there be sufficient interest.

Unless errors are found during the implementation and testing of the mechanism or completion of the documentation of the mechanism generation system, the mechanism documented in this report is the final version of SAPRC-22. Other than error corrections, any updates, condensations, or changes to levels of chemical detail will be incorporated into the next version of MechGen and SAPRC.

Finally it should be pointed that the author, who has been the sole developer of the SAPRC mechanisms, is getting closer to full retirement. This may well be the last major update of the SAPRC mechanisms made by the current developer. Someone else will need to take over this effort if this series of mechanisms is to continue to be supported into the future.

# Supplementary Information Available

This report includes an electronic supplement giving large tables needed to completely document the mechanism and files and data needed to implement the versions of SAPRC-22 mechanism discussed in this report using the SAPRC (Carter, 2020b), CMAQ (2022), and KPP (Sandu et al, 2022) modeling systems. An Excel file containing the large tables, files for implementing the mechanism, and the text of this report, is available at the SAPRC-22 web site at https://intra.cert.ucr.edu/~carter/SAPRC/22/. The supplementary tables and the files available online are listed on Table 11.

The SAPRC-22 web site also contains links to the SAPRC software and files that can be used to test the mechanism and evaluate against chamber data, available documentation of MechGen and access to its online version, and the speciation database website that now includes assignments of SAPRC-22 model species to various speciation categories used in emissions databases (Carter, 2015, 2023d).

Table 11.	Supplementary information needed for mechanism documentation and implementation, and links to other relevant data and software that is available online.

| File or link | Contents or Target |
| --- | --- |
| S22doc.pdf | Text of this report |
| S22supp.xls | Supplementary tables, as follows: |
| Table B-1. List of model species in the standard SAPRC-22 mechanism Table B-2. List of reactions and kinetic parameters in the standard SAPRC-22 mechanism Table B-3. Absorption cross sections and quantum yields for the photolysis reactions Table B-4. List of SAPRC detailed model species and assignments to SAPRC-22 model species Table B-5. Mixtures or compounds used to derive mechanisms of the lumped organic model species. Table B-6. Composition of the California 2018 anthropogenic emissions mixture used to derive mixtures to derive mechanisms of lumped model species representing emitted organics Table B-7. Composition of the California 2018 biogenic emissions mixture used to derive mixtures to derive mechanisms of lumped model species representing emitted organics Table B-8. Input conditions for implementation test calculation using SAPRC box model software. These were used as inputs for the test calculations shown on Table B-9. Table B-9. Output concentrations of test calculations using the standard SAPRC-22 mechanism |
| SAPRC22.rxn SAPRC22.mec S22-KPP.zip | Input files for the standard SAPRC-22 mechanism in SAPRC (.rxn), Models-3 (.mec), and KPP (S22-KPP.zip) formats. Note that the format of the KPP files have not been verified. |
| SAPRC22std.xlsSAPRC22full.xls SAPRC22red.xls | Spreadsheet containing all information needed to implement the standard, full, and reduced version of SAPRC-22, including macros to output .rxn, .mec, and KPPfiles such as those listed above.. |
| PHF.zip | Absorption cross sections and quantum yields used by SAPRC-22, in format used by SAPRC box modeling software |
| Link to SAPRC software | Link to the SAPRC box modeling software and files at https://intra.engr.ucr.edu/ ~carter/SAPRC/SAPRCfiles.htm. These can be used for implementing and running versions of the SAPRC mechanisms, including SAPRC-22. Includes files for evaluating mechanisms against SAPRC chamber data. |
| Link to MechGen documentation | Available documentation of the SAPRC Mechanism Generation System (MechGen) that was used to derive the mechanisms for organics used in SAPRC-22. Currently only preliminary and incomplete documentation is available while the more comprehensive draft documentation is being reviewed and finalized. |
| Link to MechGen | Link to the online version of MechGen, at http://mechgen.cert.ucr.edu |
| Speciation database link | Link to the emissions speciation database at https://intra.engr.ucr.edu/~carter /emitdb. This now includes speciation assignments for SAPRC-22. |

# Acknowledgements

This work was supported in part by the California Air Resources Board primarily through contract no 21AQP011, in part by the University of California Retirement system, and in part by EPA cooperative agreement no. 84000701, Kelley Barsanti, PI. Helpful discussions with Ajith Kwduwela, Chenxia Cai, and Majiong Jiang regarding CARB modeling needs, and with Kelley Barsanti and John Orlando regarding MechGen documentation and updates relevant to this project, are acknowledged. However, conclusions and statements in this document are entirely those of the author.

# References

Aumont B., S. Szopa, and S. Madronich S. (2005): "Modelling the evolution of organic carbon during its gas-phase tropospheric oxidation: development of an explicit model based on a self generating approach," Atmos. Chem. Phys. 5, 2497-2517. https://doi.org/10.5194/acp-5-2497-2005

Aumont, B., R. Valorso, M. Camredon, J. Lee-Taylor and S. Madronich (2012): "Modeling SOA formation from the oxidation of intermediate volatility n-alkanes," Atmos. Chem. Phys., 12, 7577-7599, https://doi.org/10.5194/acp-12-7577-2012

Aumont, B., M. Camredon, C. Mouchel-Vallon, S. La, F. Ouzebidour, R. Valorso, J. Lee-Taylor and S. Madronich (2013) "Modeling the influence of alkane molecular structure on secondary organic aerosol formation," Faraday Discuss., 165, 105-122, https://doi.org/10.1039/C3FD00029J

Barnes, I. (2006): "Mechanisms of the Photoxidation of Aromatic Hydrocarbons: Chemistry of Ring-Retaining Products," Presented at the International Conference on Atmospheric Chemical Mechanisms, Davis CA, December 6-8. See http://www.cert.ucr.edu/~carter/ Mechanism_Conference.

Barnes, I, K.H. Becker, and T. Zhu (1993): "Near UV absorption spectra and photolysis products of difunctional organic nitrates: Possible importance as NOx reservoirs," J. Atmos. Chem, 17 353-373. https://link.springer.com/article/10.1007/BF00696854

Bejan, Y. Abd el Aal, I. Barnes, T. Benter, B. Bohn, P. Wiesen and J. Kleffmann (2006): "The photolysis of ortho-nitrophenols: a new gas-phase source of HONO, " Physical Chemistry Chemical Physics 8, 2028–2035.

Blitz, M., M. J. Pilling, S. H. Robertson and P. W. Seakins (1999): "Direct studies on the decomposition of the tert-butoxy radical and its reaction with NO," Phys. Chem. Chem. Phys., 1999, 73-80. DOI: 10.1039/A806524A.

Butkovskaya, N., Kukui, A., and Le Bras, G. (2007): "HNO3 Forming Channel of the HO2 + NO Reaction as a Function of Pressure and Temperature in the Ranges of 72-600 Torr and 223-323 K," J. Phys. Chem. A, 111, 9047-9053.

Calvert, J.G., F. Su, J. W. Bottenheim, O. P. Strausz (1978): "Mechanism of the homogeneous oxidation of sulfur dioxide in the troposphere.", Atmos. Environ, 12, 198-226.

Calvert., J. G., R. Atkinson, J. A. Kerr, S. Madronich, G. K. Moortgat, T. J. Wallington and G. Yarwood (2000): "The Mechanisms of Atmospheric Oxidation of Alkenes," Oxford University Press, New York.

Calvert., J. G., R. Atkinson, K. H. Becker, R. M. Kamens, J. H. Seinfeld, T. J. Wallington and G. Yarwood (2002): "The Mechanisms of Atmospheric Oxidation of Aromatic Hydrocarbons," Oxford University Press, New York.

Calvert, J. G., A. Mellouski, J. J. Orlando, M. J. Pilling and T. J. Wallington (2011): “The Mechanisms of the Atmospheric Oxidation of the Oxygenates,” Oxford University Press, New York.

Calvert, J. G., J. J. Orlando, W. R. Stockwell, and T. J. Wallington (2015): “The Mechanisms of Reactions Influencing Atmospheric Ozone,” Oxford University Press, New York.

Caralp, F., V. Foucher, R. Lesclaux, T. J. Wallington, and M. D. Hurley (1999): "Atmospheric chemistry of benzaldehyde: UV absorption spectrum and reaction kinetics and mechanisms of the C6H5C(O)O2 radical", Phys. Chem. Chem. Phys., 1, 3509-3517.

Carter, W. P. L. (1994): “Development of Ozone Reactivity Scales for Volatile Organic Compounds,” J. Air & Waste Manage. Assoc., 44, 881-899.

Carter, W. P. L. (2000): “Documentation of the SAPRC-99 Chemical Mechanism for VOC Reactivity Assessment,” Report to the California Air Resources Board, Contracts 92-329 and 95-308, May 8. Available at http://www.cert.ucr.edu/~carter/absts.htm#saprc99.

Carter, W. P. L. (2010a): “Development of the SAPRC-07 Chemical Mechanism and Updated Ozone Reactivity Scales,” Final report to the California Air Resources Board Contract No. 03-318. January 27. Available at www.cert.ucr.edu/~carter/SAPRC.

Carter, W. P. L. (2010b): "Development of the SAPRC-07 Chemical Mechanism," Atmospheric Environment, 44, 5324-5335.

Carter, W. P. L (2010c): “Updated Maximum Incremental Reactivity Scale and Hydrocarbon Bin Reactivities for Regulatory Applications,” Report to the California Air Resources Board, Contract 07-339, January 28, available at http://www.cert.ucr.edu/~carter/SAPRC/MIR10.pdf.

Carter, W. P. L. (2015): "Development of a database for chemical mechanism assignments for volatile organic emissions," JA&WMA 65, 1171-1184  (2015).

Carter, W. P. L. (2016) "Preliminary Documentation of the SAPRC-16 Mechanism", Interim report to California Air Resources Board Contract No. 11-761. Available at: https://intra.cert.ucr.edu/ ~carter/SAPRC/16/. Mechanism files also at http://www.cert.ucr.edu/ ~carter/SAPRC/16/.

Carter, W. P. L. (2019b): "SAPRC Atmospheric Chemical Mechanisms and VOC Reactivity Scales," web site at https://intra.cert.ucr.edu/~carter/SAPRC/, last updated November 20.

Carter, W. P. L. (2020a): "Documentation of the SAPRC-18 Mechanism," Draft Report to California Air Resources Board Contract No. 11-761, May 29. Available at http://www.cert.ucr.edu/~carter/SAPRC/18/

Carter, W. P. L. (2020b): "SAPRC-07 and SAPRC-11 Chemical Mechanisms, Test Simulations, and Environmental Chamber Simulation Files," Available at https://www.cert.ucr.edu/~carter/ SAPRC/SAPRCfiles.htm

Carter, W. P. L. (2023a) Gateway to the SAPRC Mechanism Generation System. Web site at http:// mechgen.cert.ucr.edu. Last updated ??

Carter, W. P. L. (2023b): "The SAPRC Atmospheric Chemical Mechanism Generation System," manuscript in preparation, March.

Carter, W. P. L. (2023c): "Derivation of Atmospheric Reaction Mechanisms for Volatile Organic Compounds by the SAPRC Mechanism Generation System," manuscript in preparation, March.

Carter, W. P. L. (2023d): “Development of an Improved Chemical Speciation Database for Processing Emissions of Volatile Organic Compounds for Air Quality Models,” Web page at https://intra.engr.ucr.edu/~carter/emitdb/, Last updated ??.

Carter, W. P. L. and G. Heo (2012): "Development of Revised SAPRC Aromatics Mechanisms," Report to the California Air Resources Board Contracts No. 07-730 and 08-326, April 12, 2012. Available at http://www.cert.ucr.edu/~carter/absts.htm#saprc11.

Carter, W. P. L. and G. Heo (2013): "Development of Revised SAPRC Aromatics Mechanisms," Atmos. Environ. 77, 404-414.

CMAQ (2022): Web site at https://www.cmascenter.org/cmaq/, accessed December. See also "CMAQ: The Community Multiscale Air Quality Modeling System," https://www.epa.gov/cmaq, last updated September 19.

Gery, M. W., G. Z. Whitten, and J. P. Killus (1988):  “Development and Testing of the CBM-IV For Urban and Regional Modeling,”, EPA-600/ 3-88-012, January.

Goliff, W. S., Stockwell, W. R. and Lawson, C. V. (2013): “The regional atmospheric chemistry mechanism, version 2,” Atmos. Environ. 68, 174-185.

Hutzell, W. T., D.J. Luecken, K. W. Appel, and W.P.L. Carter (2012): "Interpreting predictions from the SAPRC07 mechanism based on regional and continental simulations," Atmospheric Environment, 46, 417-429. https://doi.org/10.1016/j.atmosenv.2011.09.030

IUPAC (2019): Recommendations of the IUPAC Task Group on Atmospheric Chemical Kinetic Data Evaluation as of December, 2019. See http://iupac.pole-ether.fr/.

Kaduwela, A, D. Luecken, W. Carter, and R. Derwent (2015): "New directions: Atmospheric chemical mechanisms for the future," Atmos. Environ. 112, 609-610, https://doi.org/10.1016 /j.atmosenv.2015.10.031

Klotz, B., F. Graedler, S. Sorensen, I. Barnes, and K.-H. Becker (2000): “A Kinetic Study of the Atmospheric Photolysis of (-Dicarbonyls,” Int. J. Chem. Kinet., 33, 9-20.

Lotz, C. and R. Zellner (2000): "Fluorescence excitation spectrum of the tert-butoxy radical and kinetics of its reactions with NO and NO2," Phys. Chem. Chem. Phys., 2353-2360 DOI: 10.1039/B001585G.

McGillen, M. R., W. P. L. Carter, A. Mellouki, J. J. Orlando, B. Picquet-Varrault, and T. J. Wallington (2020): "Database for the kinetics of the gas-phase atmospheric reactions of organic compounds," Earth Syst. Sci. Data, 12, 1203–1216, https://doi.org/10.5194/essd-12-1203-2020

McGillen, M. R., W. P. L. Carter, A. Mellouki, J. J. Orlando, B. Picquet-Varrault, and T. J. Wallington (2021). "Database for the Kinetics of the Gas-Phase Atmospheric Reactions of Organic Compounds, Version 2.1.0. Available at https://data.eurochamp.org/data-access/kin/#/home or https://doi.org/10.25326/mh4q-y215.

NASA (2011): “Chemical Kinetics and Photochemical Data for Use in Stratospheric Modeling, Evaluation Number 15,” JPL Publication 10-6, Jet Propulsion Laboratory, Pasadena, California, July.

NASA (2015): “Chemical Kinetics and Photochemical Data for Use in Stratospheric Modeling, Evaluation Number 18,” JPL Publication 15-10, Jet Propulsion Laboratory, Pasadena, California, July. Available at http://jpldataeval.jpl.nasa.gov/.

Orlando, J.J., and G.S. Tyndall (2003): "Gas phase UV absorption spectra for peracetic acid, and for acetic acid monomers and dimers. J. of Photochem. Photobiol. A, 161-166, DOI: http://dx.doi.org/10.1016/S1010-6030(03)00067-4.

Pankow, J. F. and W. E. Asher (2008): "SIMPOL.1: a simple group contribution method for predicting vapor pressures and enthalpies of vaporization of multifunctional organic compounds, Atmos. Chem. Phys., 8, 2773-2796. https://doi.org/10.5194/acp-8-2773-2008.

Platz, J., O. J. Nielsen, T. J. Wallington, J. C. Ball, M. D. Hurley, A. M. Straccia, W. F. Schneider, J. Sehested. (1998): Atmospheric Chemistry of the Phenoxy Radical, C6H5O(.): UV Spectrum and Kinetics of Its Reaction with NO, NO2, and O2, J. Phys Chem A1998, 102, 7965-7974.

Plum, C. N., Sanhuesa, E., Atkinson, R., Carter W. P. L. and Pitts, J. N., Jr. (1983): “OH Radical Rate Constants and Photolysis Rates of alpha-Dicarbonyls,” Environ. Sci. Technol. 17, 479-484.

Sandu, A, R, Sander, M. S. Long, H. Lin4, R. M. Yantosca, L. Estrada, Lu Shen, and D. J. Jacob (2022): "The Kinetic PreProcessor: KPP. An Environment for the Simuation of Chemical Kinetic Systems," Web site at https://kpp.readthedocs.io/en/latest/, apparently last modified in 2022 (viewed March, 2013).

Sarwar, G., D. Luecken, G. Yarwood, G.Z. Whitten and W. P. L. Carter (2008): “Impact of an Updated Carbon Bond Mechanism on Predictions from the Community Multiscale Air Quality (CMAQ) Modeling System: Preliminary Assessment,” J. of Appl. Met. and Climat., 47, 3-14

Sarwar, G., K. Fahey, R. Kwok, S. J. Roselle, R. Mathur, J. Xue, J. Yu, W. P. L. Carter (2013): "Potential impacts of two SO2 oxidation pathways on regional sulfate concentrations: aqueous-phase oxidation by NO2 and gas-phase oxidation by Stabilized Criegee Intermediates," Atmos. Environ., 68 186-197

Stavrakou, T, J.-F. Müller, K. F. Boersma, R. J. van der A, J. Kurokawa, T. Ohara, and Q. Zhang (2013): "Key chemical NOx sink uncertainties and how they influence top-down emissions of nitrogen oxides," Atmos. Chem. Phys., 13, 9057-9082.

Stockwell, W. R., P. Middleton, J. S. Chang, and X. Tang (1990): “The Second Generation Regional Acid Deposition Model Chemical Mechanism for Regional Air Quality Modeling,” J. Geophys. Res. 95, 16343-16376.

Stockwell, W.R., F. Kirchner, M. Kuhn, and S. Seefeld (1997): “A new mechanism for regional atmospheric chemistry modeling,” J. Geophys. Res., 102, 25847-25880.

Stockwell, W. R., and W. S. Goliff (2006): “The Regional Atmospheric Chemistry Mechanism, Version 2.” Presented at the International Conference on Atmospheric Chemical Mechanisms, Davis, CA, December 6-8, 2006. Available at http://www.cert.ucr.edu/~carter/Mechanism_Conference/

Tao, Zhining  and Zhuangjie Li (1999): "A kinetics study on reactions of C6H5O with C6H5O and O3 at 298 k," Int. J. Chem. Kinet. 31, 65-72. https://doi.org/10.1002/(SICI)1097-4601(1999)31:1<65::AID-KIN8>3.0.CO;2-J

Venecek, M. A., C. Cai, A. Kaduwelab, J. Avise, W. P. L. Carterc (2018): "Analysis of SAPRC16 chemical mechanism for ambient simulations," Atmos Environ, 192, 136-150. https://doi.org/10.1016/j.atmosenv.2018.08.039

Vereecken, L., A. Novelli and D. Taraborrelli (2017): "Unimolecular decay strongly limits the atmospheric impact of Criegee intermediates," Phys.Chem.Chem.Phys., 19, 31599-31612. DOI: 10.1039/c7cp05541b

Welz, O., Savee, J.D., Osborn, D.L., Basu, S.S., Percival, C. J., Shallcross, D.E., Taatjes, C.A. (2012): Direct kinetic measurements of Criegee Intermediate (CH2OO) formed by reaction of CH2I with O2. Science, 335, 204-207.

Yarwood, G., S. Rao, M. Yocke, and G. Whitten (2005): “Updates to the carbon bond chemical mechanism: CB05. Final report to the U.S. EPA, RT-0400675. Available at http:// www.camx.com/publ/pdfs/CB05_Final_Report_120805.pdf.

Yarwood, G, J. Jung, G. Z. Whitten, G. Heo, J. Melberg, and M. Estes (2010): "Updates to the Carbon Bond Mechanism for Version 6 (CB6), Presented at the 9th Annual CMAS Conference, Chapel Hill, NC, October 11-13.

# Mechanism Listing tables

Table A-1 and Table A-2 give lists of all the model species and reactions in the standard version of the SAPRC-22 mechanism. Footnotes to Table A-1 describe the model species used and footnotes to Table A-2 document the sources of the rate constants and reactions. Note that the footnotes do not discuss the derivation of the mechanisms derived using MechGen; this information can be obtained from MechGen output and documentation (Carter, 2023a-c). The listing on Table A-1 and reactions on Table A-2 do not include all the x(product), y(product) and z(product) chemical operators used, only representative examples and listings of all operators used in the footnotes. Complete listings of species and reactions, including all the species and reactions in the full mechanism, are given in the SAPRC22std.xls and SAPRC22full.xls files included in supplementary materials available online (see Table 11, above).

Table A-1.	List of model species in the SAPRC-22 mechanisms.

| Type and Name | Mechanism derivation [a] | Note [b] | Atoms | Molec. wt [c] | Description |
| --- | --- | --- | --- | --- | --- |
|  |  |  | C | N |  |  |
| Constant Species. |  |  |  |  |  |
|  | O2 | Base |  | - | - | 32.00 | Oxygen |
|  | M | Base |  | - | - | 28.85 | Air |
|  | H2O | Base |  | - | - | 18.02 | Water |
|  | HV | Base | 1 | - | - | 0.00 | Light |
| Active Inorganic Species. |  |  |  |  |  |
|  | O3 | Base |  | - | - | 48.00 | Ozone |
|  | NO | Base |  | - | 1 | 30.01 | Nitric Oxide |
|  | NO2 | Base |  | - | 1 | 46.01 | Nitrogen Dioxide |
|  | NO3 | Base |  | - | 1 | 62.01 | Nitrate Radical |
|  | N2O5 | Base |  | - | 2 | 108.02 | Nitrogen Pentoxide |
|  | HONO | Base |  | - | 1 | 47.02 | Nitrous Acid |
|  | HNO3 | Base |  | - | 1 | 63.02 | Nitric Acid |
|  | HNO4 | Base |  | - | 1 | 79.02 | Peroxynitric Acid |
|  | HO2H | Base |  | - | - | 34.01 | Hydrogen Peroxide |
|  | CO | Base |  | 1 | - | 28.01 | Carbon Monoxide |
|  | H2 | Base |  | - | - | 2.02 | Hydrogen Molecules |
|  | SO2 | Base |  | - | - | 64.06 | Sulfur Dioxide |
| Active Radical Species and Operators |  |
|  | OH | Base | 2 | - | - | 17.01 | Hydroxyl Radicals |
|  | HO2 | Base |  | - | - | 33.01 | Hydroperoxide Radicals |
| Steady State Inorganic Radical Species |  |  |  |
|  | O3P | Base |  | - | - |  | Ground State Oxygen Atoms |
|  | O1D | Base |  | - | - |  | Excited Oxygen Atoms |
| Peroxy Radical Species in Base Mechanism |  |  |
|  | MEO2 | Base | 3 | 1 | - |  | Methyl peroxy radicals |
|  | ETO2 | Base | 3 | 2 | - |  | Ethyl peroxy radicals |
|  | BZO2 | Base | 3 | 6 | - |  | Benzyl peroxy and substituted benzyl peroxy radicals |
|  | SumRO2 | Base | 4 | - | - |  | Total peroxy radical concentration |
|  | SumRCO3 | Base | 4 | - | - |  | Total acyl peroxy radical concentration |
| Acyl peroxy radical species |  |  |  |  |  |
|  | MECO3 | Base | 3 | 2 | - |  | Acetyl Peroxy Radicals (forms PAN) |
|  | R2CO3 | Base | 3 | 3 | - |  | Higher saturated peroxy acyl radicals (forms PAN2) |
|  | BZCO3 | Base | 3 | 7 | - |  | Peroxyacyl radical formed from Aromatic Aldehydes (forms PBZN) |
|  | MACO3 | Base | 3 | 4 | - |  | Peroxyacyl radicals formed from methacrolein and other unsaturated aldehydes (forms MAPAN) |
| Other organic radical or reactive intermediate species |  |
|  | TBUO | Base | 3 | 4 | - | 73.11 | t-Butoxy Radicals |
|  | BZO | Base | 3 | 6 | - | 93.10 | Phenoxy or substituted phenoxy radicals |
|  | HCHO2 | Base | 3 | 1 | - | 46.03 | Unsubstituted stabilized Criegee biradical |
|  | MECHO2 | Base | 3 | 2 | - | 60.05 | Methyl substituted stabilized Criegee biradical |
|  | RCHO2 | Base | 3 | 3 | - | 74.08 | Other stabilized Criegee biradicals |
| Radical operator species |
|  | RO2C | Base | 5 | - | - |  | Peroxy Radical Operator representing NO to NO2 and NO3 to NO2 conversions, and the effects of peroxy radical reactions on acyl peroxy and other peroxy radicals. |
|  | RO2XC | Base | 6 | - | -1 |  | Peroxy Radical Operator representing NO consumption (used in conjunction with organic nitrate formation), and the effects of peroxy radical reactions on NO3, acyl peroxy radicals, and other peroxy radicals. (used in some multi-step mechanisms) |
|  | x(product) (46 total) | Base | 3, 7 | varies |  | Formation of a product or radical after reactions of peroxy radicals with NO. |
|  | y(product) (5 total) | Base | 3, 8 | varies |  | Formation of a hydroperoxide product after reactions of peroxy radicals with HO2. |
|  | z(product) (9 total) | Base | 3, 9 | varies |  | Formation of an organic nitrate product after the reactions of peroxy radicals with NO. |
|  | spec_OH (16 total) | MechGen | 3, 10 | - | - |  | Peroxy radical operator used to represent the effects of absolute NO levels on product yields in reactions of VOC model species with OH. |
|  | spec_N3 (4 total) | MechGen | 3, 10 | - | - |  | As above, but for reactions with NO3. |
|  | spec_O3 (7 total) | MechGen | 3, 10 | - | - |  | As above, but for reactions with O3. |
|  | spec_HV (9 total) | MechGen | 3, 10 | - | - |  | As above, but for photolysis reactions. |
|  | NPRAD | Base | 3, 11 | 12 | - |  | Simplified representative of unknown naphthalene intermediates that react with NO2 forming products |
|  | PNAMIN | Base | 3, 12 | 4 | 1 |  | N-centered radicals with no alpha hydrogens that primarily react with NO2 to form Nitramines. |
| Explicitly represented organics |  |
|  | CH4 | Base | 13 | 1 | - | 16.04 | Methane |
|  | ETHAN | MechGen | 14 | 2 | - | 30.07 | Ethane |
|  | PROP | MechGen | 14 | 3 | - | 44.10 | Propane |
|  | NC4 | MechGen | 14 | 4 | - | 58.12 | n-Butane |
|  | ETHEN | MechGen | 14 | 2 | - | 28.05 | Ethylene |
|  | PROPE | MechGen | 14 | 3 | - | 42.08 | Propene |
|  | ISOP | MechGen | 13 | 5 | - | 68.12 | Isoprene |
|  | BUT13 | MechGen | 14 | 4 | - | 54.09 | 1,3-Butadiene |
|  | APINE | MechGen | 14 | 10 | - | 136.23 | a-Pinene |
|  | BPINE | MechGen | 14 | 10 | - | 136.23 | b-Pinene |
|  | ACETL | MechGen | 14 | 2 | - | 26.04 | Acetylene |
|  | BENZ | MechGen | 13 | 6 | - | 78.11 | Benzene |
|  | TOLU | MechGen | 14 | 7 | - | 92.14 | Toluene |
|  | OXYL | MechGen | 14 | 8 | - | 106.17 | o-Xylene |
|  | MXYL | MechGen | 14 | 8 | - | 106.17 | m-Xylene |
|  | PXYL | MechGen | 14 | 8 | - | 106.17 | p-Xylene |
|  | BZ123 | MechGen | 14 | 9 | - | 120.19 | 1,2,3-Trimethyl Benzene |
|  | BZ124 | MechGen | 14 | 9 | - | 120.19 | 1,2,4-Trimethyl Benzene |
|  | BZ135 | MechGen | 14 | 9 | - | 120.19 | 1,3,5-Trimethyl Benzene |
|  | C2BEN | MechGen | 14 | 8 | - | 106.17 | Ethyl Benzene |
|  | MTBE | MechGen | 15 | 5 | - | 88.14 | Methyl t-Butyl Ether |
|  | HCHO | MechGen | 13 | 1 | - | 30.03 | Formaldehyde |
|  | MEOH | MechGen | 13 | 1 | - | 32.04 | Methanol |
|  | HCOOH | MechGen | 13 | 1 | - | 46.03 | Formic Acid |
|  | MEOOH | MechGen | 16 | 1 | - | 48.04 | Methyl Hydroperoxide |
|  | MECHO | MechGen | 14 | 2 | - | 44.05 | Acetaldehyde |
|  | ETOH | MechGen | 14 | 2 | - | 46.07 | Ethanol |
|  | GLY | MechGen | 13 | 2 | - | 58.04 | Glyoxal |
|  | GLCHO | MechGen | 13 | 2 | - | 60.05 | Glycolaldehyde |
|  | ETCHO | MechGen | 16 | 3 | - | 58.08 | Propionaldehyde |
|  | ACRO | MechGen | 13 | 3 | - | 56.06 | Acrolein |
|  | ACET | MechGen | 13 | 3 | - | 58.08 | Acetone |
|  | MEK | MechGen | 13 | 4 | - | 72.11 | Methyl ethyl ketone |
|  | MACR | MechGen | 13 | 4 | - | 70.09 | Methacrolein |
|  | MVK | MechGen | 13 | 4 | - | 70.09 | Methyl Vinyl Ketone |
|  | BUDAL | MechGen | 16 | 4 | - | 84.07 | 2-Butene-1,4-dial |
|  | PHEN | MechGen | 13 | 6 | - | 94.11 | Phenol |
| Explicitly represented toxic species or other compounds of interest |
|  | CLETHE | Simplified | 17 | 2 | - | 62.50 | Vinyl chloride |
|  | ACRLNT | Simplified | 17 | 3 | 1 | 53.06 | Acrylonitrile |
|  | PCE | Simplified | 17 | 2 | - | 165.83 | Perchloroethylene |
|  | PCLBEN | Simplified | 17 | 6 | - | 147.00 | p-dichlorobenzene |
|  | MECL2 | Simplified | 17 | 1 | - | 84.93 | Methylene chloride |
|  | ETBR2 | Simplified | 17 | 2 | - | 187.86 | Ethylene dibromide |
|  | ETCL2 | Simplified | 17 | 2 | - | 98.96 | Ethylene dichloride |
|  | ETOX | Simplified | 17 | 2 | - | 44.05 | Ethylene oxide |
|  | CHCL3 | Simplified | 17 | 1 | - | 119.38 | Chloroform |
|  | CCL4 | Unreactive | 17 | 1 | - | 153.82 | Carbon tetrachloride (unreactive) |
| Lumped Organic Compounds - Primarily emitted |  |
|  | ALK1 | mix=ALK1 | 18 | 3 | - | 74.08 | Saturated compounds that react only with OH, and have kOH between 1.4 x 10-13 and 3.5 x 10-13 cm3 molec-1 s-1 |
|  | ALK2 | mix=ALK2 | 18 | 4 | - | 88.11 | Saturated compounds that have kOH between 3.5 x 10-13 and 1.7 x 10-12 cm3 molec-1 s-1 |
|  | ALK3 | mix=ALK3 | 18 | 5 | - | 80.54 | Saturated compounds that and have kOH between 1.7 x 10-12 and 3.5 x 10-12 cm3 molec-1 s-1 |
|  | ALK4 | mix=ALK4 | 18 | 5 | - | 71.04 | Saturated compounds that and have kOH between 3.5 x 10-12 and 6.0 x 10-12 cm3 molec-1 s-1 |
|  | ALK5 | mix=ALK5 | 18 | 6 | - | 96.98 | Saturated compounds that and have kOH greater than 6.0 x 10-12 cm3 molec-1 s-1 and have fewer than 12 carbons + oxygens. |
|  | ALK6 | mix=ALK6 | 18 | 13 | - | 200.16 | Saturated compounds that and have kOH greater than 6.0 x 10-12 cm3 molec-1 s-1 and have 12 or more carbons + oxygens. |
|  | OLE1 | Mix=EmitMix | 18 | 5 | - | 68.66 | Alkenes other than ethene with kOH between 8x 10-12 and 6 x 10-11 cm3 molec-1 s-1 |
|  | OLE2 | Mix=EmitMix | 18 | 5 | - | 64.92 | Alkenes other than terpenes or 1,3-butadiene that have OH rate constants greater than 6 x 10-12 cm3 molec-1 s-1. |
|  | OLE3 | Mix=EmitMix | 18 | 4 | - | 58.05 | Alkenes other than terpenes or sesquiterpenes with only -CR=CH2 groups. |
|  | OLE4 | Mix=EmitMix | 18 | 5 | - | 71.51 | Alkenes other than terpenes with non-conjugated -CH=CR- or -CR=CR- groups and possibly other double bonds and no double bonds in rings |
|  | TERP | Mix=BioMix | 19 | 10 | - | 136.23 | Lumped terpenes (C10H16 and at least one ring and alkene group) |
|  | SESQ | B-CARYOP | 20 | 15 | - | 204.35 | Sesquiterpenes |
|  | BENX | BENZENE | 20 | 6 | - | 78.11 | Benzene and substituted benzenes that react with kOH between 5 x 10-13 and 5 x 10-12 cm3 molec-1 s-1 |
|  | ARO1 | Mix=EmitMix | 18 | 10 | - | 128.78 | Alkylbenzenes that react with kOH between 5 x 10-12 and 1 x 10-11 cm3 molec-1 s-1. Mostly alkylbenzenes with only one substituent |
|  | ARO2 | Mix=EmitMix | 18 | 9 | - | 126.42 | Alkylbenzenes that react with kOH higher than 1 x 10-11 cm3 molec-1 s-1. Mostly alkylbenzenes with more than one substituent |
|  | NAPS | NAPHTHAL | 11, 20 | 11 | - | 142.20 | Naphthalenes, tetralins, and indans |
|  | FURNS | FURAN | 20 | 4 | - | 68.07 | Furans (mechanism based on furan) |
|  | STYRS | STYRENE | 20 | 8 | - | 104.15 | Styrenes |
|  | AMINS | Mix=EmitMix | 18 | 3 | 1 | 52.06 | Amines |
|  | TAMNS | TBU-AMIN | 20 | 4 | 1 | 73.14 | Amines bonded to a tertiary carbon (inhibiting) |
|  | PHOT | Base simplified | 21 | 4 | - | 86.09 | Unspecified photoreactive compounds such as nitrites or chloropicrin |
| Lumped Organic Compounds - Primarily formed as products |
|  | RCHO | Mix=Products | 22 | 5 | - | 100.45 | C4+ saturated aldehydes with 9 or fewer carbons |
|  | OLEA1 | Mix=Products | 22 | 7 | - | 143.12 | Unsaturated aldehydes with C=C next to -CHO (mostly from aromatics) |
|  | OLEA2 | Mix=Products | 22 | 8 | - | 151.84 | Unsaturated aldehydes with C=C not next to the -CHO (mostly from aromatics) |
|  | KET2 | Mix=Products | 22 | 5 | - | 99.82 | Photoreactive saturated ketones |
|  | LVKS | Mix=Products | 22 | 8 | - | 154.23 | Ketones with at least 1 C=C double bond. |
|  | OLEP | Mix=Products | 22 | 8 | - | 160.86 | Non-photoreactive, non-hydrocarbon compounds with C=C double bonds |
|  | OACID | Mix=Products | 22 | 2 | - | 60.05 | Organic acids |
|  | PACID | PAA | 20 | 2 | - | 76.05 | Organic peroxyacids |
|  | MGLY | MEGLYOX | 20 | 3 | - | 72.06 | Methyl Glyoxal and other alpha-keto aldehydes |
|  | BACL | BIACETYL | 20 | 4 | - | 86.09 | Biacetyl and other alpha-diketones |
|  | CRES | Mix=Products | 22 | 7 | - | 108.14 | Cresols |
|  | XYNL | Mix=Products | 22 | 8 | - | 124.84 | Xylenols and higher alkylphenols |
|  | CATL | Mix=Products2 | 23 | 7 | - | 124.14 | Dihydroxy phenols |
|  | CATL3 | Base simplified | 23a | 7 |  | 140.14 | Tri- and multi-hydroxy phenols |
|  | BALD | Base simplified | 24 | 7 | - | 72.06 | Aromatic aldehydes (e.g., benzaldehyde) |
|  | NPHE | Base simplified | 24 | 6 | 1 | 86.09 | Nitrophenols |
|  | RCNO3 | Mix=Products | 22 | 6 | 1 | 180.91 | Volatile organic carbonly nitrates |
|  | RHNO3 | Mix=Products | 22 | 8 | 1 | 176.59 | Volatile organic hydroxy nitrates |
|  | RANO3 | Mix=Products | 22 | 9 | 1 | 230.33 | Organic nitrates with peroxy groups (formed primarily from aromatics) |
|  | RPNO3 | Mix=Products | 22 | 9 | 1 | 230.33 | Organic nitrates with hydroperoxy groups |
|  | RDNO3 | Mix=Products | 22 | 9 | 2 | 249.44 | Volatile organic dinitrates |
|  | R1NO3 | Mix=Products | 22 | 6 | 1 | 146.57 | Other volatile organic nitrates that react with OH radicals slower than 5 x 10-12 cm3 molec-1 s-1 |
|  | R2NO3 | Mix=Products | 22 | 9 | 1 | 190.37 | Other volatile organic nitrates that react with OH radicals faster than 5 x 10-12 cm3 molec-1 s-1 |
|  | ROOH | Mix=Products | 22 | 4 | - | 97.00 | Other hydroperoxides with 3+ carbons and vapor pressure greater than 1 ppb |
|  | RAOOH | Mix=Products | 22 | 8 | - | 188.67 | Hydroperoxides with peroxy groups and with C=C double bonds (mainly hydroperoxides formed from reaction with NO with OH-aromatic-O2 adducts after peroxy cyclization) |
|  | RUOOH | Mix=Products | 22 | 7 | - | 145.11 | Hydroperoxides with C=C double bonds |
|  | HPCRB | Mix=Products | 22 | 5 | - | 128.44 | Unsaturated hydroperoxy carbonyls |
|  | AFG1 | Mix=Products | 22 | 5 | - | 99.49 | Monounsaturated 1,4-dialdehydes formed from aromatics |
|  | AFG2A | Mix=Products | 22 | 5 | - | 101.70 | Monounsaturated 1,4 aldehyde-ketones formed from aromatics, with at no substituents other than the aldehyde on the double bonds |
|  | AFG2B | Mix=Products | 22 | 6 | - | 112.13 | Monounsaturated 1,4 aldehyde-ketones formed from aromatics, with at least one substituent other than the aldehyde on a double bond |
|  | AFG3 | Mix=Products | 22 | 6 | - | 112.13 | Monounsaturated 1,4-diketone aromatic products |
|  | NAPPRD | Base simplified | 24 | 12 | - | 172.22 | Phenolic and other products formed from naphthalenes. |
|  | IMINE | Base simplified | 25 | 2 | 1 | 34.07 | Any compound with C=N bond. Assumed to rapidly hydrolize. |
| PAN and PAN Analogues |  |  |  |  |  |
|  | PAN | MechGen | 13 | 2 | 1 | 121.05 | Peroxyacetyl nitrate |
|  | PAN2 | PBN | 20 | 4 | 1 | 149.10 | Higher saturated PAN analogues |
|  | APANS | MAPAN | 20 | 4 | 1 | 147.09 | PAN analogues formed from Methacrolein and other unsaturated PAN analogues. |
|  | PBZN | Base simplified | 24 | 7 | 1 | 183.13 | PAN analogues formed from Aromatic Aldehydes |
| Non-Reacting Species (Active for testing -- can be removed if not needed) |
|  | CO2 | Inert |  | 1 | - | 44.01 | Carbon Dioxide |
|  | SULF | Inert |  | - | - | 98.08 | Sulfates (SO3 or H2SO4) |
|  | RNNO3 | Inert | 26 | 10 | 1 | 216.23 | Organic nitrates with vapor pressure less than 1e-13 atmospheres (0.1 ppt) |
|  | OTHN | Inert | 26 | 12 | - | 240.28 | Other organic products with vapor pressures less than 1 x 10-13 atmospheres (0.1 ppt) |
|  | NAMIN | Inert |  | 4 | 2 | 89.14 | Nitramines |
|  | MALAH | Inert |  | 4 | - | 98.06 | Maleic anhydride |
|  | INHIB | Inert | 27 | 4 | - | 90.00 | Radical inhibiting compounds (treated as unreactive) |
|  | NROG | Inert | 28 | - | - | 1.00 | Unreactive mass |
|  | NVOL | Inert | 29 | - | - | 1.00 | Nonvolatile mass |

[a]	Mechanism derivation notes:

Base: Part if the base mechanism, with reactions derived manually from results of data evaluations and other information. See mechanism listing on Table A-2, and footnotes to the reactions.

Base simplified: Part of the extended base mechanism, with represented by a simplified or parameterized mechanism either adjusted to fit chamber data or to give a simplified representation of the overall effects of the reactions.

Simplified: This compound, which is included in the mechanism for tracking purposes only and is not expected to significantly affect formation of secondary pollutants, is represented using a simplified mechanism primarily to track its rate of consumption.

MechGen: Mechanism for this compound derived using MechGen.

Mix=(mixture): Derived by MechGen from the compositions of mixtures that are represented using this model species, as discussed in the text. Mixtures used as as follows. EmitMix: compounds identified in anthropogenic emissions; BioMix: compounds in biogenic emissions; Products: compounds formed from reactions of compounds in EmitMix and BioMix; Products2: compounds from reactions of compounds in the "Products" mixture.

Compound name (all caps): Mechanism approximated by the MechGen-derived mechanism of the indicated compound. Compounds used are: benzene, naphthalene, furan, styrene, peroxy acetic acid (PAA), methyl glyoxal, biacetyl, b-caryophyllene, CH2=C(CH3)C(O)OONO2 (MAPAN), and CH3CH2CH2C(O)OONO2 (PBN).

Inert: Compound treated as unreactive. It could be removed from the model if its simulated concentrations are not of interest.

[b]	Notes for individual species

1	Fraction of light intensity relative to maximum or clear sunlight. May not be needed depending on photolyses are handled by the model.

2	It may be appropriate to use the steady state approximation for this species but this is not possible using the way the SAPRC modeling software implements the steady state approximation.

3	Use of the steady state approximation for this species is recommended to reduce computer time and memory if the simulation software provides for this.

4	These are the sums of total concentrations of peroxy (SumRO2) or acyl peroxy (SumRCO3) radicals that react with other peroxy radicals, and are used to compute the rates of these peroxy + peroxy reactions. Every reaction that forms a peroxy or acyl peroxy radical of this type also forms the corresponding "Sum" species at the same yield, and their loss reactions with NO, NO2 (for SumRCO3), HO2, and each other are included as separate reactions. Peroxy radicals undergo rapid isomerizations are not included because they are replaced by the products they form.

5	Represents the conversions of NO to NO2 by reactions of peroxy radicals for all the peroxy radicals generated by MechGen in the standard mechanism that are represented using the SAPRC-07 peroxy lumping approach.

6	Represents the consumption of NO by reactions of peroxy radicals forming organic nitrates for all the peroxy radicals generated by MechGen that are represented using the SAPRC-07 peroxy lumping approach.

7	Represents the formation of various products or radicals following the reactions of alkoxy radicals formed from the reactions of peroxy radicals (primarily the reaction with NO but to a lesser extent for reactions with NO3, SumRO2 or SumRCO3). The carbon and nitrogen numbers are the same as those assigned to the model species formed. Used for NO2, NO3, OH, HO2, HCHO, GLY, HCOOH, MECHO, ETCHO, GLCHO, MEK, ACRO, ACET, MACR, MVK, BACL, MGLY, BUDAL, FURNS, BALD, BENX, RCHO, KET2, LVKS, OLEA1, OLEA2, OLEP, OACID, PACID, AMINS, RPNO3, RCNO3, RHNO3, RDNO3, HPCRB, AFG1, AFG2A, AFG2B, AFG3, PAN2, MEO2, ETO2, MECO3, R2CO3, MACO3 and TBUO in the standard mechanism.

8	Represents the formation of hydroperoxide products following the reactions of peroxy radicals with HO2. Used for RUOOH, RAOOH, HPCRB, ROOH and RPNO3.

9	Represents the formation of organic nitrate products following the reactions of peroxy radicals with NO. Used for RCNO3, RHNO3, RANO3, RPNO3, RDNO3, R1NO3, R2NO3, RNNO3 and PAN2.

10	As discussed in Section 2.4.2, these intermediates were used in the standard version of SAPRC-22 to account for dependences of overall product yields on absolute NO levels in reaction sequences that involve competitions between peroxy unimolecular and bimolecular reactions. These are used only when absolute NO concentrations changed overall product yields by more than 0.015. "Spec" refers to the reacting model species. Examples include ISOP_OH, OLE2_O3, MACR_N3, and RCHO_HV. See Table A-2 for a complete list.

11	MechGen is currently not capable of handling mechanisms for naphthalenes, PAHs, and tetralins, so a simplified parameterized representation adjusted to fit chamber data where available, has to be used. "NPRAD" is one of the model species needed to implement these parameterized mechanisms.

12	Amines with no ( hydrogens cannot react with O2, so their main atmospheric sinks would be reactions with NOx or HO2. This is the intermediate used to represent these radicals.

13	These are represented explicitly in SAPRC-11 and later versions of SAPRC.

14	These are represented explicitly in the "toxics" version of SAPRC-07 as implemented in CMAQ.

15	MTBE is included as an explicit compound at the request of the CARB staff.

16	These are represented explicitly in SAPRC-18.

17	These compounds are of regulatory interest and are represented explicitly so their concentrations can be tracked in atmospheric models, even though they are not emitted in sufficient quantities or are sufficiently reactive to affect predictions of secondary pollutants. Except for carbon tetrachloride, which is unreactive, they are represented by highly simplified mechanisms designed primarily to track their consumption due to reaction with OH radicals. Note that these are not included in the extended mechanism.

18	The mechanisms for these model species were derived from mechanisms of the major components of the mixture representing anthropogenic emissions. See text.

19	The mechanism for TERP was were derived from mechanisms of the major terpenes in the mixture representing anthropogenic emissions. Note that MechGen lumps all compounds with formula C10H16 that contains at least one ring and one more double bond as a terpene. Otherwise it is lumped as OLEx or ALKx, depending on the presence and types of double bond(s).

20	Mechanism derived from that of a representative compound that is either the major compound represented by this model species or that is assumed to have a similar mechanism in cases where MechGen cannot derive a mechanism for compounds of this type.

21	A highly simplified mechanism is used for emitted photoreactive species that are not well represented by other model species but which are too reactive for their reactions to be ignored.

22	The mechanisms for these model species were derived from mechanisms of compounds major compounds represented by these model species that are formed from the reactions of the compounds in the anthropogenic or biogenic emissions mixture (with each mixture weighted equally). The product compounds are weighted both by contribution of the reactants in the emissions mixture and the yields of the products when they react under standard atmospheric conditions, as discussed in the text.

23	The mechanisms for the lumped catechol are derived from the mechanisms of the catechols in the mixture of phenol, cresol, and xylenol product compounds (see above footnote).

23a	The CATL3 model species is used to represent phenols with three or more -OH's. The mechanism is assigned based on CATL reactions but simplified and assuming that all products are non-volatile.

24	MechGen is currently not capable of generating mechanisms for these types of aromatics, so an estimated simplified mechanism is used to represent them.

25	These compounds are formed in reactions of amines with ( hydrogens. MechGen is not capable of deriving mechanisms for such compounds, but it is expected that they would be rapidly hydrolyzed in the atmosphere, forming a carbonyl compound, which is the reaction assigned to this model species.

26	These are only used for non-volatile products; NVOL is used for non-volatile emissions. Molecular weights based on weighed averages of major product compounds formed from the reactions of the anthropogenic and biogenic emissions that are lumped using these species.

27	The current mechanism does not have a good way to represent inhibiting compounds (other than those lumped as TAMINS), so treating them as unreactive is less bad than representing them using a reactive species. New species would have to be added to the mechanism if such compounds become important in emissions.

28	The "NROG" model species is used to represent unreactive compounds either in emissions or which are formed as products and are not otherwise represented. Because such compounds can have a large range of carbon numbers and molecular weights, the amounts of this model species are meaningful only on a mass basis, so this model species is not assigned any carbon or nitrogen number and is given a molecular weight of unity. Simulated concentrations would be in units proportional to mass.

29	The "NVOL" model species is used to represent nonvolatile mass in "gas" emissions profiles and is not used in the gas-phase mechanism. Note that it is not used to represent nonvolatile compounds formed in the gas-phase reactions. These are represented by "RNNO3" on a molar basis if the compound is an organic nitrate and by "OTHN" on a molar basis if not. Because emitted non-volatile compounds can have a large range of carbon numbers and molecular weights, the amounts of this model species are meaningful only on a mass basis, so this model species is not assigned any carbon or nitrogen number and is given a molecular weight of unity. Simulated concentrations would be in units proportional to mass.

[c]	Molecular weights are not assigned for steady state or counter species. They should not be needed.

Table A-2.	List of reactions and documentation notes in the standard SAPRC-22 mechanisms.

| Label. | Rate Parameters [a] | Notes [b] | Reaction and Products [a] |
| --- | --- | --- | --- |
|  | k298 | A | Ea | B |  |  |
| Inorganic reactions |
| 1 | Phot Set= NO2-06 | 1 | NO2 + HV = NO + O3P |
| 2 | 5.90e-34 | 6.00e-34 | - | 2.40 | 1 | O3P + O2 + M = O3 + M |
| 3 | 7.96e-15 | 8.00e-12 | 4.094 | - | 1 | O3P + O3 = #2 O2 |
| 4 | 1.66e-12 | Falloff, F=0.60, N=1.00 | 1 | O3P + NO = NO2 |
|  | 0: | 9.00e-32 | - | -1.50 |  |  |
|  | Inf: | 3.00e-11 | - | - |  |  |
| 5 | 1.03e-11 | 5.10e-12 | -0.417 | - | 1 | O3P + NO2 = NO + O2 |
| 6 | 3.28e-12 | Falloff, F=0.60, N=1.00 | 1 | O3P + NO2 = NO3 |
|  | 0: | 2.50e-31 | - | -1.80 |  |  |
|  | Inf: | 2.20e-11 | - | -0.70 |  |  |
| 7 | 1.95e-14 | 3.00e-12 | 2.981 | - | 1 | O3 + NO = NO2 + O2 |
| 8 | 3.23e-17 | 1.20e-13 | 4.869 | - | 1 | O3 + NO2 = O2 + NO3 |
| 9 | 2.65e-11 | 1.50e-11 | -0.338 | - | 1 | NO + NO3 = #2 NO2 |
| 10 | 1.95e-38 | 3.30e-39 | -1.053 | - | 2 | NO + NO + O2 = #2 NO2 |
| 11 | 1.24e-12 | Falloff, F=0.35, N=1.33 | 2 | NO2 + NO3 = N2O5 |
|  | 0: | 3.60e-30 | - | -4.10 |  |  |
|  | Inf: | 1.90e-12 | - | 0.20 |  |  |
| 12 | 4.46e-2 | Falloff, F=0.35, N=1.33 | 2 | N2O5 = NO2 + NO3 |
|  | 0: | 1.30e-3 | - | -3.50 |  |  |
|  | Inf: | 9.70e+14 | 22.018 | 0.10 |  |  |
| 13 | - |  |  |  | 3 | N2O5 + H2O = #2 HNO3 |
| 14 | - |  |  |  | 3 | N2O5 + H2O + H2O = #2 HNO3 + H2O |
| 15 | 6.56e-16 | 4.50e-14 | 2.504 | - | 1 | NO2 + NO3 = NO + NO2 + O2 |
| 16 | Phot Set= NO3NO-06 | 1 | NO3 + HV = NO + O2 |
| 17 | Phot Set= NO3NO2-6 | 1 | NO3 + HV = NO2 + O3P |
| 18 | Phot Set= O3O1D-06 | 1 | O3 + HV = O1D + O2 |
| 19 | Phot Set= O3O3P-06 | 1 | O3 + HV = O3P + O2 |
| 20 | 1.99e-10 | 1.63e-10 | -0.119 | - | 1 | O1D + H2O = #2 OH |
| 21 | 3.69e-11 | 2.65e-11 | -0.196 | - | 4 | O1D + M = O3P + M |
| 22 | 7.41e-12 | Falloff, F=0.60, N=1.00 | 1 | OH + NO = HONO |
|  | 0: | 7.00e-31 | - | -2.60 |  |  |
|  | Inf: | 3.60e-11 | - | -0.10 |  |  |
| 23 | Phot Set= HONO-06 | 1 | HONO + HV = OH + NO |
| 24 | 4.86e-12 | 1.80e-11 | 0.775 | - | 1 | OH + HONO = H2O + NO2 |
| 25 | 9.89e-12 | Falloff, F=0.41, N=1.24 | 2 | OH + NO2 = HNO3 |
|  | 0: | 3.20e-30 | - | -4.50 |  |  |
|  | Inf: | 3.00e-11 | - | - |  |  |
| 26 | 2.20e-11 |  |  |  | 1 | OH + NO3 = HO2 + NO2 |
| 27 | 1.54e-13 | k = k0+k3M/(1+k3M/k2) | 1 | OH + HNO3 = H2O + NO3 |
|  | k0: | 2.40e-14 | -0.914 | - |  |  |
|  | k2: | 2.70e-17 | -4.370 | - |  |  |
|  | k3: | 6.50e-34 | -2.653 | - |  |  |
| 28 | Phot Set= HNO3 | 1 | HNO3 + HV = OH + NO2 |
| 29 | 7.25e-14 | 1.70e-12 | 1.868 | - | 1 | OH + O3 = HO2 + O2 |
| 30 | 8.17e-12 | 3.30e-12 | -0.537 | - | 1 | HO2 + NO = OH + NO2 |
| 31 | 4.33e-14 | k = k1 + k2 [M] | 5 | HO2 + NO = HNO3 |
|  | k1: | 2.39e-12 | 3.400 | -13.77 |  |  |
|  | k2: | 1.83e-32 | 1.534 | -4.85 |  |  |
| 32 | 2.35e-31 | 1.20e-35 | -5.850 | - | 6 | HO2 + NO + H2O = HNO3 + H2O |
| 33 | 7.50e-13 | Falloff, F=0.40, N=1.26 | 2 | HO2 + NO2 = HNO4 |
|  | 0: | 1.40e-31 | - | -3.10 |  |  |
|  | Inf: | 4.00e-12 | - | - |  |  |
| 34 | 6.20e-2 | Falloff, F=0.40, N=1.26 | 2 | HNO4 = HO2 + NO2 |
|  | 0: | 4.10e-5 | - | - |  |  |
|  | Inf: | 6.00e+15 | 22.197 | - |  |  |
| 35 | Phot Set= HNO4-06 | 1 | HNO4 + HV = #.8 {HO2 + NO2} + #.2 {OH + NO3} |
| 36 | 4.65e-12 | 1.30e-12 | -0.755 | - | 1 | HNO4 + OH = H2O + NO2 + O2 |
| 37 | 1.93e-15 | 1.00e-14 | 0.974 | - | 1 | HO2 + O3 = OH + #2 O2 |
| 38 | 2.54e-12 | k = k1 + k2 [M] | 1 | HO2 + HO2 = HO2H + O2 |
|  | k1: | 3.00e-13 | -0.914 | - |  |  |
|  | k2: | 2.10e-33 | -1.828 | - |  |  |
| 39 | 5.71e-30 | k = k1 + k2 [M] | 1 | HO2 + HO2 + H2O = HO2H + O2 + H2O |
|  | k1: | 4.20e-34 | -5.286 | - |  |  |
|  | k2: | 2.94e-54 | -6.200 | - |  |  |
| 40 | 3.50e-12 |  |  |  | 1 | NO3 + HO2 =OH + NO2 + O2 |
| 41 | 2.28e-16 | 8.50e-13 | 4.869 | - | 1 | NO3 + NO3 = #2 NO2 + O2 |
| 42 | Phot Set= H2O2 | 1 | HO2H + HV = #2 OH |
| 43 | 1.80e-12 |  |  |  | 1 | HO2H + OH = HO2 + H2O |
| 44 | 1.11e-10 | 4.80e-11 | -0.497 | - | 1 | OH + HO2 = H2O + O2 |
| 45 | 2.28e-13 | k = k1 + k2 [M] | 2 | CO + OH = HO2 + CO2 |
|  | k1: | 1.44e-13 | - | - |  |  |
|  | k2: | 3.43e-33 | - | - |  |  |
| 46 | 6.67e-15 | 2.80e-12 | 3.577 | - | 1 | H2 + OH = HO2 + H2O |
| Reactions used to compute loss processes for operators used to represent total RO2 and RCO3 radicals |
| R2NO | 9.13e-12 | 2.55e-12 | -0.755 | - | 7,8 | SumRO2 + NO = NO |
| R2H2 | 1.49e-11 |  |  |  | 8,9 | SumRO2 + HO2 = HO2 |
| R2N3 | 2.30e-12 |  |  |  | 7,8 | SumRO2 + NO3 = NO3 |
| R2R2 | 1.60e-14 |  |  |  | 8,10 | SumRO2 + SumRO2 = |
| R3N2 | 7.71e-12 | 7.70e-12 | - | -0.20 | 11,12 | SumRCO3 + NO2 = NO2 |
| R3NO | 2.10e-11 | 6.70e-12 | -0.676 | - | 11,13 | SumRCO3 + NO = NO |
| R3H2 | 2.20e-11 | 3.14e-12 | -1.153 | - | 11,14 | SumRCO3 + HO2 = HO2 |
| R3N3 | 4.00e-12 |  |  |  | 11,15 | SumRCO3 + NO3 = NO3 |
| R3R2 | 1.60e-11 | 4.40e-13 | -2.126 | - | 8,11,16 | SumRCO3 + SumRO2 = |
| R3R3 | 1.70e-11 |  |  |  | 11,17 | SumRCO3 + SumRCO3 = |
| Reactions of operator species designed to represent the net effects of reactions of peroxy radicals that are not represented explicitly. |
| 57 | Same k as rxn R2NO | 7,18 | RO2C + NO = NO2 |
| 58 | Same k as rxn R2H2 | 7,18 | RO2C + HO2 = |
| 59 | Same k as rxn R2N3 | 7,18 | RO2C + NO3 = NO2 |
| 60 | Same k as rxn R2R2 | 8,18 | RO2C + SumRO2 = SumRO2 |
| 61 | Same k as rxn R3R2 | 11,18 | RO2C + SumRCO3 = SumRCO3 |
| 62 | Same k as rxn R2NO | 7,19 | RO2XC + NO = |
| 63 | Same k as rxn R2H2 | 7,19 | RO2XC + HO2 = |
| 64 | Same k as rxn R2N3 | 7,19 | RO2XC + NO3 = NO2 |
| 65 | Same k as rxn R2R2 | 8,19 | RO2XC + SumRO2 = SumRO2 |
| 66 | Same k as rxn R3R2 | 11,19 | RO2XC + SumRCO3 = SumRCO3 |
| Manually assigned reactions of peroxy and acyl peroxy radicals |
| 67 | 7.66e-12 | 2.80e-12 | -0.596 | - | 1 | MEO2 + NO = NO2 + HCHO + HO2 |
| 68 | 5.21e-12 | 3.80e-13 | -1.550 | - | 2 | MEO2 + HO2 = #.9 MEOOH + #.1 {HCHO + H2O} + O2 |
| 69 | 1.20e-12 |  |  |  | 2 | MEO2 + NO3 = HCHO + HO2 + NO2 |
| 70 | 2.16e-13 |  |  |  | 8,20 | MEO2 + SumRO2 = #.3 HO2 + #.65 HCHO + #.35 MEOH |
| 71 | 1.07e-11 | 2.00e-12 | -0.994 | - | 11,21 | MEO2 + SumRCO3 = #.9 HO2 + HCHO |
| 72 | 9.13e-12 | 2.55e-12 | -0.755 | - | 7 | ETO2 + NO = NO2 + HO2 + MECHO |
| 73 | 7.44e-12 |  |  |  | 7 | ETO2 + HO2 = ROOH |
| 74 | 2.30e-12 |  |  |  | 7 | ETO2 + NO3 = NO2 + HO2 + MECHO |
| 75 | 2.90e-14 |  |  |  | 8,22 | ETO2 + SumRO2 = #.5 HO2 + #.25 ETOH + #.75 MECHO |
| 76 | 1.60e-11 |  |  |  | 20 | ETO2 + SumRCO3 = #.8 HO2 + MECHO |
| 77 | Same k as rxn R2NO | 7 | BZO2 + NO = NO2 + BZO |
| 78 | Same k as rxn R2H2 | 7 | BZO2 + HO2 = ROOH + O2 |
| 79 | Same k as rxn R2N3 | 7 | BZO2 + NO3 = BZO + NO2 |
| 80 | Same k as rxn R2R2 | 8,10 | BZO2 + SumRO2 = SumRO2 + BZO |
| 81 | Same k as rxn R3R2 | 11,16 | BZO2 + SumRCO3 = SumRCO3 + BZO |
| Q1NO | 2.00e-11 | 8.10e-12 | -0.537 | - | 1,23 | MECO3 + NO = NO2 + MEO2 + CO2 + SumRO2 |
| Q1N2 | 8.69e-12 | Falloff, F=0.60, N=1.00 | 1 | MECO3 + NO2 = PAN |
|  | 0: | 9.70e-29 | - | -5.60 |  |  |
|  | Inf: | 9.30e-12 | - | -1.50 |  |  |
| Q1N3 | 4.00e-12 |  | 14 | MECO3 + NO3 = NO2 + MEO2 + CO2 + SumRO2 |
| Q1H2 | 2.20e-11 |  | 15 | MECO3 + HO2 = #.13 O3 + #.5 OH + #.5 MEO2 + #.13 OACID + #.37 PACID + #.5 CO2 + #.5 SumRO2 |
| Q1R2 | 1.60e-11 |  | 16 | MECO3 + SumRO2 = #.9 MEO2 + #.1 OACID + #.9 CO2 + #.9 SumRO2 |
| Q1R3 | 1.40e-11 |  | 17 | MECO3 + SumRCO3 = MEO2 + CO2 + SumRO2 |
| Q4N2 | 1.11e-11 |  |  |  | 24 | BZCO3 + NO2 = PBZN |
| Q4NO | 1.60e-11 |  |  |  | 24,23 | BZCO3 + NO = NO2 + CO2 + BZO2 + SumRO2 |
| Q4H2 | Same k as rxn 53 | 14 | BZCO3 + HO2 = #.37 ALK5 + #.13 {O3 + ALK5} + #.5 {OH + BZO2 + CO2} + #.5 SumRO2 |
| Q4N3 | Same k as rxn R3H2 | 15 | BZCO3 + NO3 = NO2 + CO2 + BZO2 + O2 + SumRO2 |
| Q4R2 | Same k as rxn R3N3 | 8,16 | BZCO3 + SumRO2 = SumRO2 + BZO2 + CO2 + SumRO2 |
| Q4R3 | Same k as rxn R3R2 | 11,17 | BZCO3 + SumRCO3 = SumRCO3 + CO2 + BZO2 + SumRO2 |
| Manually assigned reactions of other types of radical intermediates |
| 94 | 2.24e-11 | 3.50e-12 | -1.100 | - | 25 | TBUO + NO2 = R1NO3 |
| 95 | 1.43e+3 | 1.40e+13 | 13.624 | - | 26,23 | TBUO = ACET + MEO2 + SumRO2 |
| 96 | 2.08e-12 |  |  |  | 27 | BZO + NO2 = NPHE |
| 97 | Same k as rxn R2H2 | 28 | BZO + HO2 = CRES |
| 98 | 2.86e-13 |  |  |  | 29 | BZO + O3 = BZO2 + O2 + SumRO2 |
| 99 | 1.49e-11 |  |  | 29 | BZO + BZO = |
| 100 | Same k as rxn R3N2 | 30 | NPRAD + NO2 = NPHE |
| 101 | Same k as rxn R3H2 | 30 | NPRAD + HO2 = NAPPRD |
| 102 | 1.00e-3 |  |  |  | 31 | NPRAD = NAPPRD |
| 103 | Same k as rxn R3N2 | 32 | PNAMIN + NO2 = NAMIN |
| 104 | Same k as rxn R3H2 | 32 | PNAMIN + HO2 = AMINS |
| 105 | 1.00e-3 |  |  |  | 31 | PNAMIN = AMINS |
| Reactions of stabilized Criegee ntermediates |
| G1N2 | 7.00e-12 |  |  |  | 33 | HCHO2 + NO2 = HCHO + NO3 |
| G1WA | 2.40e-15 |  |  |  | 34 | HCHO2 + H2O = HCOOH |
| G2N2 | Same k as rxn G1N2 | 35 | MECHO2 + NO2 = MECHO + NO3 |
| G2WA | Same k as rxn G1WA | 35 | MECHO2 + H2O = OACID |
| G3N2 | Same k as rxn G1N2 | 35 | RCHO2 + NO2 = RCHO + NO3 |
| G3WA | Same k as rxn G1WA | 35 | RCHO2 + H2O = OACID |
| Reactions of SO2 |
| S2OH | 9.59e-13 | Falloff, F=0.60, N=1.00 | 1 | SO2 + OH = HO2 + SULF |
| G1S2 | 3.80e-11 |  |  |  | 1,36 | HCHO2 + SO2 = SULF + HCHO |
| G2S2 | Same k as rxn G1S2 | 36 | MECHO2 + SO2 = SULF + MECHO |
| G3S2 | Same k as rxn G1S2 | 36 | RCHO2 + SO2 = SULF + RCHO |
| Reactions of explicit and lumped organic compounds assigned manually |
| C1OH | 6.34e-15 | 2.45e-12 | 3.527 | - | 1,23 | CH4 + OH = MEO2 + SumRO2 |
| 117 | Phot Set= HCHOR-13 | 37 | HCHO + HV = #2 HO2 + CO |
| 118 | Phot Set= HCHOM-13 | 37 | HCHO + HV = H2 + CO |
| 119 | 8.37e-12 | 5.50e-12 | -0.248 | - | 1 | HCHO + OH = HO2 + CO + H2O |
| 120 | 5.80e-16 |  |  |  | 1 | HCHO + NO3 = HNO3 + HO2 + CO |
| P1UI | 3.82e-4 | Falloff, F=0.60, N=1.00 | 1,23 | PAN = NO2 + MECO3 + SumRCO3 |
|  | 0: | 1.08e+0 | - | -5.60 |  |  |
|  | Inf: | 1.03e+17 | 27.821 | -1.50 |  |  |
| P1HV | Phot Set= PAN-11 | 1,23,G | PAN + HV = #.6 NO2 + #.4 NO3 + #.4 MEO2 + #.6 MECO3 + #.4 CO2 + #.4 SumRO2 + #.6 SumRCO3 |
| 123 | Phot Set= GLY-I13R | 2 | GLY + HV = #2 {CO + HO2} |
| 124 | Phot Set= GLY-I13M | 2 | GLY + HV = HCHO + CO |
| 125 | 1.15e-11 | 1.15e-11 | - | - | 1 | GLY + OH = #1.7 CO + #.7 HO2 + #.3 {OH + CO2} |
| 126 | 4.00e-16 |  |  |  | 2 | GLY + NO3 = HNO3 + #1.7 CO + #.7 HO2 + #.3 {OH + CO2} |
| BLOH | 1.20e-11 |  |  |  | 2,23 | BALD + OH = BZCO3 + SumRCO3 |
| BLHV | Phot Set= BALD-11, qy= 9.0e-2 | 38 | BALD + HV = |
| BLN3 | 4.00e-15 |  |  |  | 39,23 | BALD + NO3 = HNO3 + BZCO3 + SumRCO3 |
| PBUI | 3.18e-4 | 2.10e+16 | 27.026 | - | 24,23 | PBZN = BZCO3 + NO2 + SumRCO3 |
| PBHV | Phot Set= PPN-11 | 40,23 | PBZN + HV = #.6 {BZCO3 + NO2} + #.4 {CO2 + BZO2 + NO3} + #.4 SumRO2 + #.6 SumRCO3 |
| NPOH | 3.50e-12 |  |  |  | 41 | NPHE + OH = BZO + NO2 |
| NPHV | Phot Set= NO2-06, qy= 1.5e-3 | 42 | NPHE + HV = HONO + PHEN |
| NAOH | 2.30e-11 | 1.55e-11 | -0.233 | - | 43,23 | NAPS + OH = #.741 HO2 + #.707 CATL + #.034 RO2C + #.017 AFG2A + #.017 AFG2B + #.034 GLY + #.330 NPRAD + #.250 MACO3 + #.034 SumRO2 + #.250 SumRCO3 |
| CTOH | 5.97e-10 |  |  |  | 44 | CATL3 + OH = HO2 + OTHN |
| CTN3 | 4.86e-10 |  |  |  | 44 | CATL3 + NO3 = HNO3 + OTHN |
| PNOH | 2.00e-10 |  |  |  | 45 | NAPPRD + OH = HO2 + OTHN |
| PNN3 | 1.70e-10 |  |  |  | 45 | NAPPRD + NO3 = HNO3 + OTHN |
| 137 | Phot Set= BACL-11 | 23,46 | PHOT + HV = #2 {HO2 + RO2C + SumRO2} + ALK3 |
| 138 | 2.78e-4 |  |  |  | 47 | IMINE = MECHO |
| Reactions of reactive toxic species included for tracking purposes |
| 147 | 7.56e-12 | 2.54e-12 | -0.646 | - | 48 | CLETHE + OH = xHO2 + RO2C + xHCHO + yROOH + SumRO2 |
| 148 | 4.13e-12 |  |  |  | 48 | ACRLNT + OH = xHO2 + RO2C + xHCHO + yROOH + SumRO2 |
| 149 | 1.60e-13 | 3.50e-12 | 1.828 | - | 48 | PCE + OH = xHO2 + RO2C + yROOH + SumRO2 |
| 150 | 4.03e-13 |  |  |  | 48 | PCLBEN + OH = xHO2 + RO2C + yROOH + SumRO2 |
| 151 | 1.00e-13 | 1.80e-12 | 1.709 | - | 48 | MECL2 + OH = xHO2 + RO2C + yROOH + SumRO2 |
| 152 | 2.22e-13 | 7.69e-12 | 2.098 | - | 48 | ETBR2 + OH = xHO2 + RO2C + yROOH + SumRO2 |
| 153 | 2.40e-13 | 8.69e-12 | 2.126 | - | 48 | ETCL2 + OH = xHO2 + RO2C + yROOH + SumRO2 |
| 154 | 9.21e-14 | 1.63e-12 | 1.701 | - | 48 | ETOX + OH = xHO2 + RO2C + yROOH + SumRO2 |
| 155 | 1.04e-13 | 1.80e-12 | 1.689 | - | 48 | CHCL3 + OH = xHO2 + RO2C + yROOH + SumRO2 |
| Operator reactions representing the formation of individual products formed in peroxy radical reactions [c] |
|  | Same k as rxn R2NO | 7,49 | x(Spec) + NO = NO + (Spec) |
|  | Same k as rxn R2H2 | 7,49 | x(Spec) + HO2 = HO2 |
|  | Same k as rxn R2N3 | 7,49 | x(Spec) + NO3 = NO3 + (Spec) |
|  | Same k as rxn R2R2 | 8,49 | x(Spec) + SumRO2 = SumRO2 + #.5 (Spec) |
|  | Same k as rxn R3R2 | 11,49 | x(Spec) + SumRCO3 = SumRCO3 + (Spec) |
|  | Same k as rxn R2NO | 7,50 | y(Spec) + NO = NO |
|  | Same k as rxn R2H2 | 7,50 | y(Spec) + HO2 = HO2 + (Spec) |
|  | Same k as rxn R2N3 | 7,50 | y(Spec) + NO3 = NO3 |
|  | Same k as rxn R2R2 | 8,50 | y(Spec) + SumRO2 = SumRO2 + #.5 (Spec-2) |
|  | Same k as rxn R3R2 | 11,50 | y(Spec) + SumRCO3 = SumRCO3 |
|  | Same k as rxn R2NO | 7,51 | z(Spec) + NO = NO + (Spec) |
|  | Same k as rxn R2H2 | 7,51 | z(Spec) + HO2 = HO2 |
|  | Same k as rxn R2N3 | 7,51 | z(Spec) + NO3 = NO3 + (Spec-2) + HO2 |
|  | Same k as rxn R2R2 | 8,51 | z(Spec) + SumRO2 = SumRO2 + #.5 (Spec-2) + #.5 HO2 |
|  | Same k as rxn R3R2 | 11,51 | z(Spec) + SumRCO3 = SumRCO3 + (Spec-2) + HO2 |
| Reactions of lumped radicals imported directly from MechGen [d] |
| Q2NO | 2.10e-11 | 6.70e-12 | -0.676 | - | 52 | R2CO3 + NO = NO2 + #.95 xHO2 + #.96 RO2C + #.04 RO2XC + #.95 xETCHO + #.04 zR1NO3 + CO2 + yROOH + SumRO2 |
| Q2N2 | 7.70e-12 |  | 52 | R2CO3 + NO2 = PAN2 |
| Q2N3 | 4.00e-12 |  | 52 | R2CO3 + NO3 = NO2 + #.95 xHO2 + #.96 RO2C + #.04 RO2XC + #.95 xETCHO + #.04 zR1NO3 + CO2 + yROOH + SumRO2 |
| Q2H2 | 2.20e-11 |  | 52 | R2CO3 + HO2 = #.13 O3 + #.5 OH + #.48 xHO2 + #.48 RO2C + #.02 RO2XC + #.48 xETCHO + #.13 OACID + #.37 PACID + #.02 zR1NO3 + #.5 CO2 + #.5 yROOH + #.5 SumRO2 |
| Q2R2 | 1.44e-11 |  | 52 | R2CO3 + SumRO2 = #.95 xHO2 + #.96 RO2C + #.04 RO2XC + #.95 xETCHO + #.04 zR1NO3 + CO2 + yROOH + SumRO2 |
| Q5UI | 3.98e+1 | 7.79e+8 | 9.942 | - | 52 | MACO3 = #.93 xHO2 + #.93 RO2C + #.07 RO2XC + #.93 xPACID + #.07 zRCNO3 + SumRO2 |
| Q5NO | 2.10e-11 | 6.70e-12 | -0.676 | - | 52 | MACO3 + NO = NO2 + MEO2 + HCHO + CO + CO2 + SumRO2 |
| Q5N2 | 7.70e-12 |  | 52 | MACO3 + NO2 = APANS |
| Reactions of explicitly represented VOCs or intermediates imported directly from MechGen [d] |
| C2OH | 2.49e-13 | 1.51e-12 | 1.059 | 1.92 | 48 | ETHAN + OH = ETO2 + SumRO2 |
| C3OH | 1.11e-12 | 2.00e-12 | 0.342 | 1.76 | 48 | PROP + OH = #.95 xHO2 + #.01 xMEO2 + #.96 RO2C + #.04 RO2XC + #.01 xMECHO + #.27 xETCHO + #.68 xACET + #.04 zR1NO3 + yROOH + SumRO2 |
| C4OH | 2.38e-12 | 2.09e-12 | -0.083 | 1.82 | 48 | NC4 + OH = #.59 xHO2 + #.33 xETO2 + #1.02 RO2C + #.08 RO2XC + #.33 xMECHO + #.12 xRCHO + #.48 xMEK + #.07 zR1NO3 + #.01 zRHNO3 + #1.1 yROOH + #1.1 SumRO2 |
| E1OH | 7.90e-12 | Falloff, F=0.60, N=1.00 | 48 | ETHEN + OH = xHO2 + RO2C + #1.48 xHCHO + #.26 xGLCHO + yROOH + SumRO2 |
|  | 0: | 1.10E-28 | - | -3.5 | 53 |  |
|  | Inf: | 8.40E-12 | - | -1.75 | 53 |  |
| E1O3 | 1.55e-18 | 6.82e-15 | 4.968 | - | 48 | ETHEN + O3 = #.17 OH + #.27 HO2 + #.42 HCHO2 + HCHO + #.18 H2 + #.35 CO + #.23 CO2 |
| E1N3 | 2.10e-16 | 3.30e-12 | 5.723 | - | 48 | ETHEN + NO3 = #.01 xNO2 + #.99 xHO2 + RO2C + #.01 xHCHO + #.99 xRCNO3 + yRPNO3 + SumRO2 |
| E1OP | 7.30e-13 | 1.07e-11 | 1.590 | - | 54 | ETHEN + O3P = #1.09 HO2 + #.51 MEO2 + #.1 MECHO + #.51 CO + #4.41 NROG + #.51 SumRO2 |
| E2OH | 2.44e-11 | 1.20e-11 | -0.417 | -0.62 | 48 | PROPE + OH = #.97 xHO2 + #.97 RO2C + #.03 RO2XC + #.97 xHCHO + #.97 xMECHO + #.03 zRHNO3 + yROOH + SumRO2 |
| E2O3 | 1.05e-17 | 5.77e-15 | 3.736 | - | 48 | PROPE + O3 = PROPE_O3 + #.3 OH + #.17 HO2 + #.16 xHO2 + #.03 MEO2 + #.21 HCHO2 + #.12 MECHO2 + #.22 RO2C + #.5 HCHO + #.05 xHCHO + #.05 MEOH + #.5 MECHO + #.09 H2 + #.22 CO + #.24 CO2 + #.09 CH4 + #.25 SumRO2 |
| 492 | 2.45e+0 |  | 53 | PROPE_O3 = #.05 xOH + #.16 xPACID + #.05 CO2 |
| 493 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | PROPE_O3 + NO = NO + #.06 xHO2 + #.15 xHCHO + #.2 CO + #.18 yHPCRB |
| E2N3 | 9.54e-15 | 4.60e-13 | 2.295 | - | 48 | PROPE + NO3 = #.29 xNO2 + #.68 xHO2 + #.97 RO2C + #.03 RO2XC + #.29 xHCHO + #.29 xMECHO + #.68 xRCNO3 + #.03 zRDNO3 + yRPNO3 + SumRO2 |
| E2OP | 3.99e-12 | 1.02e-11 | 0.556 | - | 54 | PROPE + O3P = #.25 ETCHO + #.25 ACET + #.5 ALK2 |
| IPOH | 9.99e-11 | 2.70e-11 | -0.775 | - | 48 | ISOP + OH = ISOP_OH + #.57 xHO2 + #.55 RO2C + #.05 RO2XC + #.5 xHCHO + #.23 xMACR + #.27 xMVK + #.05 zRHNO3 + #.05 xFURNS + #.6 yRUOOH + #.6 SumRO2 |
| 497 | 1.31e+0 |  | 53 | ISOP_OH = #.06 xOH + #.32 HO2 + #.31 HPCRB + #.06 xHPCRB |
| 498 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | ISOP_OH + NO = NO + #.33 xHO2 + #.38 RO2C + #.05 RO2XC + #.03 xHCHO + #.34 xOLEA1 + #.05 zRHNO3 + #.42 yRUOOH + #.43 SumRO2 |
| IPO3 | 1.28e-17 | 1.05e-14 | 3.974 | - | 48 | ISOP + O3 = #.13 OH + #.62 HO2 + #.16 MECO3 + #.23 HCHO2 + #.06 RCHO2 + #.4 HCHO + #.39 MACR + #.16 MVK + #.05 OLEP + #.1 H2 + #.33 CO + #.13 CO2 + #.16 SumRCO3 |
| IPN3 | 6.52e-13 | 2.95e-12 | 0.894 | - | 48 | ISOP + NO3 = ISOP_N3 + #.71 xNO2 + #.07 xHO2 + #.91 RO2C + #.1 RO2XC + #.49 xHCHO + #.22 xOLEA1 + #.48 xMVK + #.04 xRCNO3 + #.1 zRDNO3 + yRPNO3 + #1.01 SumRO2 |
| 501 | 1.07e+0 |  | 53 | ISOP_N3 = #.11 xNO2 + #.04 xRPNO3 + #.12 xHPCRB |
| 502 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | ISOP_N3 + NO = NO + #.11 xHO2 + #.14 RO2C + #.01 RO2XC + #.09 xHCHO + #.05 xRHNO3 + #.09 xRCNO3 + #.01 zRDNO3 + #.11 yRPNO3 + #.15 SumRO2 |
| IPOP | 3.50e-11 |  | 54 | ISOP + O3P = #.25 HO2 + #.25 MEO2 + #.75 OLEP + #.25 SumRO2 |
| E3OH | 6.63e-11 | 1.12e-11 | -1.053 | - | 48 | BUT13 + OH = BUT13_OH + #.63 xHO2 + #.66 RO2C + #.04 RO2XC + #.61 xHCHO + #.58 xACRO + #.02 xOLEA1 + #.04 zRHNO3 + #.05 xFURNS + #.69 yRUOOH + #.7 SumRO2 |
| 505 | 1.17e+0 |  | 53 | BUT13_OH = #.02 xOH + #.31 HO2 + #.31 HPCRB |
| 506 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | BUT13_OH + NO = NO + #.31 xHO2 + #.3 RO2C + #.02 RO2XC + #.29 xOLEA1 + #.02 zRHNO3 + #.33 yRUOOH + #.32 SumRO2 |
| E3O3 | 6.31e-18 | 1.34e-14 | 4.537 | - | 48 | BUT13 + O3 = BUT13_O3 + #.08 OH + #.5 HO2 + #.27 xHO2 + #.21 HCHO2 + #.14 RCHO2 + #.36 RO2C + #.5 HCHO + #.09 xHCHO + #.5 ACRO + #.09 H2 + #.54 CO + #.12 CO2 + #.36 SumRO2 |
| 508 | 2.63e+0 |  | 53 | BUT13_O3 = #.09 xOH + #.27 xPACID + #.09 CO2 |
| 509 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | BUT13_O3 + NO = NO + #.09 xHO2 + #.25 xHCHO + #.02 xGLY + #.33 CO + #.3 yHPCRB |
| E3N3 | 1.10e-13 |  | 48 | BUT13 + NO3 = #.89 xNO2 + #.06 xHO2 + #.94 RO2C + #.06 RO2XC + #.74 xHCHO + #.74 xACRO + #.14 xOLEA1 + #.06 xRCNO3 + #.06 zRDNO3 + yRPNO3 + SumRO2 |
| E3OP | 1.98e-11 | 2.26e-11 | 0.079 | - | 54 | BUT13 + O3P = #.25 OLEA2 + #.25 MVK + #.5 OLEP |
| APOH | 5.31e-11 | 1.34e-11 | -0.815 | - | 48 | APINE + OH = APINE_OH + #.01 HO2 + #.67 xHO2 + #1.05 RO2C + #.29 RO2XC + #.08 xHCHO + #.51 xRCHO + #.08 xOLEA2 + #.17 xACET + #.06 xMVK + #.03 xLVKS + #.01 zR2NO3 + #.28 zRHNO3 + #.02 xHPCRB + #.53 yROOH + #.7 yRUOOH + #.12 yHPCRB + #1.34 SumRO2 |
| 513 | 3.93e+0 |  | 53 | APINE_OH = #.01 xOH + #.07 xHPCRB |
| 514 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | APINE_OH + NO = NO + #.07 RO2C + #.02 RO2XC + #.01 xHCHO + #.06 xOLEA2 + #.02 zRHNO3 + #.09 yHPCRB + #.09 SumRO2 |
| APO3 | 9.59e-17 | 8.22e-16 | 1.272 | - | 48 | APINE + O3 = #.68 OH + #.03 xOH + #.01 HO2 + #.16 xHO2 + #.03 xMECO3 + #.2 xR2CO3 + #.29 RCHO2 + #.79 RO2C + #.26 RO2XC + #.2 xHCHO + #.15 xRCHO + #.09 xACET + #.03 KET2 + #.03 xBACL + #.07 xPACID + #.26 zRCNO3 + #.17 CO + #.03 CO2 + #.81 yHPCRB + #1.05 SumRO2 |
| APN3 | 6.22e-12 | 1.20e-12 | -0.974 | - | 48 | APINE + NO3 = #.81 xNO2 + #.81 RO2C + #.19 RO2XC + #.81 xRCHO + #.19 zRDNO3 + yRPNO3 + SumRO2 |
| APOP | 3.20e-11 |  | 54 | APINE + O3P = #.5 KET2 + #.5 ALK4 |
| BPOH | 7.58e-11 | 1.62e-11 | -0.914 | - | 48 | BPINE + OH = BPINE_OH + #.01 xOH + #.49 xHO2 + #.03 xR2CO3 + #1.45 RO2C + #.43 RO2XC + #.35 xHCHO + #.03 xRCHO + #.23 xOLEA2 + #.29 xACET + #.11 xKET2 + #.02 xPACID + #.02 zR2NO3 + #.31 zRHNO3 + #.09 zRCNO3 + #.02 xHPCRB + #.32 yROOH + yRUOOH + #.47 yHPCRB + #1.88 SumRO2 |
| 519 | 3.45e+0 |  | 53 | BPINE_OH = #.04 xOH + #.01 HO2 + #.04 xPACID + #.1 xHPCRB + #.01 CO2 |
| 520 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | BPINE_OH + NO = NO + #.13 RO2C + #.03 RO2XC + #.02 xHCHO + #.01 xRCHO + #.08 xOLEA2 + #.03 zRHNO3 + #.01 zRCNO3 + #.01 yRUOOH + #.19 yHPCRB + #.16 SumRO2 |
| BPO3 | 1.89e-17 | 1.39e-15 | 2.544 | - | 48 | BPINE + O3 = #.39 OH + #.19 HO2 + #.19 xR2CO3 + #.21 HCHO2 + #.2 RCHO2 + #.19 RO2C + #.06 RO2XC + #.5 HCHO + #.5 KET2 + #.06 zRCNO3 + #.09 H2 + #.17 CO + #.12 CO2 + #.21 yHPCRB + #.25 SumRO2 |
| BPN3 | 2.50e-12 |  | 48 | BPINE + NO3 = #.06 xOH + #.18 xHO2 + #.14 xR2CO3 + #2.25 RO2C + #.63 RO2XC + #.04 xHCHO + #.02 xRCHO + #.27 xACET + #.14 xPACID + #.23 xRCNO3 + #.43 zRCNO3 + #.19 zRDNO3 + #.04 CO2 + yRPNO3 + #2.88 SumRO2 |
| BPOP | 2.70e-11 |  | 54 | BPINE + O3P = #.5 RCHO + #.5 ALK5 |
| ACOH | 7.47e-13 | Falloff, F=0.60, N=1.00 | 1 | ACETL + OH = #.67 OH + #.33 HO2 + #.33 HCOOH + #.67 GLY + #.33 CO |
|  | 0: | 5.50E-30 | - | - |  |  |
|  | Inf: | 8.30E-13 | - | 2 |  |  |
| ACO3 | 1.00e-20 |  | 48 | ACETL + O3 = #.26 HO2 + #.34 RCHO2 + #.34 HCHO + #.18 HCOOH + #.31 CO + #.47 CO2 |
| BZOH | 1.21e-12 | 2.30e-12 | 0.378 | - | 48 | BENZ + OH = #.69 HO2 + #.28 xHO2 + #.28 RO2C + #.04 RO2XC + #.28 xGLY + #.12 OLEA2 + #.57 PHEN + #.28 xBUDAL + #.04 zRANO3 + #.31 yRAOOH + #.32 SumRO2 |
| TLOH | 5.64e-12 | 1.80e-12 | -0.676 | - | 48 | TOLU + OH = #.41 HO2 + #.5 xHO2 + #.5 RO2C + #.08 RO2XC + #.22 xGLY + #.22 xMGLY + #.01 OLEA1 + #.2 OLEA2 + #.19 CRES + #.06 xBALD + #.22 xBUDAL + #.02 xAFG1 + #.19 xAFG2A + #.01 zR1NO3 + #.07 zRANO3 + #.08 yROOH + #.51 yRAOOH + #.58 SumRO2 |
| OXOH | 1.36e-11 |  | 48 | OXYL + OH = #.35 HO2 + #.54 xHO2 + #.54 RO2C + #.11 RO2XC + #.12 xGLY + #.22 xMGLY + #.1 OLEA1 + #.1 OLEA2 + #.06 LVKS + #.15 xBACL + #.08 XYNL + #.06 xBALD + #.15 xBUDAL + #.01 xAFG1 + #.22 xAFG2A + #.11 xAFG2B + #.02 zR2NO3 + #.09 zRANO3 + #.08 yROOH + #.57 yRAOOH + #.65 SumRO2 |
| MXOH | 2.31e-11 |  | 48 | MXYL + OH = #.21 HO2 + #.66 xHO2 + #.66 RO2C + #.13 RO2XC + #.04 xGLY + #.59 xMGLY + #.13 OLEA2 + #.07 XYNL + #.03 xBALD + #.05 xAFG1 + #.58 xAFG2A + #.01 zR2NO3 + #.12 zRANO3 + #.03 yROOH + #.75 yRAOOH + #.79 SumRO2 |
| PXOH | 1.21e-11 | 4.14e-12 | -0.634 | - | 48 | PXYL + OH = #.38 HO2 + #.52 xHO2 + #.52 RO2C + #.11 RO2XC + #.16 xGLY + #.29 xMGLY + #.02 OLEA1 + #.23 OLEA2 + #.14 XYNL + #.07 xBALD + #.29 xAFG1 + #.16 xAFG3 + #.02 zR2NO3 + #.09 zRANO3 + #.09 yROOH + #.53 yRAOOH + #.63 SumRO2 |
| X1OH | 3.27e-11 |  | 48 | BZ123 + OH = #.18 HO2 + #.67 xHO2 + #.67 RO2C + #.15 RO2XC + #.03 xGLY + #.07 xMGLY + #.03 OLEA1 + #.03 OLEA2 + #.1 LVKS + #.54 xBACL + #.02 XYNL + #.02 xBALD + #.54 xAFG2A + #.1 xAFG2B + #.01 zR2NO3 + #.14 zRANO3 + #.03 yROOH + #.78 yRAOOH + #.82 SumRO2 |
| X2OH | 3.25e-11 |  | 48 | BZ124 + OH = #.23 HO2 + #.63 xHO2 + #.63 RO2C + #.14 RO2XC + #.03 xGLY + #.51 xMGLY + #.04 OLEA1 + #.11 OLEA2 + #.02 LVKS + #.06 xBACL + #.05 XYNL + #.03 xBALD + #.08 xAFG1 + #.04 xAFG2A + #.27 xAFG2B + #.21 xAFG3 + #.01 zR2NO3 + #.13 zRANO3 + #.04 yROOH + #.73 yRAOOH + #.77 SumRO2 |
| X3OH | 5.86e-11 |  | 48 | BZ135 + OH = #.17 HO2 + #.68 xHO2 + #.68 RO2C + #.15 RO2XC + #.67 xMGLY + #.11 OLEA2 + #.05 XYNL + #.02 xBALD + #.67 xAFG2A + #.01 zR2NO3 + #.15 zRANO3 + #.02 yROOH + #.81 yRAOOH + #.83 SumRO2 |
| EBOH | 7.00e-12 |  | 48 | C2BEN + OH = #.36 HO2 + #.51 xHO2 + #.01 xMEO2 + #.54 RO2C + #.12 RO2XC + #.02 xHCHO + #.18 xGLY + #.18 xMGLY + #.01 OLEA1 + #.17 OLEA2 + #.16 XYNL + #.03 xBALD + #.18 xBUDAL + #.02 xAFG1 + #.16 xAFG2A + #.05 zR2NO3 + #.07 zRANO3 + #.13 xBENX + #.23 yROOH + #.44 yRAOOH + #.66 SumRO2 |
| MTOH | 3.09e-12 | 1.87e-13 | -1.675 | 3.34 | 48 | MTBE + OH = #.72 xHO2 + #.19 xMEO2 + #1.12 RO2C + #.09 RO2XC + #.2 xHCHO + #.09 zR1NO3 + #.17 ALK1 + #.72 ALK2 + #.01 ALK3 + #.89 yROOH + #1.21 SumRO2 |
| MLOH | 8.78e-13 | 2.32e-13 | -0.799 | 2.72 | 48 | MEOH + OH = HO2 + HCHO |
| FAOH | 4.50e-13 |  | 48 | HCOOH + OH = HO2 + CO2 |
| H1OH | 1.00e-11 | 5.30e-12 | -0.378 | - | 48 | MEOOH + OH = #.03 OH + #.97 MEO2 + #.03 HCHO + #.97 SumRO2 |
| H1HV | Phot Set= COOH | 55 | MEOOH + HV = OH + HO2 + HCHO |
| A2OH | 1.49e-11 | 2.40e-12 | -1.085 | 0.77 | 48 | MECHO + OH = #.01 xOH + #.04 xHO2 + #.95 MECO3 + #.05 RO2C + #.02 xHCHO + #.03 xPACID + #.01 CO + #.01 CO2 + #.01 yHPCRB + #.05 SumRO2 + #.95 SumRCO3 |
| A2N3 | 2.73e-15 | 1.40e-12 | 3.696 | - | 48 | MECHO + NO3 = HNO3 + MECO3 + SumRCO3 |
| A2HV | Phot Set= CCHOR-13 | 56 | MECHO + HV = HO2 + #.9 MEO2 + #.1 MECO3 + #.9 CO + #.9 SumRO2 + #.1 SumRCO3 |
| EAOH | 3.32e-12 | 4.42e-13 | -1.204 | 2.29 | 48 | ETOH + OH = #.95 HO2 + #.05 xHO2 + #.05 RO2C + #.07 xHCHO + #.95 MECHO + #.01 xGLCHO + #.05 yROOH + #.05 SumRO2 |
| GAOH | 1.10e-11 |  | 48 | GLCHO + OH = #.2 HO2 + #.8 R2CO3 + #.2 GLY + #.8 SumRCO3 |
| GAN3 | 1.84e-14 |  | 48 | GLCHO + NO3 = HNO3 + #.1 HO2 + #.9 R2CO3 + #.1 GLY + #.9 SumRCO3 |
| GAHV | Phot Set= GLALD-14 | 57 | GLCHO + HV = #.07 OH + #.01 xOH + #1.66 HO2 + #.06 xHO2 + #.07 RO2C + #.83 HCHO + #.03 xHCHO + #.1 MEOH + #.04 xPACID + #.95 CO + #.01 CO2 + #.02 yHPCRB + #.07 SumRO2 |
| A3OH | 1.99e-11 | 6.63e-13 | -2.023 | 1.99 | 48 | ETCHO + OH = #.04 xHO2 + #.96 R2CO3 + #.04 RO2C + #.04 xMECHO + #.01 xPACID + #.04 CO + #.03 yHPCRB + #.04 SumRO2 + #.96 SumRCO3 |
| A3N3 | 6.30e-15 |  | 48 | ETCHO + NO3 = HNO3 + R2CO3 + SumRCO3 |
| A3HV | Phot Set= C2CHOabs | 58 | ETCHO + HV = HO2 + ETO2 + CO + SumRO2 |
| AROH | 2.17e-11 | 7.10e-12 | -0.662 | - | 48 | ACRO + OH = ACRO_OH + #.31 xHO2 + #.68 MACO3 + #.31 RO2C + #.01 RO2XC + #.07 xHCHO + #.24 xGLCHO + #.01 xGLY + #.01 zRHNO3 + #.24 CO + #.22 yHPCRB + #.32 SumRO2 + #.68 SumRCO3 |
| 551 | 1.12e+0 |  | 53 | ACRO_OH = #.06 xPACID |
| 552 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | ACRO_OH + NO = NO + #.06 xGLY + #.06 yHPCRB |
| ARO3 | 2.80e-19 |  | 48 | ACRO + O3 = #.15 OH + #.27 HO2 + #.38 HCHO2 + #.03 RCHO2 + #.13 HCHO + #.02 HCOOH + #.9 GLY + #.16 H2 + #.34 CO + #.26 CO2 |
| ARN3 | 1.10e-15 |  | 48 | ACRO + NO3 = #.94 HNO3 + #.06 xHO2 + #.94 MACO3 + #.06 RO2C + #.06 xRCNO3 + #.06 CO + #.05 yRPNO3 + #.06 SumRO2 + #.94 SumRCO3 |
| ARHV | Phot Set= ACROL-16 | 59 | ACRO + HV = ACRO_HV + #.22 OH + #.49 HO2 + #.17 xHO2 + #.05 MEO2 + #.15 MACO3 + #.22 RO2C + #.15 HCHO + #.06 xHCHO + #.06 MEOH + #1.06 CO + #.16 CO2 + #.12 CH4 + #.25 ETHEN + #.27 SumRO2 + #.15 SumRCO3 |
| 556 | 2.46e+0 |  | 53 | ACRO_HV = #.06 xOH + #.17 xPACID + #.06 CO2 |
| 557 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | ACRO_HV + NO = NO + #.05 xHO2 + #.15 xHCHO + #.21 CO + #.19 yHPCRB |
| K3OH | 1.87e-13 | 1.97e-14 | -1.347 | 3.88 | 48 | ACET + OH = #.96 xMECO3 + #.96 RO2C + #.04 RO2XC + #.96 xHCHO + #.04 zRCNO3 + #.85 yHPCRB + SumRO2 |
| K3HV | Phot Set= ACET-06 | 56 | ACET + HV = MEO2 + MECO3 + SumRO2 + SumRCO3 |
| K4OH | 1.05e-12 | 5.42e-14 | -1.767 | 3.57 | 48 | MEK + OH = #.29 xHO2 + #.55 xMECO3 + #.08 xR2CO3 + #.94 RO2C + #.07 RO2XC + #.11 xHCHO + #.54 xMECHO + #.29 xRCHO + #.07 zRCNO3 + #.91 yHPCRB + #1.01 SumRO2 |
| K4HV | Phot Set= MEK-06, qy= 1.75e-1 | 60 | MEK + HV = #.15 MEO2 + #.85 ETO2 + #.85 MECO3 + #.15 R2CO3 + SumRO2 + SumRCO3 |
| MAOH | 2.86e-11 | 8.00e-12 | -0.755 | - | 48 | MACR + OH = MACR_OH + #.05 xHO2 + #.21 MACO3 + #.75 RO2C + #.04 RO2XC + #.05 xHCHO + #.61 xKET2 + #.79 SumRO2 + #.21 SumRCO3 |
| 563 | 5.55e-1 |  | 53 | MACR_OH = #.69 xOH + #.08 xKET2 + #.05 xPACID + #.04 zRCNO3 + #.69 CO2 |
| 564 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | MACR_OH + NO = NO + #.69 xHO2 + #.09 xHCHO + #.14 xMGLY + #.04 zRHNO3 + #.61 CO + #.68 yHPCRB |
| MAO3 | 1.22e-18 | 1.40e-15 | 4.173 | - | 48 | MACR + O3 = #.19 OH + #.01 xOH + #.25 HO2 + #.03 xHO2 + #.01 MECO3 + #.38 HCHO2 + #.03 RCHO2 + #.04 RO2C + #.1 HCHO + #.02 xHCHO + #.02 MECHO + #.9 MGLY + #.01 OACID + #.02 xPACID + #.16 H2 + #.38 CO + #.24 CO2 + #.01 yHPCRB + #.04 SumRO2 + #.01 SumRCO3 |
| MAN3 | 3.40e-15 |  | 48 | MACR + NO3 = MACR_N3 + #.3 HNO3 + #.3 MACO3 + #.66 RO2C + #.04 RO2XC + #.66 xRCNO3 + #.7 SumRO2 + #.3 SumRCO3 |
| 567 | 5.24e-1 |  | 53 | MACR_N3 = #.66 xOH + #.04 zRCNO3 + #.66 CO2 |
| 568 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | MACR_N3 + NO = NO + #.66 xHO2 + #.04 zRDNO3 + #.66 CO + #.59 yRPNO3 |
| MAHV | Phot Set= MACR-06 | 61 | MACR + HV = #.45 OH + #.3 HO2 + #.15 MEO2 + #.43 xMECO3 + #.15 MACO3 + #.43 RO2C + #.02 RO2XC + #.15 HCHO + #.43 xHCHO + #.02 zRCNO3 + CO + #.25 PROPE + #.38 yHPCRB + #.6 SumRO2 + #.15 SumRCO3 |
| MVOH | 2.01e-11 | 2.60e-12 | -1.212 | - | 48 | MVK + OH = #.28 xHO2 + #.66 xMECO3 + #.95 RO2C + #.05 RO2XC + #.28 xHCHO + #.66 xGLCHO + #.28 xMGLY + #.05 zRCNO3 + #.9 yHPCRB + SumRO2 |
| MVO3 | 5.17e-18 | 8.50e-16 | 3.021 | - | 48 | MVK + O3 = #.18 OH + #.26 HO2 + #.02 xHO2 + #.4 HCHO2 + #.01 RCHO2 + #.02 RO2C + #.05 HCHO + #.01 xHCHO + #.01 MECHO + #.95 MGLY + #.01 xPACID + #.17 H2 + #.36 CO + #.23 CO2 + #.01 yHPCRB + #.02 SumRO2 |
| MVHV | Phot Set= MVK-16 | 56 | MVK + HV = #.4 MEO2 + #.4 MACO3 + #.6 CO + #.6 PROPE + #.4 SumRO2 + #.4 SumRCO3 |
| F1OH | 5.29e-11 |  | 48 | BUDAL + OH = BUDAL_OH + #.29 OH + #.44 xHO2 + #.44 RO2C + #.02 RO2XC + #.41 xGLY + #.05 xPACID + #.02 CO + #.29 MALAH + #.46 SumRO2 |
| 574 | 2.08e+1 |  | 53 | BUDAL_OH = #.25 OH + #.39 xPACID + #.02 zRCNO3 + #.25 MALAH |
| 575 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | BUDAL_OH + NO = NO + #.25 xHO2 + #.25 RO2C + #.62 xGLY + #.25 CO + #.35 yHPCRB + #.25 SumRO2 |
| F1HV | Phot Set= AFGS, qy= 2.50e-1 | 62 | BUDAL + HV = OH + HO2 + MALAH |
| PHOH | 2.82e-11 | 4.70e-13 | -2.424 | - | 48 | PHEN + OH = #.85 HO2 + #.07 xHO2 + #.07 BZO + #.07 RO2C + #.01 RO2XC + #.03 xGLY + #.04 xMGLY + #.01 OLEA1 + #.04 OLEA2 + #.03 OLEP + #.77 CATL + #.04 xBUDAL + #.01 xAFG1 + #.02 xAFG2A + #.01 zRANO3 + #.08 yRAOOH + #.08 SumRO2 |
| PHN3 | 4.50e-12 |  | 48 | PHEN + NO3 = HNO3 + BZO |
| Reactions of lumped emitted and product VOCs imported directly from MechGen [d, e] |
| L1OH | 3.35e-13 |  | G | ALK1 + OH = #.96 xHO2 + #.01 xMECO3 + #.97 RO2C + #.03 RO2XC + #.01 xHCHO + #.09 xMGLY + #.43 xOACID + #.03 zRCNO3 + #.43 CO + #39.33 NROG + #.62 yHPCRB + SumRO2 |
| L2OH | 1.67e-12 |  | G | ALK2 + OH = #.1 xHO2 + #.01 xMEO2 + #.84 xMECO3 + #.95 RO2C + #.05 RO2XC + #.01 xHCHO + #.08 xRCHO + #.01 xMGLY + #.84 xOACID + #.05 zRCNO3 + #1.38 NROG + #.64 yHPCRB + SumRO2 |
| L3OH | 2.85e-12 |  | G | ALK3 + OH = #.34 xHO2 + #.14 xETO2 + #.07 xR2CO3 + #.33 xTBUO + #1.2 RO2C + #.12 RO2XC + #.1 xHCHO + #.1 xMECHO + #.09 xRCHO + #.07 xACET + #.01 xKET2 + #.12 xOACID + #.06 zR1NO3 + #.02 zRHNO3 + #.03 zRCNO3 + #.05 CO + #.12 ALK1 + #16.91 NROG + #.81 yROOH + #.33 yHPCRB + #1.32 SumRO2 |
| L4OH | 4.54e-12 |  | G | ALK4 + OH = #.01 xOH + #.26 HO2 + #.37 xHO2 + #.23 xETO2 + #.96 RO2C + #.12 RO2XC + #.05 xHCHO + #.12 xMECHO + #.05 xETCHO + #.07 xRCHO + #.26 ACET + #.3 xACET + #.03 xMEK + #.15 xKET2 + #.09 zR1NO3 + #.03 zRHNO3 + #.01 CO2 + #1.05 yROOH + #.01 yHPCRB + #1.08 SumRO2 |
| L5OH | 1.14e-11 |  | G | ALK5 + OH = ALK5_OH + #.3 HO2 + #.39 xHO2 + #.02 xETO2 + #.01 xR2CO3 + RO2C + #.22 RO2XC + #.01 HCHO + #.03 xHCHO + #.04 xMECHO + #.02 xETCHO + #.06 GLCHO + #.01 xGLCHO + #.1 RCHO + #.04 xRCHO + #.05 xACET + #.05 xMEK + #.13 KET2 + #.23 xKET2 + #.01 xPACID + #.08 zR1NO3 + #.05 zR2NO3 + #.06 zRHNO3 + #.02 zRCNO3 + #.01 ALK4 + #.01 ALK5 + #1.05 yROOH + #.12 yHPCRB + #1.22 SumRO2 |
| 584 | 6.87e-1 |  | 53 | ALK5_OH = #.02 HO2 + #.03 xHO2 + #.03 xPACID + #.06 xHPCRB |
| 585 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | ALK5_OH + NO = NO + #.02 xMECO3 + #.02 xR2CO3 + #.1 RO2C + #.02 RO2XC + #.01 xETCHO + #.06 xRCHO + #.01 xACET + #.01 zRHNO3 + #.01 zRCNO3 + #.01 CO + #.01 ALK5 + #.05 yROOH + #.09 yHPCRB + #.12 SumRO2 |
| L6OH | 1.69e-11 |  | G | ALK6 + OH = #.16 HO2 + #.46 xHO2 + #.01 xMEO2 + #.02 xR2CO3 + #1.09 RO2C + #.35 RO2XC + #.09 xHCHO + #.01 xMECHO + #.01 xETCHO + #.07 RCHO + #.09 xRCHO + #.2 xACET + #.09 KET2 + #.27 xKET2 + #.01 xPACID + #.15 zR2NO3 + #.12 zRHNO3 + #.08 zRCNO3 + #.01 xHPCRB + #.03 ALK2 + #.06 ALK3 + #.01 ALK4 + #.02 ALK5 + #1.05 yROOH + #.34 yHPCRB + #1.44 SumRO2 |
| O1OH | 3.18e-11 |  | G | OLE1 + OH = #.78 xHO2 + #.01 xMEO2 + #.11 xTBUO + #1.12 RO2C + #.1 RO2XC + #.69 xHCHO + #.01 xMECHO + #.35 xETCHO + #.15 xGLCHO + #.35 xRCHO + #.02 xACRO + #.03 xACET + #.02 xKET2 + #.01 xMVK + #.01 zR1NO3 + #.01 zR2NO3 + #.08 zRHNO3 + #1.15 yROOH + #.07 yRUOOH + #1.22 SumRO2 |
| O1O3 | 8.70e-18 |  | G | OLE1 + O3 = #.26 OH + #.01 xOH + #.17 HO2 + #.16 xHO2 + #.01 ETO2 + #.01 xTBUO + #.21 HCHO2 + #.17 RCHO2 + #.18 RO2C + #.01 RO2XC + #.5 HCHO + #.02 ETOH + #.08 xMECHO + #.19 ETCHO + #.04 xETCHO + #.31 RCHO + #.02 xRCHO + #.04 xACET + #.01 zRCNO3 + #.09 H2 + #.37 CO + #.24 CO2 + #.03 ETHAN + #.02 PROP + #.01 NC4 + #.01 ALK2 + #.02 ALK3 + #.01 ALK4 + #.02 yROOH + #.14 yHPCRB + #.2 SumRO2 |
| O1N3 | 1.44e-14 |  | G | OLE1 + NO3 = #.09 xNO2 + #.55 xHO2 + #.09 xETO2 + #.15 xTBUO + #1.41 RO2C + #.13 RO2XC + #.09 xHCHO + #.09 xETCHO + #.01 xRCHO + #.14 xACET + #.02 zR1NO3 + #.81 xRCNO3 + #.11 zRDNO3 + #1.22 yRPNO3 + #.31 yROOH + #1.54 SumRO2 |
| O1OP | 4.43e-12 |  | G | OLE1 + O3P = #.25 RCHO + #.1 MEK + #.15 KET2 + #.09 ALK2 + #.36 ALK3 + #.05 ALK4 |
| O2OH | 6.29e-11 |  | G | OLE2 + OH = #.93 xHO2 + #.94 RO2C + #.07 RO2XC + #1.25 xMECHO + #.4 xETCHO + #.12 xRCHO + #.07 zRHNO3 + #.99 yROOH + #.02 yRUOOH + #1.01 SumRO2 |
| O2O3 | 1.90e-16 |  | G | OLE2 + O3 = OLE2_O3 + #.46 OH + #.06 HO2 + #.32 xHO2 + #.04 MEO2 + #.01 ETO2 + #.15 MECHO2 + #.1 RCHO2 + #.4 RO2C + #.07 xHCHO + #.06 MEOH + #.02 ETOH + #.67 MECHO + #.09 xMECHO + #.22 ETCHO + #.01 xETCHO + #.07 RCHO + #.01 xACET + #.19 CO + #.23 CO2 + #.12 CH4 + #.03 ETHAN + #.09 yHPCRB + #.45 SumRO2 |
| 593 | 2.54e+0 |  | 53 | OLE2_O3 = #.01 OH + #.08 xOH + #.01 RCHO + #.22 xPACID + #.07 CO2 |
| 594 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLE2_O3 + NO = NO + #.08 xHO2 + #.01 RO2C + #.2 xHCHO + #.02 xGLY + #.27 CO + #.26 yHPCRB + #.02 SumRO2 |
| O2N3 | 4.34e-13 |  | G | OLE2 + NO3 = #.8 xNO2 + #.11 xHO2 + #1.01 RO2C + #.08 RO2XC + #1.11 xMECHO + #.33 xETCHO + #.09 xRCHO + #.01 xACET + #.12 xRCNO3 + #.08 zRDNO3 + #1.08 yRPNO3 + #.01 yROOH + #1.09 SumRO2 |
| O2OP | 1.95e-11 |  | G | OLE2 + O3P = #.21 MEK + #.29 KET2 + #.21 ALK1 + #.22 ALK2 + #.07 ALK3 |
| O3OH | 5.26e-11 |  | G | OLE3 + OH = #.94 xHO2 + #.94 RO2C + #.06 RO2XC + #.94 xHCHO + #.82 xACET + #.13 xMEK + #.06 zRHNO3 + yROOH + SumRO2 |
| O3O3 | 1.18e-17 |  | G | OLE3 + O3 = #.58 OH + #.14 HO2 + #.45 xMECO3 + #.03 xR2CO3 + #.21 HCHO2 + #.48 RO2C + #.02 RO2XC + #.5 HCHO + #.45 xHCHO + #.03 xMECHO + #.43 ACET + #.07 MEK + #.02 zRCNO3 + #.09 H2 + #.17 CO + #.12 CO2 + #.42 yHPCRB + #.5 SumRO2 |
| O3N3 | 3.62e-13 |  | G | OLE3 + NO3 = #.86 xNO2 + #.01 xMEO2 + #.07 xETO2 + #.94 RO2C + #.06 RO2XC + #.86 xHCHO + #.8 xACET + #.06 xMEK + #.08 xRCNO3 + #.06 zRDNO3 + yRPNO3 + SumRO2 |
| O3OP | 1.70e-11 |  | G | OLE3 + O3P = #.5 RCHO + #.5 ALK2 |
| O4OH | 8.71e-11 |  | G | OLE4 + OH = #.91 xHO2 + #.91 RO2C + #.08 RO2XC + #.83 xMECHO + #.09 xETCHO + #.91 xACET + #.08 zRHNO3 + yROOH + #.99 SumRO2 |
| O4O3 | 4.05e-16 |  | G | OLE4 + O3 = OLE4_O3 + #.72 OH + #.03 HO2 + #.17 xHO2 + #.03 MEO2 + #.48 xMECO3 + #.1 MECHO2 + #.01 RCHO2 + #.7 RO2C + #.02 RO2XC + #.53 xHCHO + #.04 MEOH + #.45 MECHO + #.02 xMECHO + #.05 ETCHO + #.5 ACET + #.02 zRCNO3 + #.07 CO + #.12 CO2 + #.08 CH4 + #.01 ETHAN + #.44 yHPCRB + #.75 SumRO2 |
| 603 | 2.62e+0 |  | 53 | OLE4_O3 = #.05 xOH + #.15 xPACID + #.05 CO2 |
| 604 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLE4_O3 + NO = NO + #.05 xHO2 + #.13 xHCHO + #.18 CO + #.17 yHPCRB |
| O4N3 | 9.31e-12 |  | G | OLE4 + NO3 = #.91 xNO2 + #.92 RO2C + #.09 RO2XC + #.83 xMECHO + #.08 xETCHO + #.91 xACET + #.09 zRDNO3 + yRPNO3 + #1.01 SumRO2 |
| O4OP | 5.11e-11 |  | G | OLE4 + O3P = #.5 KET2 + #.5 ALK2 |
| TPOH | 1.10e-10 |  | G | TERP + OH = TERP_OH + #.01 xOH + #.01 HO2 + #.6 xHO2 + #.02 xR2CO3 + #.01 xMACO3 + #1.1 RO2C + #.29 RO2XC + #.16 xHCHO + #.29 xRCHO + #.13 xOLEA2 + #.09 xACET + #.05 xKET2 + #.01 xMVK + #.04 xLVKS + #.05 xOLEP + #.01 xAFG2A + #.01 zR2NO3 + #.2 zRHNO3 + #.07 zRCNO3 + #.01 xHPCRB + #.51 yROOH + #.55 yRUOOH + #.27 yHPCRB + #1.39 SumRO2 |
| 608 | 2.70e+0 |  | 53 | TERP_OH = #.05 xOH + #.03 xPACID + #.02 xAFG2A + #.06 xHPCRB |
| 609 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | TERP_OH + NO = NO + #.02 xHO2 + #.01 xR2CO3 + #.13 RO2C + #.04 RO2XC + #.01 xHCHO + #.03 xRCHO + #.03 xOLEA1 + #.01 xOLEA2 + #.01 zR2NO3 + #.01 zRHNO3 + #.03 zRCNO3 + #.01 yROOH + #.01 yRUOOH + #.2 yHPCRB + #.17 SumRO2 |
| TPO3 | 1.17e-16 |  | G | TERP + O3 = TERP_O3 + #.57 OH + #.02 xOH + #.13 HO2 + #.09 xHO2 + #.08 xMECO3 + #.07 xR2CO3 + #.08 HCHO2 + #.25 RCHO2 + #.36 RO2C + #.11 RO2XC + #.18 HCHO + #.06 xHCHO + #.12 xRCHO + #.03 xGLY + #.01 xMACR + #.01 ACET + #.01 xACET + #.17 KET2 + #.01 LVKS + #.02 OLEP + #.01 xPACID + #.01 xAFG3 + #.11 zRCNO3 + #.01 xHPCRB + #.03 H2 + #.12 CO + #.06 CO2 + #.01 yROOH + #.39 yHPCRB + #.47 SumRO2 |
| 611 | 1.22e+0 |  | 53 | TERP_O3 = #.01 OH + #.03 xOH + #.08 xHO2 + #.01 xPACID + #.04 xHPCRB |
| 612 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | TERP_O3 + NO = NO + #.04 xMECO3 + #.01 xR2CO3 + #.04 xMACO3 + #.06 RO2C + #.03 RO2XC + #.04 xHCHO + #.01 xRCHO + #.04 xOLEA2 + #.03 zRCNO3 + #.01 CO + #.08 yHPCRB + #.09 SumRO2 |
| TPN3 | 1.10e-11 |  | G | TERP + NO3 = TERP_N3 + #.51 xNO2 + #.02 xOH + #.07 xHO2 + #.03 xR2CO3 + #1.17 RO2C + #.29 RO2XC + #.02 xHCHO + #.29 xRCHO + #.21 xOLEA2 + #.15 xACET + #.01 xMVK + #.01 xOLEP + #.13 xRCNO3 + #.09 zRCNO3 + #.19 zRDNO3 + yRPNO3 + #.05 yROOH + #.01 yRUOOH + #.01 yHPCRB + #1.46 SumRO2 |
| 614 | 2.47e+0 |  | 53 | TERP_N3 = #.01 xNO2 + #.07 xOH + #.02 xPACID + #.03 xRCNO3 + #.02 xHPCRB |
| 615 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | TERP_N3 + NO = NO + #.04 xHO2 + #.12 RO2C + #.04 RO2XC + #.01 xACET + #.04 zRCNO3 + #.01 zRDNO3 + #.01 yRPNO3 + #.16 SumRO2 |
| TPOP | 4.24e-11 |  | G | TERP + O3P = #.16 RCHO + #.04 OLEA2 + #.18 KET2 + #.01 LVKS + #.27 OLEP + #.18 ALK3 + #.08 ALK4 + #.08 ALK5 |
| SQOH | 2.00e-10 |  | G | SESQ + OH = SESQ_OH + #.05 xOH + #.03 HO2 + #.57 xHO2 + #.83 RO2C + #.25 RO2XC + #.04 xHCHO + #.45 xOLEA2 + #.01 xACET + #.07 xOLEP + #.18 zRHNO3 + #.03 zRCNO3 + #.02 xHPCRB + #.01 yROOH + #.97 yRUOOH + #.09 yHPCRB + #1.08 SumRO2 |
| 618 | 3.19e+0 |  | 53 | SESQ_OH = #.03 xOH + #.08 xHO2 + #.02 xLVKS + #.01 xOLEP + #.03 zRPNO3 + #.06 xHPCRB + #.01 yROOH |
| 619 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | SESQ_OH + NO = NO + #.25 RO2C + #.09 RO2XC + #.08 xHCHO + #.07 xOLEA2 + #.09 xACET + #.12 zRHNO3 + #.01 zRCNO3 + #.11 yRUOOH + #.23 yHPCRB + #.34 SumRO2 |
| SQO3 | 3.14e-16 |  | G | SESQ + O3 = SESQ_O3 + #.66 OH + #.02 xOH + #.01 HO2 + #.07 xHO2 + #.15 xMACO3 + #.33 RCHO2 + #.25 RO2C + #.1 RO2XC + #.01 HCHO + #.15 xHCHO + #.01 OLEP + #.07 zRCNO3 + #.01 xHPCRB + #.22 yHPCRB + #.35 SumRO2 |
| 621 | 4.27e+0 |  | 53 | SESQ_O3 = #.03 xOH + #.29 xHO2 + #.05 OTHN + #.03 zRNNO3 |
| 622 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | SESQ_O3 + NO = NO + #.17 xMECO3 + #.35 RO2C + #.14 RO2XC + #.02 xHCHO + #.02 xRCHO + #.22 xOLEA2 + #.02 xACET + #.16 zRCNO3 + #.51 yHPCRB + #.49 SumRO2 |
| SQN3 | 1.90e-11 |  | G | SESQ + NO3 = #.74 xNO2 + #.03 xOH + #.01 xHO2 + #.84 RO2C + #.23 RO2XC + #.74 xOLEA2 + #.03 xRCNO3 + #.01 zRCNO3 + #.21 zRDNO3 + #.01 RNNO3 + yRPNO3 + #1.07 SumRO2 |
| SQOP | 6.85e-11 |  | G | SESQ + O3P = #.13 OLEA2 + #.87 OLEP |
| BXOH | 1.21e-12 |  | G | BENX + OH = #.69 HO2 + #.28 xHO2 + #.28 RO2C + #.04 RO2XC + #.28 xGLY + #.12 OLEA2 + #.57 PHEN + #.28 xBUDAL + #.04 zRANO3 + #.31 yRAOOH + #.32 SumRO2 |
| B1OH | 7.69e-12 |  | G | ARO1 + OH = #.26 HO2 + #.48 xHO2 + #.05 xETO2 + #.75 RO2C + #.21 RO2XC + #.01 xHCHO + #.06 xMECHO + #.11 xETCHO + #.01 xRCHO + #.13 xGLY + #.13 xMGLY + #.01 OLEA1 + #.13 OLEA2 + #.12 XYNL + #.2 xBALD + #.13 xBUDAL + #.01 xAFG1 + #.11 xAFG2A + #.03 zR1NO3 + #.11 zR2NO3 + #.01 zRHNO3 + #.06 zRANO3 + #.04 ARO1 + #3.11 NROG + #.64 yROOH + #.32 yRAOOH + #.96 SumRO2 |
| B2OH | 2.20e-11 |  | G | ARO2 + OH = #.28 HO2 + #.56 xHO2 + #.61 RO2C + #.15 RO2XC + #.01 xHCHO + #.07 xGLY + #.39 xMGLY + #.02 OLEA1 + #.13 OLEA2 + #.01 xKET2 + #.01 LVKS + #.03 xBACL + #.01 xOACID + #.08 XYNL + #.04 BALD + #.03 xBALD + #.03 xBUDAL + #.07 xAFG1 + #.29 xAFG2A + #.04 xAFG2B + #.05 xAFG3 + #.02 zR2NO3 + #.01 zRCNO3 + #.11 zRANO3 + #.03 xBENX + #1.67 NROG + #.11 yROOH + #.59 yRAOOH + #.04 yHPCRB + #.76 SumRO2 |
| FUOH | 3.84e-11 |  | G | FURNS + OH = #.75 HO2 + #.24 xHO2 + #.24 RO2C + #.01 RO2XC + #.07 xRCHO + #.03 xOLEA1 + #.14 xOLEP + #.75 BUDAL + #.01 zRHNO3 + #.08 CO + #.15 yRUOOH + #.01 yHPCRB + #.25 SumRO2 |
| FUO3 | 2.40e-18 |  | G | FURNS + O3 = #.44 HO2 + #.33 xHO2 + #.4 RCHO2 + #.33 RO2C + #.01 RO2XC + #.14 OLEA1 + #.01 zRCNO3 + #.07 HPCRB + #.74 CO + #.19 CO2 + #.33 ALK1 + #.2 yHPCRB + #.34 SumRO2 |
| FUN3 | 1.20e-12 |  | G | FURNS + NO3 = #.08 xNO2 + #.87 xHO2 + #.95 RO2C + #.05 RO2XC + #.07 xOLEA1 + #.01 xOLEP + #.87 xRCNO3 + #.05 zRDNO3 + #.28 CO + #.63 yRPNO3 + SumRO2 |
| STOH | 5.80e-11 |  | G | STYRS + OH = #.06 HO2 + #.79 xHO2 + #.79 RO2C + #.15 RO2XC + #.74 xHCHO + #.02 xGLY + #.02 xMGLY + #.03 OLEA2 + #.02 XYNL + #.74 xBALD + #.02 xBUDAL + #.02 xAFG2A + #.14 zRHNO3 + #.01 zRANO3 + #.88 yROOH + #.06 yRAOOH + #.94 SumRO2 |
| STO3 | 1.60e-17 |  | G | STYRS + O3 = #.03 xBZO + #.08 OH + #.17 HO2 + #.21 HCHO2 + #.34 RCHO2 + #.03 RO2C + #.5 HCHO + #.05 PHEN + #.5 BALD + #.09 H2 + #.22 CO + #.23 CO2 + #.09 BENZ + #.03 yROOH + #.03 SumRO2 |
| AMOH | 4.35e-11 |  | G | AMINS + OH = #.02 HO2 + #.96 xHO2 + #.01 xMEO2 + #.97 RO2C + #.02 RO2XC + #.08 xHCHO + #.02 RCHO + #.02 zR2NO3 + #.97 xAMINS + #.99 yROOH + #.99 SumRO2 |
| AMO3 | 3.09e-18 |  | G | AMINS + O3 = #.61 AMINS + #29.54 NROG |
| TAOH | 1.01e-11 |  | G | TAMNS + OH = #.03 xMEO2 + #.06 RO2C + #.03 xHCHO + #.03 xAMINS + #.97 PNAMIN + #.06 yROOH + #.06 SumRO2 |
| A4OH | 3.12e-11 |  | G | RCHO + OH = #.02 xOH + #.05 HO2 + #.05 xHO2 + #.01 xMECO3 + #.81 R2CO3 + #.16 RO2C + #.04 RO2XC + #.03 xHCHO + #.04 RCHO + #.04 xRCHO + #.02 MGLY + #.03 xACET + #.01 xBACL + #.02 xPACID + #.04 zRCNO3 + #.03 CO + #.01 ALK4 + #.07 NROG + #.15 yHPCRB + #.2 SumRO2 + #.81 SumRCO3 |
| A4N3 | 2.09e-14 |  | G | RCHO + NO3 = HNO3 + #.04 HO2 + #.95 R2CO3 + #.02 RO2C + #.01 RO2XC + #.02 RCHO + #.02 MGLY + #.01 zRCNO3 + #.02 yHPCRB + #.03 SumRO2 + #.95 SumRCO3 |
| A4HV | Phot Set= C2CHOabs | G,63 | RCHO + HV = RCHO_HV + #1.21 HO2 + #.6 xHO2 + #.04 xMECO3 + #.76 RO2C + #.14 RO2XC + #.09 xHCHO + #.09 MECHO + #.02 xMECHO + #.03 xETCHO + #.12 GLCHO + #.42 xRCHO + #.06 xACET + #.03 xKET2 + #.01 xPACID + #.01 zRHNO3 + #.12 zRCNO3 + CO + #.01 ALK4 + #.04 NROG + #.31 yROOH + #.51 yHPCRB + #.9 SumRO2 |
| 639 | 2.25e+0 |  | 53 | RCHO_HV = #.01 xOH + #.06 xPACID + #.01 CO2 |
| 640 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | RCHO_HV + NO = NO + #.01 xHO2 + #.01 RO2C + #.04 xHCHO + #.01 xRCHO + #.05 CO + #.06 yHPCRB + #.01 SumRO2 |
| A5OH | 5.06e-11 |  | G | OLEA1 + OH = OLEA1_OH + #.17 HO2 + #.27 xHO2 + #.03 MACO3 + #.6 RO2C + #.05 RO2XC + #.2 xGLCHO + #.06 RCHO + #.05 xGLY + #.19 xKET2 + #.02 xPACID + #.05 AFG1 + #.01 AFG2A + #.04 AFG2B + #.01 HPCRB + #.06 CO2 + #.05 yHPCRB + #.65 SumRO2 + #.03 SumRCO3 |
| 642 | 9.69e-1 |  | 53 | OLEA1_OH = #.33 xOH + #.15 HO2 + #.01 xHCHO + #.19 xKET2 + #.19 xPACID + #.02 AFG2A + #.04 AFG2B + #.05 zRCNO3 + #.09 HPCRB + #.27 CO2 |
| 643 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLEA1_OH + NO = NO + #.43 xHO2 + #.14 RO2C + #.01 RO2XC + #.09 xHCOOH + #.25 xGLCHO + #.08 xGLY + #.48 xMGLY + #.06 zRHNO3 + #.1 CO + #.59 yHPCRB + #.15 SumRO2 |
| A5O3 | 3.50e-18 |  | G | OLEA1 + O3 = #.62 OH + #.71 HO2 + #.16 RCHO2 + #.04 HCHO + #.1 MEOH + #.02 HCOOH + #.01 MECHO + #.06 GLCHO + #.42 GLY + #.81 MGLY + #.02 KET2 + #.01 OACID + #.06 CO + #.33 CO2 + #.05 ALK4 |
| A5N3 | 9.62e-14 |  | G | OLEA1 + NO3 = #.56 xNO2 + #.04 HNO3 + #.22 HO2 + #.16 xHO2 + #.71 RO2C + #.06 RO2XC + #.01 xHCHO + #.52 xGLCHO + #.03 xGLY + #.03 xKET2 + #.52 xPACID + #.02 AFG1 + #.01 AFG2B + #.15 xRHNO3 + #.19 RCNO3 + #.01 xRCNO3 + #.05 zRCNO3 + #.02 zRDNO3 + #.15 CO + #.17 yRPNO3 + #.77 SumRO2 |
| A5HV | Phot Set= MACR-06 | G,63 | OLEA1 + HV = #.43 OH + #.86 HO2 + #.01 xHO2 + #.1 MEO2 + #.03 MACO3 + #.01 RO2C + #.01 xHCHO + #.01 HCOOH + #.09 GLCHO + #.06 MGLY + #.03 KET2 + #.25 OLEP + #.01 xPACID + #.03 AFG2A + #.08 AFG2B + #.99 CO + #.03 CO2 + #.02 ALK4 + #.01 ALK5 + #.11 SumRO2 + #.03 SumRCO3 |
| A6OH | 9.04e-11 |  | G | OLEA2 + OH = OLEA2_OH + #.08 OH + #.16 xOH + #.11 HO2 + #.24 xHO2 + #.01 xMECO3 + #.03 xR2CO3 + #.12 MACO3 + #.03 xMACO3 + #.51 RO2C + #.1 RO2XC + #.01 xHCHO + #.03 xGLCHO + #.23 xRCHO + #.03 xGLY + #.01 xMGLY + #.04 OLEA1 + #.05 OLEA2 + #.01 xOLEA2 + #.02 LVKS + #.1 xPACID + #.01 xAFG3 + #.05 zRHNO3 + #.05 zRCNO3 + #.08 HPCRB + #.01 xHPCRB + #.18 CO + #.09 CO2 + #.07 MALAH + #.3 yHPCRB + #.61 SumRO2 + #.12 SumRCO3 |
| 648 | 3.25e+0 |  | 53 | OLEA2_OH = #.01 OH + #.07 xOH + #.02 HO2 + #.03 xMACO3 + #.13 xPACID + #.04 HPCRB + #.04 xHPCRB + #.02 MALAH |
| 649 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLEA2_OH + NO = NO + #.08 xHO2 + #.04 xMECO3 + #.15 RO2C + #.01 RO2XC + #.04 xRCHO + #.06 xMGLY + #.01 zRCNO3 + #.01 CO + #.06 CO2 + #.15 yHPCRB + #.16 SumRO2 |
| A6O3 | 2.99e-17 |  | G | OLEA2 + O3 = OLEA2_O3 + #.44 OH + #.16 HO2 + #.17 xHO2 + #.03 xMECO3 + #.03 HCHO2 + #.34 RCHO2 + #.24 RO2C + #.01 RO2XC + #.02 HCHO + #.03 xHCHO + #.01 HCOOH + #.21 RCHO + #.32 GLY + #.01 xGLY + #.36 MGLY + #.05 BACL + #.01 xPACID + #.01 zRCNO3 + #.01 H2 + #.38 CO + #.15 CO2 + #.03 yHPCRB + #.25 SumRO2 |
| 651 | 1.44e+0 |  | 53 | OLEA2_O3 = #.01 OH + #.08 xOH + #.01 HO2 + #.01 RCHO + #.06 xBACL + #.13 xPACID + #.03 xHPCRB + #.06 CO2 |
| 652 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLEA2_O3 + NO = NO + #.05 xHO2 + #.03 xR2CO3 + #.04 RO2C + #.02 RO2XC + #.03 xHCHO + #.06 xGLY + #.12 xMGLY + #.02 zRCNO3 + #.12 CO + #.22 yHPCRB + #.06 SumRO2 |
| A6N3 | 3.30e-12 |  | G | OLEA2 + NO3 = OLEA2_N3 + #.32 xNO2 + #.49 HNO3 + #.2 xOH + #.06 xHO2 + #.01 xMECO3 + #.03 xR2CO3 + #.1 MACO3 + #.06 xMACO3 + #.67 RO2C + #.16 RO2XC + #.02 xHCHO + #.26 xRCHO + #.01 xMGLY + #.19 xPACID + #.01 xAFG3 + #.07 xRCNO3 + #.1 zRCNO3 + #.06 zRDNO3 + #.09 CO + #.1 CO2 + #.05 MALAH + #.29 yRPNO3 + #.83 SumRO2 + #.1 SumRCO3 |
| 654 | 3.07e+0 |  | 53 | OLEA2_N3 = #.05 xOH + #.07 xMACO3 + #.21 xPACID + #.01 xAFG3 + #.04 xRCNO3 + #.04 xHPCRB + #.05 MALAH |
| 655 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLEA2_N3 + NO = NO + #.07 xHO2 + #.03 xMECO3 + #.21 RO2C + #.01 RO2XC + #.04 xRCHO + #.04 xMGLY + #.02 xACET + #.01 xRHNO3 + #.01 zRDNO3 + #.02 CO + #.14 CO2 + #.1 yRPNO3 + #.22 SumRO2 |
| A6HV | Phot Set= C2CHOabs | G,63 | OLEA2 + HV = OLEA2_HV + #.28 OH + HO2 + #.45 xHO2 + #.05 xMECO3 + #.64 RO2C + #.15 RO2XC + #.04 xHCHO + #.04 xRCHO + #.06 OLEA2 + #.07 xOLEA2 + #.01 xACET + #.04 xLVKS + #.26 OLEP + #.26 xAFG2A + #.02 xAFG2B + #.01 xAFG3 + #.08 zRHNO3 + #.06 zRCNO3 + #.03 xHPCRB + #1.21 CO + #.26 yRUOOH + #.46 yHPCRB + #.79 SumRO2 |
| 657 | 1.71e+0 |  | 53 | OLEA2_HV = #.02 OH + #.04 xOH + #.01 OLEP + #.06 xHPCRB |
| 658 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | OLEA2_HV + NO = NO + #.02 xHO2 + #.01 xMECO3 + #.08 RO2C + #.02 RO2XC + #.01 xHCHO + #.07 xOLEA2 + #.02 zRHNO3 + #.01 zRCNO3 + #.02 CO + #.12 yHPCRB + #.1 SumRO2 |
| K5OH | 9.96e-12 |  | G | KET2 + OH = #.01 xOH + #.53 HO2 + #.18 xHO2 + #.01 MECO3 + #.05 xMECO3 + #.01 R2CO3 + #.13 xR2CO3 + #.49 RO2C + #.08 RO2XC + #.02 HCHO + #.16 xHCHO + #.1 xMECHO + #.01 xETCHO + #.14 RCHO + #.19 xRCHO + #.31 MGLY + #.01 xACET + #.08 KET2 + #.03 xKET2 + #.08 zRCNO3 + #.54 yHPCRB + #.57 SumRO2 + #.02 SumRCO3 |
| K5HV | Phot Set= MEK-06, qy= 7.53e-2 | G,60 | KET2 + HV = #.46 HO2 + #.2 xHO2 + #.08 MEO2 + #.14 ETO2 + #.48 MECO3 + #.42 R2CO3 + #.21 RO2C + #.01 RO2XC + #.31 HCHO + #.02 xHCHO + #.01 xMECHO + #.03 xETCHO + #.16 xRCHO + #.01 zRHNO3 + #.1 CO + #.09 ALK4 + #.01 ALK5 + #.22 yROOH + #.44 SumRO2 + #.9 SumRCO3 |
| K6OH | 6.81e-11 |  | G | LVKS + OH = LVKS_OH + #.03 HO2 + #.13 xHO2 + #.1 MECO3 + #.15 xMECO3 + #.22 xR2CO3 + #.49 RO2C + #.06 RO2XC + #.04 xHCHO + #.06 xRCHO + #.01 MGLY + #.02 xMGLY + #.1 OLEA1 + #.02 xACET + #.22 xKET2 + #.04 xBACL + #.01 xPACID + #.01 xAFG2B + #.06 zRCNO3 + #.02 HPCRB + #.07 xHPCRB + #.01 CO + #.51 yHPCRB + #.55 SumRO2 + #.1 SumRCO3 |
| 662 | 6.74e+0 |  | 53 | LVKS_OH = #.31 HO2 + #.31 HPCRB + #.08 xHPCRB + #.07 CO |
| 663 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | LVKS_OH + NO = NO + #.27 xHO2 + #.28 RO2C + #.04 RO2XC + #.08 xRCHO + #.27 xMGLY + #.27 xACET + #.04 zRCNO3 + #.3 yHPCRB + #.32 SumRO2 |
| K6O3 | 1.94e-17 |  | G | LVKS + O3 = LVKS_O3 + #.58 OH + #.1 HO2 + #.02 xHO2 + #.42 xMECO3 + #.01 xR2CO3 + #.11 HCHO2 + #.12 RCHO2 + #.5 RO2C + #.02 RO2XC + #.03 HCHO + #.37 xHCHO + #.01 MECHO + #.03 RCHO + #.01 xGLY + #.64 MGLY + #.04 ACET + #.05 KET2 + #.27 BACL + #.01 OACID + #.01 xPACID + #.02 zRCNO3 + #.05 H2 + #.26 CO + #.12 CO2 + #.34 yHPCRB + #.53 SumRO2 |
| 665 | 5.62e+0 |  | 53 | LVKS_O3 = #.05 xMECO3 + #.01 RO2C + #.12 xPACID + #.01 CO2 |
| 666 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | LVKS_O3 + NO = NO + #.05 xHO2 + #.01 RO2XC + #.03 xHCHO + #.01 zRCNO3 + #.02 CO + #.1 yHPCRB |
| K6HV | Phot Set= MVK-16 | G,63 | LVKS + HV = #.05 xOH + #.12 HO2 + #.28 MEO2 + #.05 xMECO3 + #.28 MACO3 + #.1 RO2C + #.02 RO2XC + #.12 HCHO + #.05 xMGLY + #.35 OLEP + #.05 xPACID + #.02 zRCNO3 + #.6 CO + #.25 OLE4 + #.05 MALAH + #.4 SumRO2 + #.28 SumRCO3 |
| O5OH | 7.93e-11 |  | G | OLEP + OH = #.12 HO2 + #.28 xHO2 + #.36 R2CO3 + #.16 xR2CO3 + #.45 RO2C + #.08 RO2XC + #.27 xRCHO + #.01 MGLY + #.01 xMGLY + #.01 LVKS + #.04 BACL + #.04 OLEP + #.01 AFG3 + #.08 zRCNO3 + #.5 yHPCRB + #.53 SumRO2 + #.36 SumRCO3 |
| O5O3 | 7.86e-17 |  | G | OLEP + O3 = #.3 OH + #.26 HO2 + #.01 xHO2 + #.09 xR2CO3 + #.51 RCHO2 + #.1 RO2C + #.02 RO2XC + #.04 xHCHO + #.02 RCHO + #.02 xRCHO + #.02 xGLY + #.25 MGLY + #.03 KET2 + #.12 BACL + #.01 xPACID + #.02 zRCNO3 + #.02 HPCRB + #.14 CO + #.14 CO2 + #.1 yHPCRB + #.12 SumRO2 |
| O5N3 | 3.52e-12 |  | G | OLEP + NO3 = #.27 xNO2 + #.12 HNO3 + #.11 HO2 + #.15 xHO2 + #.32 xR2CO3 + #.01 MACO3 + #.79 RO2C + #.14 RO2XC + #.36 xRCHO + #.05 xGLY + #.09 xMGLY + #.03 xACET + #.04 xKET2 + #.07 OLEP + #.03 AFG3 + #.15 xRCNO3 + #.14 zRCNO3 + #.93 SumRO2 + #.01 SumRCO3 |
| OAOH | 7.47e-13 |  | G | OACID + OH = #.3 xHO2 + #.7 MEO2 + #.3 RO2C + #.02 xHCHO + #.28 xMGLY + #.72 CO2 + #.26 yHPCRB + SumRO2 |
| PAOH | 3.00e-14 |  | G | PACID + OH = #.19 xOH + #.56 xHO2 + #.26 MECO3 + #.74 RO2C + #.19 xHCHO + #.56 xPACID + #.19 CO2 + #.74 SumRO2 + #.26 SumRCO3 |
| PAHV | Phot Set= PAA | G,64 | PACID + HV = OH + MEO2 + CO2 + SumRO2 |
| MGOH | 1.19e-11 |  | G | MGLY + OH = #.01 xHO2 + #.99 MECO3 + #.01 RO2C + #.01 xHCHO + #.01 xPACID + CO + #.01 SumRO2 + #.99 SumRCO3 |
| MGN3 | 5.00e-16 |  | G | MGLY + NO3 = HNO3 + MECO3 + CO + SumRCO3 |
| MGHV | Phot Set= MGLY-13 | G,65 | MGLY + HV = HO2 + MECO3 + CO + SumRCO3 |
| BAHV | Phot Set= BACL-11 | G,66 | BACL + HV = #2 MECO3 + #2 SumRCO3 |
| CROH | 4.65e-11 |  | G | CRES + OH = #.84 HO2 + #.11 xHO2 + #.03 BZO + #.11 RO2C + #.02 RO2XC + #.02 xGLY + #.05 xMGLY + #.02 OLEA1 + #.08 OLEA2 + #.17 LVKS + #.03 xBACL + #.14 OLEP + #.42 CATL + #.01 xBALD + #.03 xBUDAL + #.01 xAFG1 + #.04 xAFG2A + #.02 xAFG2B + #.02 zRANO3 + #.01 yROOH + #.11 yRAOOH + #.13 SumRO2 |
| CRN3 | 1.27e-11 |  | G | CRES + NO3 = HNO3 + BZO |
| XLOH | 6.73e-11 |  | G | XYNL + OH = #.79 HO2 + #.16 xHO2 + #.02 BZO + #.16 RO2C + #.03 RO2XC + #.01 xGLY + #.04 xMGLY + #.02 OLEA1 + #.06 OLEA2 + #.26 LVKS + #.1 xBACL + #.16 OLEP + #.01 XYNL + #.27 CATL + #.01 xBUDAL + #.01 xAFG1 + #.09 xAFG2A + #.03 xAFG2B + #.01 xAFG3 + #.03 zRANO3 + #.02 yROOH + #.18 yRAOOH + #.19 SumRO2 |
| XLN3 | 3.09e-11 |  | G | XYNL + NO3 = HNO3 + BZO |
| CAOH | 1.56e-10 |  | G | CATL + OH = #.96 HO2 + #.03 xHO2 + #.01 BZO + #.03 RO2C + #.01 OLEA1 + #.02 OLEA2 + #.72 LVKS + #.02 xBACL + #.06 OLEP + #.13 CATL3 + #.02 xAFG2A + #.03 yRAOOH + #.03 SumRO2 |
| CAN3 | 4.04e-11 |  | G | CATL + NO3 = HNO3 + BZO |
| N4OH | 1.78e-11 |  | G | RCNO3 + OH = RCNO3_OH + #.09 xNO2 + #.27 NO2 + #.01 OH + #.01 xOH + #.03 HO2 + #.09 xHO2 + #.04 xMECO3 + #.32 R2CO3 + #.04 xR2CO3 + #.38 RO2C + #.06 RO2XC + #.06 xHCHO + #.04 xMECHO + #.02 RCHO + #.04 xRCHO + #.01 xGLY + #.02 MGLY + #.04 xACET + #.07 KET2 + #.07 BACL + #.02 xBACL + #.01 OLEP + #.03 PACID + #.03 xPACID + #.04 RCNO3 + #.15 xRCNO3 + #.06 zRCNO3 + #.01 CO + #.01 CO2 + #.05 ALK2 + #3.73 NROG + #.02 yRPNO3 + #.02 yHPCRB + #.44 SumRO2 + #.32 SumRCO3 |
| 685 | 2.06e+0 |  | 53 | RCNO3_OH = #.01 xOH + #.04 HO2 + #.04 RCNO3 |
| 686 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | RCNO3_OH + NO = NO + #.02 xR2CO3 + #.06 RO2C + #.02 RO2XC + #.02 xHCHO + #.03 xRCNO3 + #.02 zRCNO3 + #.02 yHPCRB + #.08 SumRO2 |
| N4HV | Phot Set= CRBNIT | G,67 | RCNO3 + HV = RCNO3_HV + #.62 NO2 + #.01 xOH + #.46 HO2 + #.31 xHO2 + #.06 ETO2 + #.15 MECO3 + #.06 R2CO3 + #.03 xR2CO3 + #.51 RO2C + #.1 RO2XC + #.04 HCHO + #.01 xHCHO + #.04 MECHO + #.17 RCHO + #.03 xRCHO + #.05 xACET + #.03 xKET2 + #.03 OACID + #.02 xOACID + #.02 xPACID + #.02 AFG2A + #.03 RCNO3 + #.19 xRCNO3 + #.1 zRCNO3 + #.46 CO + #.01 CO2 + #6.89 NROG + #.04 yRPNO3 + #.15 yHPCRB + #.67 SumRO2 + #.21 SumRCO3 |
| 688 | 4.46e-1 |  | 53 | RCNO3_HV = #.15 HO2 + #.01 xACET + #.05 PACID + #.02 xPACID + #.01 AFG2A + #.05 xRCNO3 + #.08 HPCRB |
| 689 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | RCNO3_HV + NO = NO + #.03 xOH + #.04 xMECO3 + #.03 xR2CO3 + #.16 RO2C + #.03 RO2XC + #.01 xHCHO + #.12 xRCHO + #.02 xKET2 + #.04 xRHNO3 + #.02 zRCNO3 + #.03 CO + #.05 CO2 + #.11 yHPCRB + #.19 SumRO2 |
| N3OH | 3.66e-11 |  | G | RHNO3 + OH = #.01 xNO2 + #.6 NO2 + #.08 HO2 + #.26 xHO2 + #.29 RO2C + #.05 RO2XC + #.05 xHCHO + #.03 xGLCHO + #.01 xACET + #.01 KET2 + #.06 xKET2 + #.01 LVKS + #.05 xRHNO3 + #.08 RCNO3 + #.21 xRCNO3 + #.04 zRDNO3 + #.02 ALK4 + #.57 ALK5 + #.32 yRPNO3 + #.34 SumRO2 |
| N3HV | Phot Set= IC3ONO2 | G,63 | RHNO3 + HV = #-0.01 xNO2 + NO2 + #.93 HO2 + #.05 xHO2 + #.11 RO2C + #.02 RO2XC + #.73 HCHO + #.01 xHCHO + #.02 MECHO + #.04 RCHO + #.02 xRCHO + #.32 MACR + #.06 OLEA1 + #.02 OLEA2 + #.01 xOLEA2 + #.04 ACET + #.37 MVK + #.01 xMVK + #.02 zRHNO3 + #.01 HPCRB + #.01 xHPCRB + #.07 FURNS + #.07 yRUOOH + #.05 yHPCRB + #.13 SumRO2 |
| N5OH | 4.49e-11 |  | G | RANO3 + OH = #.42 NO2 + #.58 HO2 + #.01 OLEP + #.02 AFG2A + #.11 RHNO3 + #.47 RCNO3 + #.01 ALK5 + #.37 ALK6 |
| N5HV | Phot Set= COOH | G,68 | RANO3 + HV = #.34 RHNO3 + #.66 RCNO3 |
| N6OH | 4.11e-11 |  | G | RPNO3 + OH = #.18 xNO2 + #.35 NO2 + #.19 OH + #.03 xOH + #.15 HO2 + #.03 xHO2 + #.35 RO2C + #.08 RO2XC + #.09 xHCHO + #.09 xRCHO + #.05 xOLEA1 + #.03 xACET + #.02 xMVK + #.16 RHNO3 + #.02 RCNO3 + #.03 xRCNO3 + #.02 zRCNO3 + #.15 RPNO3 + #.02 xRPNO3 + #.06 zRDNO3 + #.35 ROOH + #.01 HPCRB + #.02 xHPCRB + #.33 yRPNO3 + #.43 SumRO2 |
| N6HV | Phot Set= COOH | G,68 | RPNO3 + HV = RPNO3_HV + #.9 NO2 + OH + #.01 HO2 + #.01 xHO2 + #.01 xR2CO3 + #.06 RO2C + #.02 RO2XC + #.63 HCHO + #.2 RCHO + #.54 OLEA1 + #.01 xACET + #.16 MVK + #.01 RCNO3 + #.01 xRCNO3 + #.02 zRCNO3 + #.08 SumRO2 |
| 696 | 8.74e-1 |  | 53 | RPNO3_HV = #.04 NO2 + #.02 HO2 + #.01 xPACID + #.01 RPNO3 + #.04 HPCRB |
| 697 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | RPNO3_HV + NO = NO + #.05 xHO2 + #.05 RO2C + #.04 xHCHO + #.02 xRHNO3 + #.03 xRCNO3 + #.06 yRPNO3 + #.05 SumRO2 |
| NDOH | 1.27e-11 |  | G | RDNO3 + OH = #.23 xNO2 + #.49 NO2 + #.05 xHO2 + #.77 RO2C + #.23 RO2XC + #.08 xHCHO + #.15 xACET + #.47 RHNO3 + #.02 RCNO3 + #.24 xRCNO3 + #.08 zRCNO3 + #.15 zRDNO3 + #.04 xRDNO3 + #.01 CO + SumRO2 |
| NDHV | Phot Set= DIONO2 | G,69 | RDNO3 + HV = RDNO3_HV + #1.83 NO2 + #.03 HO2 + #.02 xHO2 + #.01 xR2CO3 + #.17 RO2C + #.05 RO2XC + #.23 HCHO + #.01 xHCHO + #.4 RCHO + #.2 OLEA1 + #.03 xACET + #.23 MVK + #.01 xPACID + #.03 RCNO3 + #.03 xRCNO3 + #.05 zRCNO3 + #.22 SumRO2 |
| 700 | 8.74e-1 |  | 53 | RDNO3_HV = #.04 NO2 + #.01 xOH + #.01 HO2 + #.01 xPACID + #.01 RPNO3 + #.04 HPCRB + #.01 CO2 |
| 701 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | RDNO3_HV + NO = NO + #.05 xHO2 + #.05 RO2C + #.04 xHCHO + #.02 xRHNO3 + #.03 xRCNO3 + #.05 yRPNO3 + #.05 SumRO2 |
| N1OH | 1.47e-12 |  | G | R1NO3 + OH = #.41 xNO2 + #.17 NO2 + #.29 xHO2 + #.99 RO2C + #.12 RO2XC + #.1 xHCHO + #.29 xMECHO + #.05 xETCHO + #.02 xRCHO + #.05 ACET + #.26 xACET + #.05 MEK + #.04 xMEK + #.07 KET2 + #.05 xKET2 + #.1 xRHNO3 + #.19 xRCNO3 + #.01 xRPNO3 + #.12 zRDNO3 + #1.12 yRPNO3 + #1.11 SumRO2 |
| N1HV | Phot Set= IC3ONO2 | G,63 | R1NO3 + HV = #.04 TBUO + #-0.01 xNO2 + NO2 + #.19 HO2 + #.38 xHO2 + #.32 ETO2 + #.01 xTBUO + #.46 RO2C + #.05 RO2XC + #.05 xHCHO + #.12 MECHO + #.03 ETCHO + #.03 xETCHO + #.02 xRCHO + #.34 ACET + #.12 xACET + #.11 MEK + #.05 KET2 + #.22 xKET2 + #.05 zRHNO3 + #.01 xRHNO3 + #.51 yROOH + #.83 SumRO2 |
| N2OH | 1.16e-11 |  | G | R2NO3 + OH = #.18 xNO2 + #.05 NO2 + #.43 xHO2 + #1.17 RO2C + #.33 RO2XC + #.01 xHCHO + #.07 xRCHO + #.01 xACET + #.05 KET2 + #.08 xKET2 + #.02 xOLEP + #.04 xRHNO3 + #.4 xRCNO3 + #.01 zRCNO3 + #.32 zRDNO3 + #.01 xHPCRB + #.02 CO + #1.44 yRPNO3 + #1.5 SumRO2 |
| N2HV | Phot Set= IC3ONO2 | G,63 | R2NO3 + HV = R2NO3_HV + #-0.04 xNO2 + NO2 + #.1 HO2 + #.61 xHO2 + #.01 xMECO3 + #.01 xR2CO3 + #.82 RO2C + #.19 RO2XC + #.04 xRCHO + #.01 xACET + #.09 KET2 + #.44 xKET2 + #.02 xMVK + #.03 xPACID + #.13 zRHNO3 + #.04 xRHNO3 + #.06 zRCNO3 + #.02 CO + #.61 yROOH + #.36 yHPCRB + #1.01 SumRO2 |
| 706 | 1.28e+0 |  | 53 | R2NO3_HV = #.02 HO2 + #.02 xHO2 + #.05 xPACID + #.06 xHPCRB |
| 707 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | R2NO3_HV + NO = NO + #.13 RO2C + #.03 RO2XC + #.1 xRCHO + #.01 xACET + #.01 zRHNO3 + #.03 zRCNO3 + #.16 yHPCRB + #.16 SumRO2 |
| H4OH | 8.27e-11 |  | G | RAOOH + OH = #.76 OH + #.17 HO2 + #.06 xHO2 + #.06 RO2C + #.01 RO2XC + #.31 RCHO + #.02 xGLY + #.04 xMGLY + #.01 KET2 + #.04 OLEP + #.02 xBUDAL + #.02 AFG2A + #.03 xAFG2A + #.01 zRANO3 + #.17 HPCRB + #.01 ALK5 + #.37 ALK6 + #.07 yRAOOH + #.07 SumRO2 |
| H4HV | Phot Set= COOH | G,63 | RAOOH + HV = HPCRB |
| H3OH | 5.87e-11 |  | G | RUOOH + OH = #.64 OH + #.08 HO2 + #.25 xHO2 + #.25 RO2C + #.02 RO2XC + #.12 xHCHO + #.03 xGLCHO + #.03 xMACR + #.06 xKET2 + #.06 xMVK + #.02 LVKS + #.01 zRHNO3 + #.01 zRPNO3 + #.08 HPCRB + #.16 xHPCRB + #.02 ALK4 + #.6 ALK5 + #.01 xFURNS + #.17 yROOH + #.1 yRUOOH + #.27 SumRO2 |
| H3HV | Phot Set= COOH | G,63 | RUOOH + HV = OH + HO2 + #.86 HCHO + #.4 MACR + #.04 OLEA1 + #.47 MVK + #.09 FURNS |
| H5OH | 5.38e-11 |  | G | HPCRB + OH = #.58 OH + #.01 HO2 + #.38 xHO2 + #.38 RO2C + #.03 RO2XC + #.03 xHCHO + #.34 RCHO + #.05 xGLY + #.26 xMGLY + #.01 OLEA1 + #.21 OLEP + #.03 xPACID + #.02 AFG1 + #.03 zRPNO3 + #.01 HPCRB + #.35 xHPCRB + #.04 CO + #.39 yHPCRB + #.41 SumRO2 |
| H5HV | Phot Set= HPALDS, qy= 1.00e-1 | G,70 | HPCRB + HV = HPCRB_HV + OH + #.54 HO2 + #.09 xHO2 + #.06 RO2C + #.11 HCHO + #.03 xHCHO + #.11 OLEA1 + #.03 xPACID + #.11 AFG2A + #.29 AFG2B + #.02 xAFG2B + #.07 SumRO2 |
| 714 | 2.11e+1 |  | 53 | HPCRB_HV = #.36 HO2 + #.01 RO2XC + #.03 xHCHO + #.03 xPACID + #.11 AFG2A + #.25 AFG2B + #.01 xAFG2B + #.01 zRCNO3 |
| 715 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | HPCRB_HV + NO = NO + #.07 xHO2 + #.4 RO2C + #.39 SumRO2 |
| H2OH | 1.24e-11 |  | G | ROOH + OH = #.2 OH + #.06 xOH + #.22 HO2 + #.38 xHO2 + #.07 xETO2 + #.02 xTBUO + #.59 RO2C + #.05 RO2XC + #.01 HCHO + #.34 xHCHO + #.14 xMECHO + #.01 xETCHO + #.06 GLCHO + #.04 xGLCHO + #.01 RCHO + #.03 xRCHO + #.02 ACET + #.14 xACET + #.02 MEK + #.02 xMEK + #.09 KET2 + #.03 xKET2 + #.02 zR1NO3 + #.01 zRHNO3 + #.01 zRCNO3 + #.02 zRPNO3 + #.22 HPCRB + #.03 xHPCRB + #.61 yROOH + #.03 yHPCRB + #.64 SumRO2 |
| H2HV | Phot Set= COOH | G,63 | ROOH + HV = #.02 TBUO + OH + #.79 HO2 + #.06 xHO2 + #.11 ETO2 + #.09 RO2C + #.01 RO2XC + #.74 HCHO + #.23 MECHO + #.01 ETCHO + #.09 GLCHO + #.08 RCHO + #.16 ACET + #.03 xACET + #.04 MEK + #.05 KET2 + #.03 xKET2 + #.01 zRCNO3 + #.06 yROOH + #.03 yHPCRB + #.21 SumRO2 |
| F2OH | 3.39e-11 |  | G | AFG1 + OH = AFG1_OH + #.24 OH + #.01 xOH + #.02 HO2 + #.2 xHO2 + #.18 RO2C + #.02 RO2XC + #.18 xGLY + #.02 xPACID + #.02 HPCRB + #.01 CO + #.24 MALAH + #.2 SumRO2 |
| 719 | 1.77e+1 |  | 53 | AFG1_OH = #.19 OH + #.01 xOH + #.32 HO2 + #.19 xPACID + #.02 zRCNO3 + #.32 HPCRB + #.01 xHPCRB + #.18 MALAH |
| 720 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | AFG1_OH + NO = NO + #.39 xHO2 + #.52 RO2C + #.03 RO2XC + #.39 xGLY + #.56 xMGLY + #.2 CO + #.43 yHPCRB + #.55 SumRO2 |
| F2HV | Phot Set= AFGS, qy= 2.20e-1 | G,62 | AFG1 + HV = AFG1_HV + #.26 OH + #.54 xOH + #.94 HO2 + #.03 xHO2 + #.06 MEO2 + #.03 RO2C + #.23 PACID + #.05 xPACID + #.01 AFG1 + #.02 AFG2A + #.02 xHPCRB + #.03 CO + #.09 SumRO2 |
| 722 | 1.80e+1 |  | 53 | AFG1_HV = #.01 OH + #.17 xOH + #.33 xPACID + #.33 xHPCRB |
| 723 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | AFG1_HV + NO = NO + #.1 xHO2 + #.64 RO2C + #.08 RO2XC + #.08 zRCNO3 + #.05 CO + #.49 MALAH + #.72 SumRO2 |
| F3OH | 5.99e-11 |  | G | AFG2A + OH = #.57 xHO2 + #.15 xMECO3 + #.01 xR2CO3 + #.2 MACO3 + #.73 RO2C + #.07 RO2XC + #.03 xRCHO + #.47 xGLY + #.54 xMGLY + #.23 xPACID + #.07 zRCNO3 + #.03 CO + #.47 yHPCRB + #.8 SumRO2 + #.2 SumRCO3 |
| F3HV | Phot Set= AFGS, qy= 2.50e-1 | G,62 | AFG2A + HV = OH + #.91 MEO2 + #.09 ETO2 + MALAH + SumRO2 |
| F4OH | 4.58e-11 |  | G | AFG2B + OH = AFG2B_OH + #.02 HO2 + #.4 xHO2 + #.17 MACO3 + #.4 RO2C + #.05 RO2XC + #.39 xGLY + #.39 xBACL + #.05 zRCNO3 + #.02 HPCRB + #.38 yHPCRB + #.45 SumRO2 + #.17 SumRCO3 |
| 727 | 1.46e+1 |  | 53 | AFG2B_OH = #.36 HO2 + #.36 HPCRB |
| 728 | 9.13e-12 | 2.55e-12 | -0.755 | - | 53 | AFG2B_OH + NO = NO + #.2 xHO2 + #.12 xMECO3 + #.32 RO2C + #.04 RO2XC + #.13 xRCHO + #.2 xGLY + #.2 xBACL + #.04 zRCNO3 + #.31 yHPCRB + #.36 SumRO2 |
| F4HV | Phot Set= AFGS, qy= 2.20e-1 | G,62 | AFG2B + HV = #.86 OH + #.1 xOH + #.03 xHO2 + MEO2 + #.04 RO2C + #.08 xPACID + #.05 xHPCRB + #.03 CO + #.87 MALAH + #1.04 SumRO2 |
| F5OH | 7.20e-11 |  | G | AFG3 + OH = #.27 xHO2 + #.62 xMECO3 + #.88 RO2C + #.11 RO2XC + #.62 xRCHO + #.54 xMGLY + #.11 zRCNO3 + #.85 yHPCRB + #.99 SumRO2 |
| P2UI | 3.39e-4 |  | G | PAN2 = NO2 + R2CO3 + SumRCO3 |
| P2OH | 3.42e-12 |  | G | PAN2 + OH = #.05 NO3 + #.73 xNO3 + #1.15 xHO2 + #1.55 RO2C + #.07 RO2XC + #.17 xHCHO + #.66 xMECHO + #.07 xETCHO + #.15 xPAN2 + #.07 zPAN2 + #.5 CO + #.73 CO2 + #.05 ALK3 + #1.62 SumRO2 |
| P2HV | Phot Set= PPN-11 | G,71 | PAN2 + HV = NO2 + R2CO3 + SumRCO3 |
| P4UI | 3.39e-4 |  | G | APANS = NO2 + MACO3 + SumRCO3 |
| P4OH | 2.90e-11 |  | G | APANS + OH = #.74 NO3 + #.18 xNO3 + #.07 xHO2 + #.25 RO2C + #.01 RO2XC + #.07 xHCHO + #.18 xKET2 + #.19 OACID + #.07 xPAN2 + #.01 zPAN2 + #.18 CO2 + #.56 ALK4 + #.26 SumRO2 |
| P4O3 | 8.20e-18 |  | G | APANS + O3 = #.05 NO2 + #.19 OH + #.34 HO2 + #.38 HCHO2 + #.01 RCHO2 + #.1 HCHO + #.9 PAN2 + #.16 H2 + #.31 CO + #.21 CO2 |
| P4N3 | 1.60e-16 |  | G | APANS + NO3 = HO2 |
| P4HV | Phot Set= PPN-11 | G | APANS + HV = #.6 NO2 + #.4 NO3 + #.4 MEO2 + #.6 MACO3 + #.4 HCHO + #.4 CO + #.4 CO2 + #.4 SumRO2 + #.6 SumRCO3 |

Notes

[a]	Except as indicated, the rate constants are given by k(T) = A · (T/300)B · e-Ea/RT, where the units of k and A are cm3 molec-1 s-1, Ea are kcal mol-1, T is oK, and R=0.0019872 kcal mol-1 deg-1. The following special rate constant expressions are used:

Phot Set = name: The absorption cross sections and (if applicable) wavelength-dependent quantum yields for the photolysis reaction, where “name” indicates the photolysis set used. The absorption cross sections and (where applicable) quantum yields for each photolysis set are given in Table B-3 in the electronic supplement of this report. If a “qy=number” notation is given, the number given is the overall quantum yield, which is assumed to be wavelength independent.

Falloff: The rate constant as a function of temperature and pressure is calculated using k(T,M) = {k0(T)·[M]/[1 + k0(T)·[M]/kinf(T)]}· FZ, where Z = {1 + [log10{k0(T)·[M])/kinf(T)}/N]2 }-1, [M] is the total pressure in molecules cm-3, F and N are as indicated on the table, and the temperature dependences of k and kinf are as indicated on the table.

k = k0+k3M(1+k3M/k2): The rate constant as a function of temperature and pressure is calculated using k(T,M) = k0(T) + k3(T)·[M] ·(1 + k3(T)·[M]/k2(T)), where [M] is the total bath gas (air) concentration in molecules cm-3, and the temperature dependences for k0, k2 and k3 are as indicated on the table.

k = k1 + k2 [M]: The rate constant as a function of temperature and pressure is calculated using k(T,M) = k1(T) + k2(T)·[M], where [M] is the total bath gas (air) concentration in molecules cm-3, and the temperature dependences for k1, and k2 are as indicated on the table.

Same K as for (reaction): Uses the same rate constant as the reaction indicated.

[b]	Documentation notes are as follows:

G	The rate constant and product distribution derived using the MechGen mechanism generation system as documented by Carter (2023c). Overall reactions are derived using the lumping procedures described in the text. See Carter (2023c) for a discussion of how the rate constant parameters or photolysis rate constants are derived, and for documentation of the detailed mechanisms that were used to derive these lumped reactions.

1	Based on the NASA (2015) evaluation.

2	Based on the IUPAC (2019) evaluation.

3	IUPAC (2019) does not recommend incorporation of this reaction in models of the atmosphere but sets an upper limit of 1×10-22 cm3 molec-1 s-1 for the bimolecular process only. NASA (2011) gives an upper limit of 2.0×10–21 cm3 molec-1 s-1. It is recommended that this reaction not be included in gas-phase mechanisms, but that models include this as a heterogeneous process if appropriate.

4	Derived from the recommendations of the NASA (2015) evaluation for O2 and N2 and their mole fractions in air.

5	The temperature and pressure-dependence parameters were adjusted to fit the rate constants for the HNO3 forming reaction calculated using the temperature-dependent rate expression of NASA (2015) for the total HO2 + NO reaction and the temperature- and pressure-dependent expression for the ratio of the rate constant for the HNO3-forming reaction relative to the total rate constant as given by Butkovska et al (2007), which is recommended by IUPAC (2019). The data were fit for a standard atmosphere for 0 - 5 KM altitude, and atmospheres for 0 - 5 KM with the temperature increased or decreased by 10K.

6	Temperature-dependence parameters adjusted to fit the rate constant for a water concentration corresponding to 50% RH at 300K as a function of temperature at 1 atmosphere, using the parameters given by Stavrakou et al (2013). The reaction is assumed not to be pressure-dependent. This formula somewhat overpredicts the reaction at 100%RH, but probably not by more than the likely uncertainty.

7	The rate constants used for the reactions of peroxy radicals other than methyl peroxy with NO, HO2, and NO3 are the IUPAC (2019) recommendations for the corresponding reactions of ethyl peroxy.

8	The SumRO2 counter species is the sum of concentrations of all explicitly represented peroxy radical (RO2) species and of the operators RO2C and RO2XC that are used for peroxy radicals not represented explicitly. The products formed would depend on the peroxy radical that this peroxy radical is reacting with, but it is assumed that most have alpha hydrogens and can form disproportionation products. For the current mechanism and mechanism generation system, it is assumed that half react to form O2 + the corresponding alkoxy radicals and half disproportionate, with the two disproportionation reactions assumed to be equally probable if the peroxy radical has an alpha hydrogen. If the radical does not have an ( hydrogen, the H is assumed to be abstracted from the other radical. Note that the current peroxy lumping approach requires that the same rate constant be used for the reaction of a given peroxy radical with any other peroxy radical if the latter is represented by SumRO2. SumRO2 is shown as a product in its reactions with individual peroxy or acyl peroxy species since its loss by these reactions are represented separately by its reactions with SumRO2 or SumRCO3. See Carter (2023c) for a discussion of the derivation or rate constants and mechanisms used for peroxy radicals in MechGen, which are used for these reactions as well.

9	The rate constant used by model to estimate consumption rate for all peroxy radicals by reaction with HO2 is from the general estimate above for non-oxygenated peroxy radicals with 5 carbons (Carter, 2023c), which is the approximate average carbon number of the mixture of anthropogenic emissions used for developing the general mechanism.

10	The peroxy + peroxy rate constants are highly variable depending on the radical, but the peroxy lumping approach does not allow use of separate rate constants for each pair of rate constants. The rate constant used for estimating total rates of consumption of peroxy radicals by peroxy + perpoxy reactions are approximated by those appropriate for secondary peroxy + secondary peroxy reactions, based on averages of such rate constants tabulated by Carter (2023c).

11	The SumRCO3 counter species is the sum of concentrations of all lumped or explicitly represented acyl peroxy radical (RCO3) species that react with other peroxy radicals. Except when reacting with methyl peroxy radicals, the major reaction of these species with RO2 or other RCO3 radials is formation of the corresponding alkoxy radical, which rapidly decomposes to CO2 and the corresponding alkyl radical. SumRCO3 is shown as a product in its reactions with individual peroxy or acyl peroxy species since its loss by these reactions are represented separately by its reactions with SumRO2 or SumRCO3. See Carter (2023c) for a discussion of the derivation or rate constants and mechanisms used for acyl peroxy radicals in MechGen, which are used for these reactions as well.

12	The rate constant expression is based on the NASA (2015) recommendation for the high pressure limit for CH3CH2C(O)OO + NO2.

13	The rate constant based on the IUPAC (2019) recommendation for CH3CH2C(O)OO + NO.

14	The rate constant expression and product branching ratios used for all acyl peroxy + HO2 reactions is based on the IUPAC (2019) recommendation for acetyl peroxy + HO2.

15	The rate constant expression for all acyl peroxy + NO3 reactions is based on the IUPAC (2019) recommendation for acetyl peroxy + NO3.

16	The rate constant and product yields used are the IUPAC (2019) recommendation for ethyl peroxy + acetyl peroxy. No information could be found about reactions of other peroxy or acyl peroxy combinations.

17	The rate constant used is the IUPAC (2019) recommendation for self-reactions of CH3CH2C(O)OO radicals. Because of lack of information, this is assumed to apply to all acyl peroxy + acyl peroxy reactions except for acetyl peroxy.

18	The chemical operator RO2C is used to represent NO to NO2 conversions in reactions of peroxy radicals that are not represented explicitly. This is the approach used in SAPRC-07 and is based on the approximation that the products can be approximated by those that are formed when reactions with NO dominate. The rate constants used are the same as used for the corresponding reactions of SumRO2, which are based primarily on rate constants used for ethyl peroxy radicals.

19	The chemical operator RO2XC is used to represent NO consumption in the nitrate formation reactions of peroxy radicals that are not represented explicitly.  This is also part of the approach used in SAPRC-07.

20	The rate constant used for all methyl peroxy + other peroxy reactions is the average of IUPAC (2019) recommendations for methyl peroxy + methyl peroxy and methyl peroxy + ethyl peroxy rate reactions (3.5 and 2 x 10-13 cm3 molec-1 s-1, respectively). This may overpredict rates of these reactions for other radicals, though other primary + primary peroxy reactions have higher rate constants than this (IUPAC, 2019).

21	The rate constant and product yields used are the IUPAC (2019) recommendation for methyl peroxy + acetyl peroxy.

22	The rate constant used for all ethyl peroxy + other peroxy reactions is the IUPAC (2019) recommendation for the ethyl peroxy self-reaction. This is higher than its rate constant for reaction with methyl peroxy, but lower than other primary + primary peroxy reactions (IUPAC, 2019).

23	SumRO2 or SumRCO3 is added as a product to all reactions that form peroxy or acyl peroxy radicals that react with other peroxy radicals.

24	Rate constants expressions based on the data of Caralp et al (1999).

25	Rate constant from Lotz and Zellner (2000). The reaction with NO is ignored because nitrite formation expected to be rapidly reversed by photolysis.

26	Rate constant expression from Blitz et al (1999).

27	Rate constant from Platz et al (1998).

28	Assumed to have the same rate constant as used for ethyl peroxy + HO2.

29	Rate constant from Tao and Li (1999).

30	The NPRAD model species represents unknown naphthalene intermediates that react with NO2 forming nitrogen-containing products. In the absence of NO2 the reaction with HO2 is assumed to be the major fate, with the reaction with NO2 forming a compound represented by NPHE and the reaction with HO2 forming compounds represented by NAPPRD, the unspecified non-nitrogen-containing product of reactions of naphthalenes. The rate constants are unknown but are estimated to be similar to those for the reactions of acyl peroxy radicals.

31	This is added to avoid problems in the (generally unlikely) conditions where these radicals are formed when concentrations of both NO2 and HO2 are low. The rate constant used is is arbitrary and is such that this process becomes significant only if [NO2] < ~3 x 10-6 ppm and [HO2] < 1x10-5 ppm. The likely process is reaction with some VOC forming compounds similar to those formed when the radicals react with HO2.

32	The PNAMIN model species represents nitrogen-centered radicals that do not have alpha hydrogens and can only react with NO2 or other radicals. The reaction with NO2 is usually the major fate, since reaction with NO forms highly photoreactive nitrosoamines, which rapidly re-forms the radicals. In the absence of NO2 the reaction with HO2 is assumed to be the major fate, with the reaction with NO2 forming a nitramine and the reaction with HO2 forming an amine. The rate constants are unknown but are estimated to be similar to those for the reactions of acyl peroxy radicals.

33	Rate constant from Welz et al (2012).

34	This reaction is predicted to be the major fate of most types of Criegee intermediates under most atmospheric conditions, even if it has a rate constant lower than the upper limit of Welz et al (2012). The rate constant estimate used here is based on the estimate used by Sarwar et al (2013), which in turn is based on the rate constant ratio relative to reaction with SO2 given by Calvert et al (1978). This is highly uncertain, and varies with the intermediate.

35	Assumed to have the same rate constants as assigned for HCHO2. Note that these reactions are only applicable to stabilized biradicals that do not have rapid unimolecular reactions. Reactions of excited or reactive stabilized Criegee intermediates are handled by MechGen and are discussed by Carter (2023c).

36	Previous versions of SAPRC assumed that reaction with H2O, forming the acid, was the major fate of stabilized Criegee biradicals that did not have rapid unimolecular reactions, and represented their formation by the formation of the acid. These are now represented separately in order to account for effects of their reactions with SO2 and NO2 as well as H2O. The rate constants probably depend on the radical, but for now the same rate constants are used for all reactions. See Sarwar et al (2013) and Vereecken et al (2017) for a discussion of stabilized Criegee reactions and rate constants, and Carter (2023c) for a discussion of how MechGen treats unimolecular reactions of excited and stabilized Criegee intermediates.

37	Absorption cross-sections and quantum yields at 298K and 1 atmosphere are from the IUPAC (2019) recommendation. IUPAC gives recommendation for effect of temperature on the absorption cross-sections, but the effect is negligible (<1% change in action spectrum) for tropospheric modeling applications. The recommendation indicates no significant temperature or pressure effects on quantum yields for radical formation, but that the quantum yield for H2 + CO formation increases with decreasing pressure. The pressure effect is expected to increase the overall rate constant by about 15% at 15 KM, which is probably a small effect compared to the other uncertainties in modeling reaction rates at such altitudes.

38	Absorption cross sections recommended by Calvert et al (2011). Based on the discussion there, photolysis under atmospheric conditions forms primarily non-radical products, with benzene + CO formation being important at wavelengths that are too low to be important at ground-level conditions. However, using their recommended quantum yields for the higher wavelengths significantly overpredicts rates of consumption of benzaldehyde measured in chamber experiments, which were used as the basis for the photolysis rate used in previous version of this mechanism. Therefore, for this mechanism the overall quantum yield was derived to give the same atmospheric photolysis rate as used in SAPRC-07. The overall quantum yield derived (0.09) is higher than used in SAPRC-07 because the updated absorption cross sections give lower photolysis rates for the same quantum yields at higher wavelengths. Calvert et al (2011) gives no recommendation as to the major products formed at higher wavelengths, but indicates that they are "unidentified products leading to polymer". Currently they are represented as lost carbon, but it may be more appropriate to represent them using a non-volatile model species such as OTHN.

39	Rate constant expression from review of Calvert et al (2015).

40	Absorption cross sections, quantum yields, and reactions based on those used for PPN.

41	NPHE is used to represent various nitrogen-containing aromatic products formed primarily in the reactions of phenolic compounds or naphthalenes, and its mechanism is based that estimated for nitrophenols. The rate constant used is from SAPRC-07, and is in the range cited by Barnes (2006) for various nitrocresols. The reaction is assumed to occur via abstraction of H from OH, analogous to pathway in the phenol and cresol + OH reactions that occur with similar rates.

42	Rates of photolysis of nitrophenols forming HONO, relative to the photolysis rate of NO2, based on the data of Bejan et al (2006) for 2-nitrophenol and various methyl substituted 2-nitrophenols. The co-products are unknown, and are assumed to go mainly into the particle phase and its gas-phase reactivity is assumed not to be significant. Loss by other photolysis processes might be significant, but are ignored. Nitrophenols were found to have lifetimes relative to photolysis in the Euphore chamber of 1-2 hours (Barnes, private communication, 2007). A photolysis rate relative to NO2 of 0.015 corresponds approximately to this range. The products formed are unknown, but based on the data of Bejan et al (2006) it is apparent that NO2 formation is not important and that HONO formation represents only about 10% of this process. We assume that the co-product forming HONO has similar reactivity of phenol and that the product for the other routes can be represented by the NPHE model species, so this reaction has no effect on the model and is ignored.

43	The "NAPS" model species is used to represent all naphthalenes but its mechanism is based on that derived for naphthalene. The current mechanism generation system is not yet capable of predicting mechanisms for naphthalene, so the highly simplified and parameterized representation based on that used in SAPRC-07 is retained, with the product model species changed to be consistent with the model species used in this version of the mechanism, and the parameters adjusted to fit results of naphthalene - NOx chamber experiments. The rate constant used is that recommended by Calvert et al (2015) for naphthalene.

33	Rate constant from Welz et al (2012).

34	This reaction is predicted to be the major fate of most types of Criegee intermediates under most atmospheric conditions, even if it has a rate constant lower than the upper limit of Welz et al (2012). The rate constant estimate used here is based on the estimate used by Sarwar et al (2013), which in turn is based on the rate constant ratio relative to reaction with SO2 given by Calvert et al (1978). This is highly uncertain, and varies with the intermediate.

35	Assumed to have the same rate constants as assigned for HCHO2. Note that these reactions are only applicable to stabilized biradicals that do not have rapid unimolecular reactions. Reactions of excited or reactive stabilized Criegee intermediates are handled by MechGen and are discussed by Carter (2023c).

36	Previous versions of SAPRC assumed that reaction with H2O, forming the acid, was the major fate of stabilized Criegee biradicals that did not have rapid unimolecular reactions, and represented their formation by the formation of the acid. These are now represented separately in order to account for effects of their reactions with SO2 and NO2 as well as H2O. The rate constants probably depend on the radical, but for now the same rate constants are used for all reactions. See Sarwar et al (2013) and Vereecken et al (2017) for a discussion of stabilized Criegee reactions and rate constants, and Carter (2023c) for a discussion of how MechGen treats unimolecular reactions of excited and stabilized Criegee intermediates.

37	Absorption cross-sections and quantum yields at 298K and 1 atmosphere are from the IUPAC (2019) recommendation. IUPAC gives recommendation for effect of temperature on the absorption cross-sections, but the effect is negligible (<1% change in action spectrum) for tropospheric modeling applications. The recommendation indicates no significant temperature or pressure effects on quantum yields for radical formation, but that the quantum yield for H2 + CO formation increases with decreasing pressure. The pressure effect is expected to increase the overall rate constant by about 15% at 15 KM, which is probably a small effect compared to the other uncertainties in modeling reaction rates at such altitudes.

38	Absorption cross sections recommended by Calvert et al (2011). Based on the discussion there, photolysis under atmospheric conditions forms primarily non-radical products, with benzene + CO formation being important at wavelengths that are too low to be important at ground-level conditions. However, using their recommended quantum yields for the higher wavelengths significantly overpredicts rates of consumption of benzaldehyde measured in chamber experiments, which were used as the basis for the photolysis rate used in previous version of this mechanism. Therefore, for this mechanism the overall quantum yield was derived to give the same atmospheric photolysis rate as used in SAPRC-07. The overall quantum yield derived (0.09) is higher than used in SAPRC-07 because the updated absorption cross sections give lower photolysis rates for the same quantum yields at higher wavelengths. Calvert et al (2011) gives no recommendation as to the major products formed at higher wavelengths, but indicates that they are "unidentified products leading to polymer". Currently they are represented as lost carbon, but it may be more appropriate to represent them using a non-volatile model species such as OTHN.

39	Rate constant expression from review of Calvert et al (2015).

40	Absorption cross sections, quantum yields, and reactions based on those used for PPN.

41	NPHE is used to represent various nitrogen-containing aromatic products formed primarily in the reactions of phenolic compounds or naphthalenes, and its mechanism is based that estimated for nitrophenols. The rate constant used is from SAPRC-07, and is in the range cited by Barnes (2006) for various nitrocresols. The reaction is assumed to occur via abstraction of H from OH, analogous to pathway in the phenol and cresol + OH reactions that occur with similar rates.

42	Rates of photolysis of nitrophenols forming HONO, relative to the photolysis rate of NO2, based on the data of Bejan et al (2006) for 2-nitrophenol and various methyl substituted 2-nitrophenols. The co-products are unknown, and are assumed to go mainly into the particle phase and its gas-phase reactivity is assumed not to be significant. Loss by other photolysis processes might be significant, but are ignored. Nitrophenols were found to have lifetimes relative to photolysis in the Euphore chamber of 1-2 hours (Barnes, private communication, 2007). A photolysis rate relative to NO2 of 0.015 corresponds approximately to this range. The products formed are unknown, but based on the data of Bejan et al (2006) it is apparent that NO2 formation is not important and that HONO formation represents only about 10% of this process. We assume that the co-product forming HONO has similar reactivity of phenol and that the product for the other routes can be represented by the NPHE model species, so this reaction has no effect on the model and is ignored.

43	The "NAPS" model species is used to represent all naphthalenes but its mechanism is based on that derived for naphthalene. The current mechanism generation system is not yet capable of predicting mechanisms for naphthalene, so the highly simplified and parameterized representation based on that used in SAPRC-07 is retained, with the product model species changed to be consistent with the model species used in this version of the mechanism, and the parameters adjusted to fit results of naphthalene - NOx chamber experiments. The rate constant used is that recommended by Calvert et al (2015) for naphthalene.

44	The CATL3 model species is used to represent phenols with three or more -OH's. The mechanism is assigned based on CATL reactions but simplifed and assuming that all products are non-volatile. The rate constants are based on those estimated for 2,3,4-trihydroxy toluene, which is the highest yield product for reaction of OH with lumped CATL.

45	The NAPPRD model species is used to represent unspecified non-nitrogen-containing products of the reactions of OH with phenolic naphthalenes. A highly simplified mechanism is used, with the same rate constants as used in the simplified mechanism for NVPHE, used for unspecified products in the reactions of the phenols.

46	The model species "PHOT" is used to represent highly photoreactive model species such as nitrites, which are not important enough in emissions to be represented by separate model species, but is not well represented by other model species. A highly simplified mechanism is used for such compounds, using photolysis rates calculated for biacetyl. This model species should not be used for assessing impacts of specific compounds, only for representing compounds in as minor components in mixtures.

47	The main compound represented by IMINE is CH3CH=NH, which is assumed to rapidly hydrolyze to form acetaldehyde and ammonia. Therefore it is treated as in steady state and replaced by the formation of MECHO. The ammonia that is also formed is not represented because it is expected to be relatively unreactive and is not included in the gas-phase mechanism. The rate constant is arbitrarily set at 1 hour-1. The major gas-phase reaction would be expected to react with OH radicals, probably forming the same products with a similar lifetime.

48	Rate constants from the compilation of McGillen et al (2020, 2021).

49	The x(Spec) operators represent the formation of various products or radicals following the reactions of alkoxy radicals formed from the reactions of peroxy radicals (primarily the reaction with NO but to a lesser extent for reactions with NO3, SumRO2 or SumRCO3). They are represented as reacting with the same species and rate constants used for SumRO2, the model species representing the sum of all peroxy radicals. Alkoxy radicals and their subsequent products are assumed to be formed in 100% yields in reactions of these operators with NO, NO3, and RCO3, and in 50% yields in their reactions with RO2. Note that the reactions of peroxy radicals with NO forming nitrates are represented separately using the z(product) model species, and the formation of non-alkoxy products in their reactions HO2 and RO2 are are represented using the y(product) model species.

There are five reactions such as those shown for each of the 46 species that is assigned an x(Spec) operator, making a total of 230 such reactions (numbers 154-398). The 46 species of this type are as follows: OH, HO2, NO2, NO3, HCHO, GLY, HCOOH, MECHO, ETCHO, GLCHO, MEK, ACRO, ACET, MACR, MVK, BACL, MGLY, BUDAL, FURNS, BALD, BENX, RCHO, KET2, LVKS, OLEA1, OLEA2, OLEP, OACID, PACID, AMINS, R2NO3, RPNO3, RCNO3, RHNO3, RDNO3, RUOOH, HPCRB, AFG1, AFG2A, AFG2B, AFG3, PAN2, MEO2, ETO2, MECO3, R2CO3, MACO3, and TBUO.

50	The y(product) operator is used primarily to represent the formation of hydroperoxide species from the reactions of peroxy radicals with HO2. ). These are only used in the standard version of SAPRC-22. The also approximately represent the formation of disproportion products (with assumed 50% yields -- see Carter, 2023), with a single VOC model species chosen to represent the distribution of carbonyl and alcohol products predicted to be formed in these relatively minor reactions. The y(product) operators are represented as reacting with the same species and rate constants used for SumRO2, as with the other types of these operators.

There are five such reactions for each of the 5 species that are assigned y(Spec) operators, making a total of 25 such reactions (numbers 399-423). Spec-2 is the species representing those formed from disproportion reactions with other peroxy radicals. See the mechanism listing in the electronic supplement for the full list of these reactions. The 5 species of this type, and the Spec-2 species assigned to each are as follows (Spec, Spec-2): (ROOH, KET2), (RUOOH, OLEP), (RAOOH, OLEP), (HPCRB, KET2), and (RPNO3, R1NO3).

51	The z(Product) operator is used primarily to represent the formation of organic nitrates following the reactions of peroxy radicals with NO. These are only used in both the standard and in the full versions of SAPRC-22. The z(product) operators are represented as reacting with the same species and rate constants used for the other types of these operators. They also approximately represent the formation of products from reactions of alkoxy radicals that are formed in the reactions of peroxy radicals with NO3, RCO3, and (in half molar yields) with RO2. A single model species is chosen for each to represent these products of these relatively minor reactions.

There are five such reactions for each of the 9 organic nitrate model species that are assigned such operators, making a total of 45 such reactions (numbers 424-468). Spec-2 is the species representing those formed from reactions other than with NO or HO2. See the mechanism listing in the electronic supplement for the full list of these reactions. The 9 nitrate species assigned such operators, and the Spec-2 species assigned to each, are as follows (Spec, Spec-2): (RCNO3, KET2), (RHNO3, OTH3), (RANO3, RUOOH), (RPNO3, RUOOH), (RDNO3, R1NO3), (R1NO3, OTH3), (R2NO3, OLE1), (RNNO3, OTHN), and (PAN2, RCHO).

52	Rate constants used for the lumped higher acyl peroxy radicals are the IUPAC (2019) recommendation for the reaction of CH3CH2C(O)OO· with NO, for the high pressure limit for the reactions of acetyl peroxy radicals with NO2, and for reactions of acetyl peroxy radicals with NO3, HO2, ethyl peroxy, and acetyl peroxy radicals. Products formed are based on MechGen estimates and assignments for the reactions of CH3CH2CH2C(O)OO· or CH2=C(CH3)C(O)OO·. These in general are based on IUPAC (2019) recommendations.

53	The unimolecular rate constants for the unimolecular reactions of these operators, which are added to account for the dependences of product yields on absolute NO concentrations, were derived as discussed in Section 2.4.2. The rate constant for the reaction with NO is the same as used for other peroxy + NO reactions.2.4.2

54	Rate constant recommended by Calvert et al (2000).

55	Absorption cross sections recommended by IUPAC (2019). Unit quantum yields assumed.

56	Absorption cross sections and quantum yields based on IUPAC (2022) recommendations.

57	Absorption cross sections recommended by NASA (2015). Unit quantum yields assumed.

58	Absorption cross sections from IUPAC (2022). Unit quantum yields are assumed for HCO at wavelengths above ~285 nm, based on data of Chen and Zhu (2001) as discussed by IUPAC (2022).

59	Absorption cross-sections and quantum yields recommended by NASA (2015).

60	Alkyl ketone absorption cross-sections based on IUPAC (2019) recommendations for methyl ethyl ketone. Overall, wavelength-independent quantum yields adjusted to fit results of ketone - NOx chamber experiments, and tend to decrease with carbon number as follows: 0.175, 0.1, 0.1, 0.02 for 4 (MEK), 5, 6, and ³7 carbons, respectively. Overall quantum yield for KET2 based on distribution of C5+ ketones in the emissions mixture.

61	Absorption cross sections recommended by IUPAC (2019). The quantum yields were derived using the pressure and wavelength-dependent expression given by IUPAC (2019) for methyl vinyl ketone, with the total pressure adjusted so that the radical forming photolysis rates for the chamber experiments are the same as those that fit the chamber data.

62	The absorption cross sections used are based on those of trans-2-butene 1,4-dial and cis and trans 4-oxo-2-pentenal as reported by Calvert et al (2002). Cross sections used for lumped species based on a previous estimate of the distribution of these products from aromatics, giving 31.6% butenedial and 68.4% 4-oxo-2-pentenal. These have not been updated based on updated estimates of aromatic reactions, but are reasonably representative. The overall absorption cross sections for the photolysis of BUDAL, AFG1, AFG2A, and AFG2B were re-adjusted to minimize biases in predictions of NO oxidation and O3 formation rates in the aromatic - NOx experiments.

63	The rates of photolyses of these lumped model species are assumed to be the same as those for the simplest compound represented by the model species, as follows: Propionaldehyde for lumped higher aldehydes with no adjacent double bond (RCHO and OLEA2); methacrolein for lumped a-unsaturated aldehydes (OLEA1); methyl vinyl ketone for lumped a-unsaturated ketones (LVKS); isopropyl nitrate for lumped organic nitrates without carbonyl or hydroperoxy groups (R1NO3, R2NO3, RHNO3); methyl hydroperoxide for lumped hydroperoxides without carbonyl groups (ROOH, RAOOH, RUOOH)

64	Absorption cross sections of peroxyaetic acid given by Orlando and Tyndall (2003) used for lumped peroxy acids.

65	Absorption cross sections and quantum yields for lumped a-keto aldehydes are based on those recommended by IUPAC (2019) for methyl glyoxal. Quantum yield calculated from the expression given for 425 torr N2. This "pressure" adjustment was made so the calculated photlysis rates, relative to NO2, are consistent with the data of Plum et al (1983) and Klotz et al (2000).

66	Absorption cross sections and quantum yields for lumped a-keto ketones are based on those recommended by IUPAC (2019) for biacetyl. Quantum yield calculated from the expression given by IUPAC (2019) for the pressure and wavelength-dependence quantum yields for methyl glyoxal, but with the effective pressure adjusted so the photolysis rate, relative to that for NO2, under ambient conditions is consistent with  the data of Plum et al (1983) and Klotz et al (2000).

67	Absorption cross sections for carbonyl nitrates from Barnes et al (1993), with primary and secondary nitrates weighed equally. Assume unit quantum yields based on discussions in Barnes et al (1993).

68	Compounds with both hydroperoxide and nitrate substituents are assumed to photolyze with the same rate constant assigned for lumped hydroperoxides, based on methyl hydroperoxide, because photolyses of hydroperoxides are faster than those of organic nitrates under atmospheric conditions.

69	Absorption cross sections for lumped dinitrates based on averages of absorption cross sections for 1,2-propandiol dinitrate,1,2-butandiol dinitrate, 2,3-butandiol dinitrate, 3,4-dinitrooxy-l-butene, and 1,4-dinitrooxy-2-butene from Barnes et al (1993). Quantum yields based on discussions in Barnes et al (1993).

70	Unsaturated hydroperoxy aldehydes are assumed to have absorption cross sections similar to unsaturated carbonyls, and the absorption cross sections used are averages of the IUPAC (2019)-recommended values for methacrolein and methyl vinyl ketone. Reaction is assumed to be breaking the weakest bond (the O-O bond in hydroperoxy groups) with unit quantum yield.

71	Absorption cross section and quantum yields based on NASA (2011) recommendations for PPN (for PAN2) and PAN (for APANS).

# Footnotes

The intermediates in the queue are reacted according to the following priority: (1) most carbons; (2) most hydrogens; (3) highest estimated yield (see used to judge if reactions are non-negligible – see following paragraph); and (4) first formed. This is to minimize cases where reactions that form an intermediate are processed after the reactions of the intermediate, which can result in incorrect yield estimates.

This requirement can be satisfied for mechanisms generated for SAPRC-22 as long as phenoxy radicals are represented by lumped species (so their interconversions involving phenoxy + O3 and phenyl peroxy + NO to not have to be generated), reversible radical addition to bonds followed by decomposition are represented by a single net addition process, and formation of reactive peroxynitrates are either ignored or their reactions are generated separately. It is also necessary to ignore the fast H-shift "scrambling" reactions that interconvert isomers of hydroperoxy-substituted peroxy radicals (Carter, 2023c).

This would also include alkoxy radicals that only have bimolecular reactions, such as phenoxy radicals, which are lumped in SAPRC mechanisms, or CF3O·, which is currently not handled by MechGen.

MechGen represents molecules as sets of "groups" that consist of one major atom (such as carbon and nitrogen) and variable numbers of hydrogen or oxygens bonded to them (Carter, 2023b). Examples include -CH3, =CH-, -C(O)-, -OH, -O-, -ONO2, etc.

# Comments

Starting point: Second draft submitted to the CARB on March 9, 2023. Reflects updates to the mechanism generation process and methods used to evaluate peroxy representations. Has more discussion of base mechanism as requested by CARB staff. Listings for full versions removed because the standard version is recommended.

7/12/23: Added CATL3 to mechanism listings and corrected nC and Mwt for CATL. No other changes (adding CATL3 to mechgen lumping caused only affected CATL products and had only a very small effect on calculated results except for NVOL).

7/1/23: Corrected mechanism after MG found not to process fast UNI RCO3's correctly.

4/3/23. Minor changes to Table 2 as a result of comments by Bill Hutzell. Mechanisms regenerated to correct error found by Hutzell and listings of generated portion of mechanism in supplements updated. This did not affect the listings in the Appendix and the changes in the model predictions were too small to necessitate updating the figures.

5/13/23 Corrected mechanism listing table to improve documentation and use no correction for acetone photolysis.

9/6/23	Revised for version K -- after updating peroxy RO2 isom

Updated 7/12/23. Corrected sizes for SAPRC22H

Based on F:\Work\SAPRC18\S18doc.xls, same as  what was in F:\Work\SAPRC15\Doc\S16doc.xls. Updated to reflect change in glyoxal photolysis but no other changes made for S16D.

SAPRC22 OK. F:\Work\SAPRC22\CompMDD-1.xls. (48%) revised 5/15/23; 7/1/23, 7/7/23, 9/7/23

SAPRC22 OK. F:\Work\SAPRC22\CompMDD-2.xls. Revised 9/7/23. Note had to do a screenshot for plots to be imported..

SAPRC22 OK. F:\Work\SAPRC22\CompMDD-0.xls 9/7/23

From F:\Work\SAPRC22\S22doc.xls "Std Conds" Sheet, col A. 3/8/23

Original version from F:\Work\SAPRC22\S22doc.xls "Std Conds" Sheet. 12/29/22. Revised version from F:\work\EnvCond\StdConds.xls "S22 report" Sheet at A32. 4/6/23. Not changed 7/23 because mechanism correction should not affect appearance results that are shown.

Based on calculations prior to correction of 6-7/23. Not expected to be much different after corrections.

From F:\Work\SAPRC22\S22doc.xls "Terpene Runs" Sheet. 12/29/22 x 85%. Updated 4/6/23. No difference when updated S22.3 to S22.4 5/15/23. Revised 7/1/23

From F:\Work\SAPRC22\S22doc.xls "Imp. test plot" Sheet. Data copied from Table A11 in F:\work\SAPRC22\SAPRC22.XLS. Updated 4/6/23; 7/1/23, 7/7/23, 9/9/23

Copied from F:\work\saprc22\SAPRC22.xls "A-1" Sheet 12/13/22. Corr 12/16. Corrected 3/23 to reflect changes in lumping approach, and to remove "XC" and "XN". CATL3 added and nC and Mwt for CATL corrected 7/12/23. Updated in this document but not SAPRC22.xls on 9/8/23

From F:\work\saprc22\S22doc.xls "Rxn Table and Rxn Notes" sheets. Corrected 3/4/23 to reflect changes in lumping and lumped mechanisms. Corrected 5/13/23 to improve documentation and include full reactions. Documentation consistent with no adjustment for acetone photolysis. Corrected 7/1/23, 7/7/23. CATL3 added 7/12/23. Rxno's corrected 7/13. Updated in F:\work\saprc22\S22doc.xls and comments renumbered and changed reactions and comments copied 9/8/23.