Lab2 Current mirror

Object: The current source is a basic building block in CMOS IC design and is used extensively in analog integrated circuit design. PSIPCE and BSIM3 model is introduced in this lab to simulate a current mirror.

Introduction: We are going to using BSIM3 model for N,P MOSFET in PSPICE circuit simulation.

This is a circuit of current sink.

Before simulation,calculate:

If you want to get Id(M4)=10uA,Id(M5)=20uA,  R0=?  M4  W/L= ?/2um M/L=?/2um

Project:

Using Pspice to simulation the current mirror with Id=20uA.

Steps:

A. Edit a netlist file for the circuit.

Use text edit tools such as WORDPAD, edit a netlist file.Example

R0 100 101 100E3

V4 102 0 2.5

V0 100 102 2.5

M5 101 101 0 0 AMI06N  L=4.95E-6 W=15E-6 AD=22.5E-12 AS=22.5E-12 PD=33E-6

+PS=33E-6 M=1

M4 102 101 0 0 AMI06N  L=4.95E-6 W=30E-6 AD=45E-12 AS=45E-12 PD=63E-6 PS=63E-6

+M=1

* level 11 for Cadence Spectre

* DATE: Jan 25/99

* LOT: n8bn                  WAF: 03

* Temperature_parameters=Default

* Include files

* End of Netlist

* Model File

.MODEL AMI06N NMOS (Level=       7

+Tnom=27.0

+Nch= 2.498E+17  Tox=9E-09 Xj=1.00000E-07

+Lint=9.36e-8 Wint=1.47e-7

+Vth0= .6322    K1= .756  K2= -3.83e-2  K3= -2.612

+Dvt0= 2.812  Dvt1= 0.462  Dvt2=-9.17e-2

+Nlx= 3.52291E-08  W0= 1.163e-6

+K3b= 2.233

+Vsat= 86301.58  Ua= 6.47e-9  Ub= 4.23e-18  Uc=-4.706281E-11

+Rdsw= 650  U0= 388.3203 wr=1

+A0= .3496967 Ags=.1    B0=0.546    B1= 1

+ Dwg = -6.0E-09 Dwb = -3.56E-09 Prwb = -.213

+Keta=-3.605872E-02  A1= 2.778747E-02  A2= .9

+Voff=-6.735529E-02  NFactor= 1.139926  Cit= 1.622527E-04

+Cdsc=-2.147181E-05

+Cdscb= 0  Dvt0w =  0 Dvt1w =  0 Dvt2w =  0

+ Cdscd =  0 Prwg =  0

+Eta0= 1.0281729E-02  Etab=-5.042203E-03

+Dsub= .31871233

+Pclm= 1.114846  Pdiblc1= 2.45357E-03  Pdiblc2= 6.406289E-03

+Drout= .31871233  Pscbe1= 5000000  Pscbe2= 5E-09 Pdiblcb = -.234

+Pvag= 0 delta=0.01

+ Wl =  0 Ww = -1.420242E-09 Wwl =  0

+ Wln =  0 Wwn =  .2613948 Ll =  1.300902E-10

+ Lw =  0 Lwl =  0 Lln =  .316394

+ Lwn =  0

+kt1=-.3  kt2=-.051

+At= 22400

+Ute=-1.48

+Ua1= 3.31E-10  Ub1= 2.61E-19 Uc1= -3.42e-10

+Kt1l=0 Prt=764.3

+L=1.05e-6 W=10.9e-6      )

*end of model file

.probe

.DC V4

+  2.500000E+00  2.510000E+00  1.000000E-02

.TEMP 0.2500E+02

.OP

.END

Save the file as Lab2test.cir

B. Open Pspice AD

C. Load file lab2test.cir

D. Simulation>Run

E. Trace>Add trace     select the Id

You get

Now you are ready to edit your file. You need change the R ,L and W of  transistors so as to make Id(M4)=10uA,Id(M5)=20uA

Also you need replace the Model file of NMOS with the BSIM3 model.

.model N1 NMOS

+Level=        7

+Tnom=27.0

+Nch= 2.498E+17  Tox=9E-09 Xj=1.00000E-07

+Lint=9.36e-8 Wint=1.47e-7

+Vth0= .6322    K1= .756  K2= -3.83e-2  K3= -2.612

+Dvt0= 2.812  Dvt1= 0.462  Dvt2=-9.17e-2

+Nlx= 3.52291E-08  W0= 1.163e-6

+K3b= 2.233

+Vsat= 86301.58  Ua= 6.47e-9  Ub= 4.23e-18  Uc=-4.706281E-11

+Rdsw= 650  U0= 388.3203 wr=1

+A0= .3496967 Ags=.1    B0=0.546    B1= 1

+ Dwg = -6.0E-09 Dwb = -3.56E-09 Prwb = -.213

+Keta=-3.605872E-02  A1= 2.778747E-02  A2= .9

+Voff=-6.735529E-02  NFactor= 1.139926  Cit= 1.622527E-04

+Cdsc=-2.147181E-05

+Cdscb= 0  Dvt0w =  0 Dvt1w =  0 Dvt2w =  0

+ Cdscd =  0 Prwg =  0

+Eta0= 1.0281729E-02  Etab=-5.042203E-03

+Dsub= .31871233

+Pclm= 1.114846  Pdiblc1= 2.45357E-03  Pdiblc2= 6.406289E-03

+Drout= .31871233  Pscbe1= 5000000  Pscbe2= 5E-09 Pdiblcb = -.234

+Pvag= 0 delta=0.01

+ Wl =  0 Ww = -1.420242E-09 Wwl =  0

+ Wln =  0 Wwn =  .2613948 Ll =  1.300902E-10

+ Lw =  0 Lwl =  0 Lln =  .316394

+ Lwn =  0

+kt1=-.3  kt2=-.051

+At= 22400

+Ute=-1.48

+Ua1= 3.31E-10  Ub1= 2.61E-19 Uc1= -3.42e-10

+Kt1l=0 Prt=764.3